## Slide 1: Efficient Device and Service Discovery for Peer-to-Peer (P2P) scenarios
Authors:
10-25-2011

## Slide 2: Abstract
We investigate a number of problems that need to be addressed to enable efficient pre-association discovery between 802.11 STAs for station to station i.e., peer to peer (P2P) communication. We also highlight some techniques to address these problems, most of which would impact the 802.11 MAC / PHY industry standard

## Slide 3: Introduction
Increased industry interest in direct discovery between devices to provide proximity-based services such as peer to peer (P2P) communication between devices
  3GPP is evaluating standards development in this direction
  WFA is evaluating enhancements needed to enable proximity based services and service discovery
Typical connection cycle for P2P communication:
  Device and Service Discovery of proximal devices
    Scan for device and service advertising messages from proximal devices
  Authentication
  Association and application level session setup.
In this presentation, we focus on pre-association P2P steps (1,2 above)

## Slide 4: High Level Requirements for Efficient P2P Communication
Low Power Consumption
  P2P communication targeted at mobile handsets with stringent power requirements .
Coexistence with legacy traffic
  Ensure that discovery messages do not significantly affect legacy device behavior.
Scalable Device and Service Discovery
  Operate with low overhead yet preserve reasonable discovery time in scenarios with large number of devices
Security/Privacy
  Secure communication must be established without an infrastructure in place

## Slide 5: Power Consumption Issues for P2P Discovery
P2P communications are likely to target mobile devices that have stringent power drain requirements
Contributing factors to increased power drain:
  Un-coordinated transmission of discovery messages requires all P2P devices to remain in receive state for extended periods
  Contention, and collisions between discovery/paging packets and other data packets especially as number of users increase.

## Slide 6: Co-Existence and Security Requirements
Co-Existence Issues
  Need to ensure that legacy data traffic is not significantly hindered by discovery packet transmissions.
    Reduce likelihood of collision between discovery messages and data traffic by P2P devices
Security Issues
  Validate advertisements from other P2P devices
  Mechanisms for set up and tear down of secure P2P data sessions
    Security methods requiring infrastructure (e.g. Authentication Servers) may not be suitable for setup and tear down of P2P sessions

## Slide 7: Scalability of Device Discovery
Places of congregation like malls, downtown, amusement parks, stations, stadiums can have large number of devices within WLAN range.
  Typical range values are
    2.4GHz Band: ~70-140m*
    900MHz Band: ~200-400m* (1MHz channel)
  Such ranges can accommodate several 1000s of devices
    E.g. Assuming 9m2 (~3m X 3m square) per person, a
      70m range accommodates ~1700 people
      200m range accommodates ~14000 people
    E.g. Assuming 3m2 (~1.7m X 1.7m square) per person, a
      70m range accommodates ~5000 people
      200m range accommodates ~40,000 people
Messaging with Query/Response based protocols lead to extremely large message load that scales as O(N2) (see next slide)
Multicast protocols may alleviate messaging burden, however mechanisms for co-ordination of transmissions between devices need to be in place to realize efficiency gains
*Based on 802.11 Channel Model D and 0 -10dB shadowing/wall-penetration losses, 18dBm Tx power, single antenna devices

## Slide 8: Sample Calculation for Unicast Discovery
Chart: Minimum Device on time to Receive Discovery Messages from all P2P devices in Range for a 1 Minute Discovery Interval
| 1 | 10 | 20 | 30 | 35 | 40 | 50 | 100 | 200 | 500
WiFi Direct (900MHz) | 0 | 2.0196 | 8.5272 | 19.5228 | 26.7036 | 35.0064 | 54.978 | 222.156 | 893.112 | 5598.78
WiFi Direct (2.4GHz) | 0.10746 | 0.45372 | 1.0388 | 1.4209 | 1.8626 | 2.9253 | 11.8206 | 47.5212 | 297.903
WiFi Direct operation is based on query request/response type messaging that leads to O(N2) messaging
Observations: For a Discovery Interval of 1 minutes*
  With 2.4GHz (20MHz channel): beyond 100 devices, discovery on time overhead exceeds 20%
  With a 1MHz channel e.g. in 900MHz Band :device on time overhead exceeds 100% minute beyond 50 devices
*See Appendix for details on message sizes and other assumptions
200

## Slide 9: Potential Concepts to Address Requirements - I
Features to allow for Low Power Consumption
  Enable P2P devices to be awake for short time for receiving discovery messages and be in sleep state other wise
  Enable efficient paging of discovered devices
    P2P devices should not be required to remain indefinitely on to receive requests to connect
  Shorter discovery messages would also result in lower power consumption
Enable scalable device discovery
  Use broadcast of discovery messages
    Avoid query response model due to O(N2) scaling
    Enhance CSMA to reduce collisions between discovery messages from P2P devices during discovery message transmission intervals
    Design shorter messages for discovery. E.g. techniques include
      Reduce MAC header fields
      Avoid IP/UDP and potentially other application-layer overheads for discovery messages

## Slide 10: Potential Concepts to Address Requirements - II
Solve co-existence issues
  Reduce collisions between discovery messages and data traffic by partitioning time between discovery message transmission and data transmission
    Develop techniques to allow P2P devices to achieve this time partitioning in a distributed manner
Investigate security requirements for P2P
  Methods to authenticate P2P discovery messages
    Where authentication is required for Use Case
  Methods to setup secure P2P data connections without infrastructure support

## Slide 11: Conclusion
Enabling efficient pre-association discovery for P2P scenarios may enable valuable new usages for 802.11 technology
A number of problems as well as techniques have been highlighted, most of which would impact the 802.11 MAC / PHY industry standard

## Slide 12: Straw Poll
Are you interested in continued discussion in WNG on the topic of ‘Pre-association Peer to Peer Device Discovery’ to explore the potential of creating an 802.11 Study Group?
  Y:
  N:
  A:

## Slide 13: Appendix

## Slide 14: Potential to leverage existing 802.11 Concepts
Several existing .11 mechanisms can be leveraged for P2P communication
Examples:
  802.11u:
    Use GAS (Generic Advertisement Services) frames for discovery and paging messages. GAS messages can be exchanged without association
  802.11p:
    Use “Time Advertisement” frames for synchronization of P2P devices
      Would provide lower overhead than using beacon frames
  802.11ad: PCP (PBSS Control Point) concept can be leveraged for P2P device coordination
    E.g., PCP like device to provide synchronization, transmit medium reservation messages etc.

## Slide 15: Assumptions for Unicast Discovery Computation
Message Sizes for WiFi Direct
  ~ 200 bytes (probe request/response)
PHY
  2.4GHZ band: 20MHz Channel
  900MHz band : 1 MHz Channel (11ah 900MHz band)
PHY Rates: MCS0 rate
  6Mbps for 2.4GHz channel
  ~ 300Kbps for 900MHz
Other Salient assumptions:
  20% collisions for discovery packets
  50% medium time loaded by other traffic
    Approximately doubles the total time taken for all nodes to complete transmitting their discovery messages