## Slide 1: Access Point Power Saving
Date: 2012-01-05
Authors:

## Slide 2: Abstract
802.11 has added numerous features over the years to enable associated stations to save power by allowing them to power-off their radios for some of the time
However, there is very little support for allowing an Access Point to power-off its radio
This presentation describes some reasons why an AP should be able to power-off for periods of time, while still providing service to associated stations

## Slide 3: The Numbers
Power consumption of an AP ≈ 2W .. 14W
If left on 24/7
  5.2W1 = 0.12 KWh/day = 46 KWh/year
  UK cost 2 ≈ £6.13/year, CA cost 3 ≈ $6.97/year
Providing power for 46m APs1 = 240MW
  About ½ a natural gas (CCGT) power station
Turning AP off from 11pm to 6am
  17 hours/day = 32KWh/year = $4.94/year
  Over 46m APs, saves 614GWh/year
  614GWh/year ≈ $93M/year
  614GWh/year ≈ 626597 tonnes CO2 6 ≈ 227853 people on transatlantic flights 7 ≈ 49 years of 802.11 meetings
Notes: CCGT = combined cycle gas turbine 46million = CEA estimate of number of APs in the US
Meeting estimate assumes average 390 attendees, 6 meetings a year, 11 hours per flight

## Slide 4: Set top boxes
Many set top boxes are nocturnal
  Downloading updates, “pushed” content, series links, etc.
  Done over night because STB is normally idle at this time and there is spare broadcast capacity
Hybrid boxes are increasingly popular
  E.g. Satellite + IP
Downloading from the satellite over night is a solved problem, but what if the STB needs to use the IP network?
  A problem if the WiFi is turned off!

## Slide 5: Other devices
Cell phones
  Downloading updates or sync with the cloud while charging
  Could always use cellular network
Laptops, Tablets, etc
  Updates (OS, virus scanner, etc) outside of office hours
Surveillance cameras
  WiFi IP cameras
Enterprise
  Offices, shops, factories, etc. that don’t operate 24/7 but need to provide ad hoc out of hours WiFi access

## Slide 6: External Factors
Companies / households wanting to be more environmentally responsible
  Improvements in power consumption in other CE devices makes the AP an increasing target for criticism
Legislation currently focussing on standby power consumption
  If an AP with no associated clients is considered “in standby” it would be obliged to meet the 1W rules (0.5W from 2013)

## Slide 7: Why not use the IP link during the day?
Peak on-demand usage of TV catch-up services tends to be a few hours after first broadcast4
Common method of billing for network usage is based upon 95th percentile of peak load5
An operator really wants to avoid scheduling downloads during a peak and really wants to schedule outside of the peak
  Increased consumption at peak = increased cost
  Increase consumption outside of peak ≈ no extra cost

## Slide 8: Why not use the IP link during the day?
Chart: 
| 0.25 | 0.33333333333333331 | 0.41666666666666669 | 0.5 | 0.58333333333333337 | 0.66666666666666663 | 0.75 | 0.83333333333333337 | 0.91666666666666663 | 0 | 8.3333333333333329E-2 | 0.16666666666666666
TV | 3 | 4.5 | 5 | 6 | 7 | 10 | 18 | 26 | 18 | 5 | 1.5 | 1
Internet | 7 | 19 | 22 | 25 | 26 | 27 | 26 | 24 | 18 | 13 | 7 | 3
OTT | 40 | 80 | 120 | 120 | 140 | 160 | 180 | 245 | 316 | 180 | 80 | 30
Much better time to schedule downloads
95th percentile
Don’t want to start downloading here, because will increase peak usage.

## Slide 9: 802.11 Power Saving
Almost every amendment seems to add new client power saving options to the 802.11 standard
  U-APSD, S-APSD, DTIM, PSMP, FMS, DMS, WNM Sleep, Proxy ARP, TIM Broadcast, TDLS PSM, TDLS U-APSD, GCR-SP, etc.
11v was the first to mention an AP powering down
  Neighbor Report - BSS Termination Duration
  Provides start time (TSF) and duration (minutes) of power down
  Only allows reporting of a neighbour powering down, not own AP
  Client can’t request AP to be awake at a certain time

## Slide 10: What’s needed?
A way for an associated STA to request an AP to be awake at a certain time of day
and/or
A way for an AP to announce regular periods of time when it will wake up
and/or
A way for an AP to use less power but still support associations
and/or
…

## Slide 11: Conclusion
Significant quantities of power, money and CO2 could be saved with modest reductions in AP power consumption

## Slide 12: Questions
What can be done with the existing spec?
Is it already possible to build a useful AP that uses less than 0.5W?
Should 802.11 work in this area, or is it a topic for other organizations?

## Slide 13: Straw Poll
Would you be interested in working on the topic of “Access Point Power Saving”?
Yes
No
Maybe

## Slide 14: References
http://www.ce.org/PDF/Energy-Consumption-of-CE-inUSHomes-2010.pdf
£0.1346/KWh (tier1 @ £0.25/KWh + tier2 @ £0.12162/KWh)
  http://www.britishgas.co.uk/products-and-services/energy/our-tariffs/standard.html
$0.153/KWh
  http://www.electricchoice.com/electricity-prices-by-state.php
http://www.bbc.co.uk/blogs/bbcinternet/2011/08/18/BBC_iPlayer_performance_monthly_1107_FINAL.pdf
http://en.wikipedia.org/wiki/Burstable_billing
http://www.epa.gov/cleanrgy/energy-and-you/affect/coal.html
http://www.carbonindependent.org/sources_aviation.htm