## Slide 1: Discussions on the better resource utilization for the next generation WLANs
Date: January 17th, 2012
Authors:
Name | Affiliations | Address | Phone | email
Yasuhiko Inoue | NTT Corporation | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | ++81-46-859-5097 | inoue.yasuhiko@lab.ntt.co.jp
Yusuke Asai |  |  | ++81-46-859-3494 | asai.yusuke@lab.ntt.co.jp
Tomoki Murakami |  |  | ++81-46-859-2057 | murakami.tomoki@lab.ntt.co.jp
Masato Mizoguchi |  |  | ++81-46-859-3758 | Mizoguchi.masato@lab.ntt.co.jp
Laurent Cariou | Orange | 4 rue du Clos Courtel 35512 Cesson Sevigne France | ++33-299124350 | Laurent.cariou@orange.com

## Slide 2: Abstract
We have proposed to exploit the frequency and spatial resources for the next generation WLAN standard (11/1464r2)
For the better resource utilization, there are some technologies that had been discussed. We have conducted some basic researches on those technologies.
We have estimated the capacity gain by adding the DL-OFDMA capability. Roughly speaking, the capacity will be doubled with the DL-OFDMA technology.

## Slide 3: Previous Works
There have been many proposals to make more efficient use of frequency and spatial resources. E.g.,
  Multi-channel/OFDMA
    Frequency domain multiplexing for MU transmissions
    Non-contiguous use of two 40MHz channels to make 80MHz transmissions
    Use of multiple 20MHz channels
  MU-MIMO
    Protection mechanisms
    Use case for uplink MU-MIMO
    Feasibility studies on PHY technique for uplink MU-MIMO
  Other topics
    Synchronization
List of the previous works are presented in the last two slides.

## Slide 4: Recap of the discussion in Nov. 2011
For the high speed WLANs beyond 802.11ac, we need to utilize frequency and spatial resources.
Technologies for the better resource utilization include, but not limited to:
  For the better use of spatial resources: Uplink MU-MIMO
  For the better use of frequency resources: OFDMA/Multi-channel
AP collaboration may also be considered to achieve higher resource utilization and coordination
One of the next interest may be the benefit of having the above features.
As a first step, we have conducted rough estimation of capacity gain with DL-OFDMA technique.

## Slide 5: Benefit of resource utilization
Ch #
time
…
48
44
40
36
.11a
.11ac
.11n
Space
.11ac
.11n
.11ac
.11*
.11*
.11ac
.11n
.11n
.11*
.11*
.11*
.11*
.11*
.11*
.11*
.11ac
.11n
.11*
.11n
.11ac
.11a
Ch #
time
…
48
44
40
36
.11a
.11ac
.11n
.11*
.11*
AP collaboration
Frequency domain extension
Frequency + Spatial domain extension
As a first step, the effect of DL-OFDMA is evaluated.

## Slide 6: Conditions
PHY types and operating channel bandwidth
  The 802.11a STA uses the primary channel only, i.e. 20MHz
  The 802.11n STA uses the primary and secondary 20MHz channels, i.e. 40MHz
  The 802.11ac STA uses the primary, secondary 20MHz, and the secondary 40MHz channels, i.e. 80MHz
  The DL-OFDMA capable STA, denoted 802.11ax, also uses 80MHz channel as 802.11ac STA
802.11a STA (20MHz)
802.11ac STA (80 MHz)
CH 36
CH 40
CH 44
CH 48
802.11n STA (40 MHz)
Primary
channel
Secondary 20MHz channel
Secondary 40MHz channel
802.11axSTA (80 MHz)

## Slide 7: Channel Usage (Isolated BSS)
An 802.11ac BSS with legacy (802.11a and 802.11n) STAs
An 802.11ax BSS with legacy (802.11a, 802.11n and 802.11ac) STAs
11a
11ac
11n
.11ac AP
.11a
STA
.11ac
STA
.11n
STA
11a
11ac
11n
11a
CH 36
(primary)
CH 40
CH 44
CH 48
11a
11ac
11n
.11ax AP
.11a
STA
.11ac
STA
.11n
STA
11a
11ac
11n
CH 36
(primary)
CH 40
CH 44
CH 48
Unused (wasted) frequency resources
.11ax
STA
11ax
11ax
11ax
11ax
11ax
11ax

## Slide 8: Improvements in throughput by introducing the DL-OFDMA
For simplicity, some more conditions are assumed.
  Data rate for 802.11a, 802.11n and 802.11ac STAs are 54 Mbit/s, 600 Mbit/s and 2.6 Gbit/s (Nss=8, MCS=7), respectively.
  Data rate for DL-OFDMA capable STA is scaled from 802.11ac STA according to the channel bandwidth
  All STAs are fully loaded
  Each STA has the same probability of gaining an access to the channel
  TXOP is common for all PHYs
Throughput calculation
  When 802.11a, 802.11n and 802.11ac STAs coexist: 1084.7 Mbit/s
  The above with DL-OFDMA capable STA: 2276 Mbit/s

## Slide 9: Channel Usage (OBSS)
.11ax AP
.11ax AP
.11n
STA
.11ax
STA
.11ax
STA
11n
CH 36
(primary)
CH 40
CH 44
CH 48
11ax
(BSS1)
11ax
(BSS2)
11ax
(BSS2)
11n
CH 36
(primary)
CH 40
CH 44
CH 48
11ax
(BSS1)
11ax
(BSS2)
.11ax AP
.11ax AP
.11n
STA
.11ax
STA
.11ax
STA
Information exchange and resource coordination
.11a
STA
.11a
STA
11a
BSS1
BSS2
BSS1
BSS2
11a
Even when a BSS is not fully loaded, high frequency utilization may be achieved by collaborating with neighboring APs in the OBSS environment.

## Slide 10: Conclusions
There are many works for better use of frequency and spatial resources that have been discussed in the previous standardization activities.
We need to reconsider those techniques for the next generation WLAN standardization.
As a first step, we have conducted rough estimation of capacity gain of having DL-OFDM feature assuming a scenario coexisting with legacy (802.11a, 802.11n and 802.11ac) STAs.
  The system capacity will be doubled by having the DL-OFDMA feature
For the better resource utilization, AP collaboration should be considered for OBSS environment.
  For such collaboration, the opportunity of using 802.11ah as a signaling band should be investigated.

## Slide 11: Next Step
We would like to continue discussions on the better resource utilization in a new 802.11 Study Group.
We would like to have two straw polls

## Slide 12: Straw Poll #1
Would you support formation of a new study group to develop PAR and 5 Criteria with the intention of creating a new task group?

## Slide 13: Straw Poll #2
When do you think is appropriate to start the new study group for this topic?
  March 2012
  July 2012
  November 2012

## Slide 14: References (1)
General
  [1] 11-09/789r2 Technology and Use Case for TGac, Robert S. and Eldad P.
  [2] 11-11/1464r2 The better spectrum utilization for the future WLAN standardization, Yasuhiko Inoue, et. al.
Multi-channel
  [3] 11-09/1037r0 Consideration on Multi-channel in TGac, Jae Seung Lee, et. al.
  [4] 11-10/1159r1 Non contiguous 40+40 additional bandwidth mode, Laurent C., et. al.
OFDMA
  [5] 11-09/138r3 OFDMA Related Issues in VHTL6, James G., et. al.
  [6] 11-10/317r1 DL-OFDMA for Mixed Clients, Brian H., et. al.
  [7] 11-10/787r1 MU with Frequency Domain Multiplexing, Chao-chuu W., et. al.
  [8] 11-10/1054r0 Wide Band OBSS Friendly PSMP, James W., et. al

## Slide 15: References (2)
Uplink MU-MIMO
  [9] 11-09/849r1 Uplink Intensive Usage Models, Rolf de Vegt
  [10] 11-09/852r0 UL MU-MIMO for 11ac, Richard Van Nee, et. al
  [11] 11-09/1036r0 Uplink MU-MIMO Sensitivity to Power Differences and Synchronization Errors, Richard Van Nee
Others
  [12] 11-09/1044r0 Distributed Transmission Timing Adjustment for Synchronous Frame Arrival, Sunggeun Jin, et. al.