## Slide 1: Short Ack
Date: 2012-03-12
Authors:

## Slide 3: Normal Ack overhead
BW (MHz) | Data rate (Kbps) | MPDU Data (bytes) | PPDU duration (us) | Single TXOP (us) | Thruput (Kbps) | Ack (us) | ACK | Ack Pre-amble | Ack Data
2 | 600 | 100 | 1600 | 2828 | 283 | 480 | 16.98% | 8.49% | 8.49%
1 (1x) | 300 | 100 | 2920 | 4388 | 182 | 720 | 16.41% | 5.47% | 10.94%
1 (2x) | 150 | 100 | 5840 | 8368 | 96 | 1400 | 16.73% | 5.74% | 10.99%
Normal Ack overhead can be significant, esp. for acknowledgment to low rate and short packet transmission

## Slide 4: The basic idea
Design a short Ack frame with only STF, LTF1, and a special SIG field
The special SIG field contains information needed for acknowledging a received frame
STF
LTF1
SIG
Frame
Control
Duration
RA
FCS
STF
LTF1
SIG
Service
Normal Ack
Short Ack

## Slide 5: Short Ack SIG design (1)
SIG Field | Bits | Comments
STBC | 1 | Same as in 11ac
Num SS | 2 | Number of spatial streams for SU
SGI | 1 | Short Guard Interval
Coding | 2 | 1st bit is coding type (LDPC/BCC), 2nd bit is for LDPC Nsym ambiguity
MCS | 4 | MCS (a reserved MCS value indicates special SIG for short Ack)
Aggregation bit | 1 | Signals use of AMPDU
Length | 9 | Length field (in symbols when aggregation is ON, is in bytes when aggregation is OFF, Mandate AMPDU for packet sizes > 511 bytes
Ack Indication | 2 | 00: Ack; 01: BA; 10: No Ack; 11: reserved
Reserved | 4 (TBD) | Some possible uses are MAC bits or any other new features etc. Details TBD
CRC | 4 | 4 bits of CRC should be enough
Tail | 6 (TBD) | Tail-biting can be explored
Total | 36 | Same applies to 2MHz SIG
Reload
Reload

## Slide 6: Short Ack SIG design (2)
Tail (6 bits - TBD)
  Same as normal SIG field
CRC (4 bits)
  Same as normal SIG field
Short Ack indication using MCS field (4 bits)
  MCS is not useful to short Ack
  MCS values 11 – 15 are reserved
  One of the reserved MCS values, e.g. 15, can be used to indicate the special SIG for the short Ack frame

## Slide 7: Short Ack SIG design (3)
The reloaded SIG bits (around 22 bits for 1MHz SIG and 34 bits for 2MHz SIG) can be used for the following subfields:
  ACK ID
    Cannot accommodate the whole RA MAC address
    Should be sufficiently long to prevent false positive cases (see next two slides)
    Suggest assigning all unused bits to Ack ID
    For 2MHz SIG, the extra 12 bits can be assigned to Ack ID
  More Data field (1 bit)
    Refer to 11-12-0127-01-00ah-lowe-power-medium-access
    So far only PS-Poll Ack needs this bit
  Short Duration or other multi-transmission protection field (TBD)
  Other fields (TBD)

## Slide 8: False positive cases (1)
An intended Ack receiver A expects an Ack from data receiver B SIFS after the corresponding data transmission; but B fails to send the expected Ack
At exact the same time, a neighbor node D is sending an Ack to C, but the Ack also reaches A
Note that the possibility of this coincidence is extremely low because
  A’s transmission will likely destroy C’s transmission at D, esp. when A’s transmission range is long
  Even if C’s transmission is not destroyed, it should end at exact the same time as A’s transmission; so that D can send out Ack SIFS after A’s (and C’s) transmission
A
B
C
D
Data
Ack
Data
Ack
Ack
A
B
C
D

## Slide 9: False positive cases (2)
Even if the coincidence indicated in previous slide does happen, A still needs to check the following fields of a received Ack before accepting it
  CRC (4 bits) pass – less than 1% at -3dB
  Ack Indication (4 bits) pass
  Ack ID (e.g. 14+ bits) pass
    A long Ack ID can effectively eliminate the false positive cases
Other false positive cases: CRC pass, but wrong Ack indication
  Regular frame (interpreted as short Ack): stop processing fields after SIG, and wait until medium becomes idle
  Ack frame (interpreted as regular frame): try to decode signals after SIG, but find the medium becomes idle

## Slide 10: Ack ID design
Some considerations:
  Short Ack SIG cannot accommodate the whole RA MAC address
  Using partial RA MAC address/AID may lead to a scenario where two or more adjacent STAs may share a same partial address
  It is good to also include some information related to the frame being acknowledged
One good candidate is the partial FCS of the frame being acknowledged
  FCS is a hash of the whole MPDU (including addressing, SC, and data payload) , which can make the Ack ID more randomized
  Partial FCS is directly available in the received frame
It can be even better to also include the scrambler seed in the Service field of the received frame in the calculation of Ack ID
  Some frames, like PS-Poll, always have fixed field values, thus unchanged FCS
  The scrambler seed can add a random factor for this case

## Slide 11: Conclusions
Ack frame with current 802.11 format can causes significant overhead, esp. for low rate and short packet transmissions
We propose a short Ack format with only STF, LTF1, and a special SIG field
We also present some design considerations of the short Ack SIG field, including short Ack indication, Ack ID, and some other subfields

## Slide 12: Motion 1
Move to define a short Ack frame with the following format?
STF
LTF1
SIG

## Slide 13: Motion 2
Move to keep the following short Ack SIG fields the same as those in normal SIG?
  CRC (4 bits)
  Tail (6 bits - TBD)

## Slide 14: Motion 3
Move to use a reserved MCS value to indicate the short Ack frame?

## Slide 15: Motion 4
Move to include an Ack ID field (bits TBD) in short Ack SIG, and use
1) partial FCS and,
2) the information from the scrambling seed in the SERVICE field
of the frame being acknowledged for the computation of the ACK ID for short ACK frames?