## Slide 1: TGah Efficient TIM Encoding
Date: 2012-05-14
Authors:

## Slide 2
Authors:

## Slide 3: Introduction
TIM element in STD 802.11 - 2012
  Supports up to 2007 STAs (2008 AIDs)
  Contains the entire traffic indication bitmap
  Inefficient to encode a low density bitmap
802.11ah requirements
  Need to support more than 2007 STAs (e.g. 6000 STAs) [1]
  Need to support two very different use cases [2]
    Sensor use case: low duty-cycle, Extended Wi-Fi use case: high duty-cycle
  One beacon interval can support only limited number of STAs (e.g. < 100 STAs)
    Low density bitmap for a large number of associated STAs
  TIM has to be encoded efficiently to minimize channel occupancy (overhead)
    TGah data rates are much lower than 802.11a/b/g/n/ac
In this presentation, an efficient TIM encoding scheme is proposed

## Slide 4: Current 802.11 STD Partial Virtual Bitmap Encoding - Example
802.11 STD Partial Virtual Bitmap Encoding
  “… the Partial Virtual Bitmap field consists of octets numbered N1 to N2 of the traffic indication virtual bitmap, where N1 is the largest even number such that bits numbered 1 to (N1 × 8) – 1 in the bitmap are all 0 and N2 is the smallest number such that bits numbered (N2 + 1) × 8 to 2007 in the bitmap are all 0.
Example:
  AID=6, AID=20, AID=45, AID=108, and AID = 1010 bits set to 1
  5 AIDs are encoded into 127 bytes Partial Virtual Bitmap
Current TIM encoding is inefficient for a low density bitmap*.
*) Bitmap density = number of paged stations/number of associated stations
Traffic
Indication
Bitmap
(total 251 Bytes)
Encoded Partial Virtual Bitmap
= 127 bytes

## Slide 5: Proposed Hierarchical Structure of Traffic Indication Map
Basic idea:
  Divide the total AID space into small blocks in a hierarchical manner and transmit only the blocks with non-zero values
    Easier to break a large TIM into small groups of STAs and easier to maintain
    Different classes of STAs can be easily grouped into different groups/pages (e.g. Sensor STAs in Page 1 and Offloading STAs in Page 2)
  Three level hierarchy: Page/Block/Sub-Block
Page 1
Page 2
Page 3
Page 4
NB (e.g. 32) Blocks:
8 Sub-blocks:
NP (e.g. 4) Pages:
1 octet
= 8 STAs
2048 STAs
Supporting max TBD STAs (e.g. 8192)
Block1
Block2
Block3
Block4
Block5
Block6
Block7
Block8
Block31
Block32
64 STAs
…

## Slide 6: AID Structure
Based on the hierarchical structure of the traffic bitmap in the previous slide, the association identifier (AID) structure is maintained as below
  STAs are grouped into Pages, Blocks, Sub-Blocks
The number of Pages and Blocks are variable

## Slide 7: TIM Encoding Propsal - Block level encoding
Partial Virtual Bitmap is encoded in Block level
  Partial virtual bitmap consists of one or more encoded Blocks of a single Page
  Block encoding:
    Block Control(3 bits) + Block Offset (5 bits) + Block Bitmap (1octet) + Sub-Block Bitmaps (0-8octets)
  Block Control field: controls how the Block Bitmap and the Sub-Block Bitmap fields are used
    Block bitmap encoding: AID = [Page Index(2b), Block Offset(5b), n(3b), m(3b)]
      The n-th bit position of the Block Bitmap indicates whether the n-th Sub-Block Bitmap is present in the Sub-Block field
      The m-th bit position of the Sub-Block Bitmap indicates whether the m-th STA has data buffered at the AP
    Single AID: AID = [Page Index(2b), Block Offset(5b), Block Bitmap[5:0]]
      When there is a single AID in a Block, 6 bits of the Block Bitmap field is used to indicate the 6 LSBs of the AID
      The Sub-Block field is not present
    Inverse bitmap: if there are many 1s in the bitmap of a Block, inverse the bitmap and encode the inversed bitmap
      Can expect many cases where STAs sleep for a long period of time
Block Offset
Block Bitmap
Sub-Blocks (variable)
Block L
Block M
Block P
…
Partial Virtual Bitmap
Bitmap Control
Block
Control
1 octet
1 octet
0-8 octets
5 bits
3 bits
Sub-Block
Bitmap 1
Sub-Block
Bitmap 2
Sub-Block
Bitmap M
…
1 octet
Block Control field:
Block Bitmap
Single AID
‘Offset+Length+Bitmap’
+
Inverse bitmap
TBD
Page
Index
2 bits
Bitmap Control (1 octet)

## Slide 8: Offset+Length+Bitmap (OLB)
    ‘Offset+Length+Bitmap’ mode: encodes more than 8 Sub-Block Bitmaps.
      The Block Bitmap field is used to indicate the length of Sub-Block Bitmaps following the Block Bitmap field.
      AID = [Page Index (2b), Block Offset(5b),zeros(6b)]+ p, the p-th bit position of the Sub-Block Bitmap field indicates whether the p-th STA has data buffered at the AP.
      This mode is used when more than 8 contiguous Sub-Blocks are transmitted.
Partial Virtual Bitmap
Bitmap Control
2 octets
Block
Control
3 bits
5 bits
Length (L)
1 octet
OLB mode
Block Offset
L Sub-Block Bitmaps
Bitmap Control (1 octet)
Block n
Block n+1
Block n+m
…
Block p
Block v
…
TBD
Page
Index
2 bits
L octets

## Slide 9: 1. Block Bitmap mode
Block Bitmap encoding
  Block offset(5b) + Block ctrl(3b) + Block bitmap(1 octet) + Sub-block bitmap (0-8 octets)
  Example bitmap:
  Total encoded length = 5 bytes
0010 1001
0000 0000
1001 0001
0000 0000
0000 0000
0001 0000
0000 0000
0000 0000
Traffic indication bitmap:
Sub-block1
1010 0010
Block
bitmap
0010 1001
1001 0001
0001 0000
00000
Block
offset
Sub-block3
Sub-block7
n-th bit position indicates presence of n-th Sub-block
Sub-block
Bitmap 1
Sub-block
Bitmap 3
Sub-block
Bitmap 7
Block Bitmap
Block
Ctrl (3b)
Encoded bitmap
Block 1
AID=51 ( 00 00000 110 011)

## Slide 10: 2. Single AID mode
Single AID mode
  Block offset (5b) + Block ctrl(3b) + last 6 bits of an AID
  Example bitmap:
  Encoded bitmap:
  Total encoded length = 2 bytes
0000 0000
0000 0000
0000 0000
0000 0000
0000 0000
0001 0000
0000 0000
0000 0000
Traffic indication bitmap:
Sub-block1
Sub-block3
Sub-block7
110011 00
Block
bitmap
6 LSBs of the AID
AID=51 ( 00 00000 110 011)
00000
Block
Offset (5b)
Single AID mode
Block
Ctrl (3b)
6 LSBs of the AID
Block 1

## Slide 11: 3. Inverse Bitmap mode
Block bitmap + Inverse mode
  Block offset(5b) + Block ctrl(3b) + Block bitmap(1 octet) + Sub-block bitmaps (0-8 octets)
  Example bitmap:
  Total encoded length = 4 bytes
  Decoding is simply the reverse procedure of the encoding
0010 1001
1111 1111
1111 1111
1111 1111
1111 1111
0001 1111
1111 1111
1111 1111
Traffic indication bitmap:
Sub-block1
1000 0010
Block
Bitmap
1101 0110
1110 0000
00000
Block
Offset(5b)
Sub-block7
n-th bit position indicates presence of n-th Sub-block
Sub-block
Bitmap 1
Sub-block
Bitmap 7
Block Bitmap +Inverse
Block
Ctrl (3bits)
Encoded bitmap
1101 0110
0000 0000
0000 0000
0000 0000
0000 0000
1110 0000
0000 0000
0000 0000
Inverse the bitmap
Block 1

## Slide 12: 4. OLB mode
Offset+Length+Bitmap mode
  Block offset(5b) + Block ctrl(3b) + Length(8b) + Sub-block Bitmaps
  Total encoded length = 16 bytes
0010 1001
0100 1010
1001 0001
0110 1001
1010 1011
0001 0000
0111 0101
0010 0001
Traffic indication
bitmap:
Sub-block1
Length=14
Block
bitmap
00000
Block
offset
Sub-block8
Indicates the length of the Sub-Block bitmaps
Block
Ctrl (3bits)
Encoded bitmap
Block#0
0001 0000
0010 0001
Block#1
0001 0000
0010 0001
1010 1011
0000 0000
0000 0000
1001 0001
0010 1001
0100 1010
1001 0001
0110 1001
1010 1011
0001 0000
0111 0101
0010 0001
0001 0000
0010 0001
0001 0000
0010 0001
1010 1011
1001 0001
Offset+Length +Bitmap mode

## Slide 13: Compression Comparison (1)
Scenario 1: 126 STAs
  126 STAs associated with AP
  X axis indicates the number of paged STAs
    randomly distributed AIDs in [1:126]
    Averaged over 200 iterations
  Y axis represents the size of the compressed bitmap
Curves
  Hierarchy: Block level compression with inverse encoding
  Hierarchy + OLB: Block level compression with ‘Offset + Bitmap + Length’ mode (indicated as ‘Adaptive’ in Y-axis)
  STD-VTIM: Standard virtual TIM map
Including OLB mode helps reduce TIM length in mid-density region of the map by up to 10%.
Compression performance of Hierarchy+OLB is the best in all TIM map densities

## Slide 14: Compression Comparison (2)
Scenario 1: 256 STAs
  256 STAs associated with AP
  X axis indicates the number of paged STAs
    randomly distributed AIDs in [1:256]
    Averaged over 200 iterations
  Y axis represents the size of the compressed bitmap
Curves
  Hierarchy: Block level compression with inverse encoding
  Hierarchy + OLB: Block level compression with ‘Offset + Bitmap + Length’ mode (indicated as ‘Adaptive’ in Y-axis).
  STD-VTIM: Standard virtual TIM map
Including OLB mode helps reduce TIM length in mid-density region of the map by more than 14%.
Compression performance of Hierarchy+OLB is the best in all TIM map densities

## Slide 15: Compression Comparison (3)
Scenario 1: 512 STAs
  512 STAs associated with AP
  X axis indicates the number of paged STAs
    randomly distributed AIDs in [1:512]
    Averaged over 200 iterations
  Y axis represents the size of the compressed bitmap
Curves
  Hierarchy: Block level compression with inverse encoding
  Hierarchy + OLB: Block level compression with ‘Offset + Bitmap + Length’ mode (indicated as ‘Adaptive’ in Y-axis)
  STD-VTIM: Standard virtual TIM map
Including OLB mode helps reduce TIM length in mid-density region of the map by more than 16%.
Compression performance of Hierarchy+OLB is the best in all TIM map densities

## Slide 16: Compression Comparison (4)
Scenario 1: 1024 STAs
  1024 STAs associated with AP
  X axis indicates the number of paged STAs
    randomly distributed AIDs in [1:1024]
    Averaged over 200 iterations
  Y axis represents the size of the compressed bitmap
Curves
  Hierarchy: Block level compression with inverse encoding
  Hierarchy + OLB: Block level compression with ‘Offset + Bitmap + Length’ mode (indicated as ‘Adaptive’ in Y-axis)
  STD-VTIM: Standard virtual TIM map
Including OLB mode helps reduce TIM length in mid-density region of the map by more than 18%.
Compression performance of Hierarchy+OLB is the best in all TIM map densities

## Slide 17: Summary
We proposed
  Hierarchical structure of TIM and AID structure
    Good for grouping and maintaining different types of STAs
    Good for dividing a large size bitmap into smaller size TIM elements
  Block level TIM encoding
    Good encoding for a wide range of number of STAs
    Good for realistic scenarios where limited number of STAs are paged in a single TIM (i.e. the number of paged STAs < 100)
    Up to 30-98% smaller encoded bitmap size compared to the current 802.11 STD for the realistic scenarios
    Compression performance of Hierarchy+OLB is the best in all TIM map densities

## Slide 18: Straw Poll 1
Do you support the hierarchical structure of the traffic indication map shown in Slide 5 and the AID structure shown in Slide 6?
  Y:
  N:
  A:

## Slide 19: Straw Poll 2
Do you support the Block-level TIM encoding outlined in Slide 7-8?
  Y:
  N:
  A:

## Slide 20: Motion 1
Move to accept the hierarchical structure of the traffic indication map shown in Slide 5 and the AID structure shown in Slide 6 in the TGah Specification Framework document.
  Y:
  N:
  A:

## Slide 21: Motion 2
Move to accept the Block-level TIM encoding outlined in Slide 7-8 in the TGah Specification Framework document.
  Y:
  N:
  A:

## Slide 22: References
[1] 11/11-905r3 “TGah Functional Requirements and Evaluation Methodology.”
[2] Rolf de Vegt, “Potential Compromise for 802.11ah Use Case Document,” 11-11/457r0.

## Slide 23: Backup

## Slide 24: Variable Number of Pages and Blocks
The number of Pages and the number of Blocks depend on how the 7 MSBs of an AID is interpreted
Blocks:
1
8
9
16
17
24
25
32
4 Blocks / Page (32 Pages in total)
8 Blocks / Page (16 Pages in total)
16 Blocks / Page (8 Pages in total)
32 Blocks / Page (4 Pages in total)
4x32
…
64
STAs

## Slide 25: Grouping
STAs supporting different use cases can be easily grouped into different Pages
  Example:
    Sensor stations  Page 1
      A large number of STAs, infrequent down-link traffic
    Offloading stations  Page 2
      A small number of STAs, frequent down-link traffic
DTIM Beacon
(Page1,Page2)
DTIM Beacon
(Page1,Page2)
TIM Beacon
(Page2)
TIM Beacon
(Page2)
TIM Beacon
(Page2)
TIM Beacon
(Page2)

## Slide 26: Simulation Setup
Parameters:
  Nasta STAs associated with an AP
  Nasta = 64, 256, 512,1024, 2048, and 8192
  X-axis indicates the number of paged STAs (Npsta)
    The paged STAs randomly distributed in the bitmap [1:Nasta]
    Averaged over 500 iterations
  Y-axis represents the size of the encoded bitmap in bits
  Performance comparison
    STD-VTIM: the current 802.11 standard virtual TIM encoding scheme including 2 byte offset
    Proposed: the proposed Block encoding scheme with Inverse bitmap mode applied

## Slide 27: Results - Scenario 1
Nasta = 64
The proposed encoding is better than or very close to STD-VTIM
  Up to 30% better encoding (Npsta<20, bitmap density < 30%)
  Up to 78% better encoding (Npsta>45, bitmap density > 70%)

## Slide 28: Results - Scenario 2
Nasta = 256
The proposed encoding is better for Npsta <45 (bitmap density < 18%)
  Up to 68% better encoding (Npsta<45)
  Not likely to have a large number of STAs (e.g. > 100 STAs) be paged in a single TIM

## Slide 29: Results - Scenario 3
Nasta = 512
The proposed encoding is better for Npsta <85 (bitmap density < 17%)
  Up to 80% better encoding (Npsta<85)
  Not likely to have >100 STAs be paged in a single TIM

## Slide 30: Results - Scenario 4
Nasta=1024
The proposed encoding is better for Npsta <165 (bitmap density<17%)
  Up to 90% better encoding (Npsta<165)
  Not likely to have >100 STAs be paged in a single TIM

## Slide 31: Results - Scenario 5
Nasta = 2048
The proposed encoding is better for Npsta <330 (bitmap density<16%)
  Up to 95% better encoding (Npsta<330)
  Not likely to have >100 STAs be paged in a single TIM

## Slide 32: Results - Scenario 6
Nasta = 8192
The proposed encoding is better for Npsta <1300 (bitmap density < 16%)
  Up to 98% better encoding (Npsta<1300)
  Not likely to have >100 STAs be paged in a single TIM