## Slide 1: General 802.11 Links
Date: 2012-05-08
Authors:

## Slide 2: Abstract
This presentation discusses the use 802.11 associations as general 802 links and recommends the formation of a study group in this area.

## Slide 3: The Idea
As 802.11 becomes faster and more capable, with higher speeds, QoS, and robust security, it becomes more reasonable to consider using an 802.11 association as a general 802 link.
Use of 802.11 as an 802 link is already supported by 802.11 mesh. But there is no standard way to do this in the non-mesh cases.
The ability to optionally use an 802.11 association as an general 802 link should be extended to ESS and IBSS associations.

## Slide 4: 802.1 Request and Two Use Cases
802.1 AVB has informally requested this 802.11 extension .
Car wiring harnesses are moving to Ethernet. If a car and the service bay of the car dealer both have 802.11, the service bay wants to be able to see the Ethernet stations on your car and automatically access diagnostic information.
Wireless between data center racks for extra capacity when hard-wired connections are saturated.
  http://www.nytimes.com/2012/01/15/business/a-wireless-way-around-data-center-traffic-jams.html

## Slide 5: Three Methods
Here are three methods:
  Just tell people to use mesh since this can already be done with an MBSS (mesh).
  Extend 802.11 so that an ESS and IBSS associations can be used as an 802 link.
  Hide all the devices behind a non-AP, non-Mesh STA through NAT so they appear to be on with the STA with one MAC address. But this is not really a general link or solution because:
    It only works for Internet Protocol traffic.
    It restricts topologies.

## Slide 6: Method 1: 802.11 Mesh Can Act as an 802 LAN Segment
1
11
5
9
7
6
2
4
3
13
14
12
802 LAN
802 LANs
802.11
Mesh
MBSS
This problem is already solved in an 802.11 Mesh MBSS.
Mesh STA with
Mesh Gate
Mesh STA with
Mesh Gate
10
Mesh STA with
Mesh Gate
16
15

## Slide 7: Method 2: Currently You Can’t Use an Infrastructure Association as General Link
1
14
802 LAN
Associated STA
2
802 LAN
Associated STA
ESS
15
1
11
13
12
802 LAN
802 LAN
Infrastructure Association
Associated STA
AP With Portal
14

## Slide 8: Method 2: Currently You Can’t Use an IBSS Association as General Link
1
11
13
14
12
802 LAN
802 LAN
IBSS Association
STA
STA

## Slide 9: Method 3: NAT to One MAC
Multiple IP Hosts can hid behind a STA/NAT and all appear as one MAC address. For example:
1
11
13
12
802 LAN with IP Hosts
802 LAN
Infrastructure Association
Associated STA
AP With Portal
NAT
H1
H2

## Slide 10: Method 3: Problems
Standard NAT only works for IP protocols (including ARP).
  Many of the protocols of concern to 802.1 AVB are non-IP.
Only supports a stub configuration where end stations are connected via an 802.11 connection.
  Method 2 does not provide a through link. Would not work with
1
2
3
4
5
802.3
802.3
802.3
802.11
802.11
802.11

## Slide 11: Possible 802.11 Extensions for Method 2
The technical details would be decided by a Task Group if one is created. But it is possible that the suggested facility would include adding the following capabilities to 802.11:
  Ability for a non-AP, non-Mesh STA to indicate that it supports this facility and has a portal.
  Ability to use
    the four-address format on single hop infrastructure (STA<->AP) and IBSS paths and
    the five-address format on an ESS STA-AP-STA path.
  Ability for an AP to advertise that it supports this facility.

## Slide 12: Loop Prevention
Except inside an 802.11 mesh, where loop prevention is already solved, this is not 802.11’s problem.
The external network(s) should include mechanisms to stop loops.
  For example, 802.1 bridges using 802.1 loop prevention mechanisms.

## Slide 13: Loop Prevention
One possible solution is to recommend adding a bridge on the non-802.11-network side of each portal. This keeps general bridging outside of 802.11.
1
14
802 LAN
Associated STA
2
802 LAN
Associated STA
15
11
AP
B
B

## Slide 14: Motion to Form a Study Committee
Motion:
Request approval by IEEE 802 LMSC to form an 802.11 Study Group on General 802.11 Links as described in doc 11-12/xxxxrx with the intent of creating a PAR and five criteria.
  802.11 WNG TG vote:
  Moved: <name>, Seconded: <name>, Result: y-n-a
Moved by <name> on behalf of the WNG Standing Committee
  802.11 WG vote:
  Moved: <name>, Seconded: <name>, Result: y-n-a

## Slide 15: References
IEEE Std 802.11-2012, “… Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 6 February 2012.