## Slide 1: Improved Spectrum Efficiency for the Next Generation WLANs
Date: 2012-07-18
Authors:

## Slide 2: Outline
Background
  Important use case of recent WLANs
  Requirements
Possible technologies for the future WLANs
  Technologies to enhance the data rate
  Technologies to improve the spectrum efficiency
Summary

## Slide 3: Background
The WLANs have evolved having 10 times higher data rate compared to the other wireless broadband systems, e.g. cellular.
Future WLANs need to have more speed, more bandwidth to support high speed applications and use cases such as cellular offload preserving the user experiences.
Year
1G
10G
100M
Wireless LANs
10M
1M
100k
100G
Data Rate [bit/s]
Cellular
LTE-Advanced
2005
2010
2015
2000
1995
GSM
PDC
WCDMA
HSDPA
LTE
.11b
802.11
.11a
.11g
.11n
.11ad
.11ac
?
The cellular system achieves 1 G bit/s of data rate around 2016
Why don’t we head for the 10 G bit/s WLAN!?

## Slide 4: Important use case of recent WLANs
The way people use the WLANs:
  More and more people enjoy rich applications provided via the Internet with their smartphones and tablets anytime anywhere.
  It is anticipated that the amount of cellular data traffic will be explosively increasing for the next five years or more.
    According to Cisco’s report, the amount of mobile data traffic in 2016 will be increased by 18 times of 2011.
    Available from http://www.cisco.com/en/US/netsol/ns827/networking_solutions_sub_solution.html
Capacity of the cellular system is limited and it is important to offload the data traffic to WLAN networks.
WLANs are expected to support growing mobile data traffic together with the cellular systems

## Slide 5: Cellular data offload
Operators intensively investing to extend their public wireless LAN service areas.
  Major operators in Japan announced their plans to extend the public wireless LAN service area to up to 100,000 spots.
  There are others public WLAN services such as FON and Freespots.
Operators also providing WLAN APs to their customers
  The intension here is to offload the data traffic to/from smartphones and tablets used in the home.
  Millions of APs have already been distributed in Japan.
As a result, dense deployment of WLAN APs can be observed not only in the public area but also residential areas.
Future WLANs need to have an ability to maintain the performance in a densely deployed environment.

## Slide 6: Requirements for the next generation WLANs
To improve the system capacity:
  Higher peak data rate
    Traditional way of enhancing the wireless LAN user experience.
  Improved spectrum efficiency
    Ability to support various kinds of user devices with different capabilities such as supported data rate, number of spatial streams, etc.
    An OBSS coordination may be desired for dense deployment of APs
The system capacity has to be improved to maintain high performance in a place where APs are densely installed.

## Slide 7: Possible technologies to achieve the system capacity of 10 G bit/s
Possible technologies:
  For the higher data rates
    Wider channels
    More spatial streams
  For the improved spectrum efficiency
    DL-OFDMA based on the 20 MHz channel
    Advanced SDMA technique
The system capacity of 10 G bit/s will be achieved by combining some possible technologies.

## Slide 8: Technologies for the higher data rates
Wider channels
  The 802.11ac specified mandatory 80 MHz and optional 160 MHz and 80+80 MHz channels
  The idea is simply to extend the bandwidth/channel, e.g. 320 MHz/ch
More spatial streams
  The 802.11ac extended the MIMO capability,
    To support up to eight spatial streams
    Multi-User MIMO (up to four STAs)
  The next generation WLAN will support more spatial streams
    To have higher data rate
    To support more users in a MU-MIMO transmission
20 MHz defined by 802.11a
40 MHz defined by 802.11n
80 MHz defined by 802.11ac
160 MHz defined by 802.11ac
320 MHz channel
for the next generation WLANs
A simple way to extend the data rate
Non-contiguous channels needs be considered
More OBSS issues being observed
f
AP
x2 Throughput of 802.11ac
STA
STA
STA
STA
STA
…
x2 Throughput
…

## Slide 9: Technologies for the Spectrum Efficiency (1)
Down link OFDMA (DL-OFDMA)
  A technology to make efficient use of frequency resources, i.e. channels, when there are STAs operating with a different channel width
Freq.
Time
802.11a
802.11n
(40 MHz)
802.11ac
(80 MHz)
802.11ac
(160 MHz)
Freq.
Time
802.11a
802.11n
(40 MHz)
802.11ac
(80 MHz)
OFDMA
Capable
STA
(802.11ax)
OFDMA
Capable
STA
(802.11ax)
OFDMA
Capable STA
(802.11ax)
OFDMA
Capable
STA
Or
802.11ac
STA
(160 MHz)
Ch.1
Ch.2
Ch.3
Ch.4
Ch.5
Ch.6
Ch.7
Ch.8
Guard Band
Guard Band
Guard Band
Benefit of this technology
  DL-OFDMA is an effective way of enhancing the frequency resource utilization especially when legacy devices are operating on the same network.
    Ref: Brian Hart, et. Al. “DL OFDMA for Mixed Clients”, IEEE 802.11-10-0317-01
NTT supports DL-OFDMA since it is an effective way to achieve high system capacity in the cases of supporting STAs with difference channel bandwidths as well as supporting legacy devices.

## Slide 10: Technologies for the spectrum efficiency (2)
Advanced SDMA technique
  Extending the transmit beamforming used in MU-MIMO, interference can be reduced by mutual null steering technique to enhance the total system capacity.
   APs on the same channel can transmit data to their STAs at the same time on the same channel
  The system capacity, ideally, will be improved by a factor of two.
AP2
STA1
STA3
AP1
Mutual
Null
Steering
Tx signal
vector
Weight for
STA3 and STA4
Weight for
STA1 and STA2
Signals to
STA3 and STA4
Null formation
(by inserting 0)
Tx Signal of AP2
Calculate from the results of
CSI feedback
STA2
STA4

## Slide 11: Rough estimation of performance improvement
Compared to the 802.11ac,
  Maximum data rate will be increased by introducing
    Wider channel width (320MHz/ch)  x 2
    More spatial stream (16 Nss)  x 2
  System capacity will be also increased by introducing
    DL-OFDMA  x 1.5
    Advanced SDMA  x 1.5
As a total, 9 times of system throughput will be anticipated.
  802.11ac have specified data rates of up to 6.933 G bit/s
  Future WLAN system will have more than 60 G bit/s if the above technologies are adopted.

## Slide 12: Summary
Future WLANs
  Need more system capacity and better connectivity to support important use cases of WLAN such as cellular data offload
Beyond 802.11ac
  System capacity of 10 G bit/s
  Considerations for the serious OBSS issue
  Better spectrum efficiency
Technologies
  Possible technologies
    For the higher data rate: wider channel, more spatial streams
    For the improved spectrum efficiency: OFDMA, Advanced SDMA
Now we have stable drafts of 802.11ac and 802.11ad, and 802.11af and 802.11ah PHYs are based on 802.11ac, it is a good time to start discussion on the next generation WLANs

## Slide 13: Straw Poll
Do you support to create a 802.11 Study Group to discuss next generation WLANs?
  Y-N-A:

## Slide 14: BACKUP SLIDES

## Slide 15: A service image of WLAN in near future
More and more people use cloud services with high performance devices
  Huge amount of data will be exchanged between the network and user terminals/handsets.
Cloud Service
Cloud Service
​
Business applications:
Remote access to the office
Document sharing
audio/video conference and collaboration
Webで調べ物，目的地までのナビゲーション，エンターテイメントサービス，SNSの利用，etc
利用場所やアプリケーションに応じたアクセス手段の選択って可能？
Appropriate access method will be chosen considering the place and application
Home/residential area
Office
Web browsing, entertainment, SNS, network storage, electric paper, navigation, etc.

## Slide 16: Analysis on the possible technologies (1)
Technology | Description | Advantages | Issues
Wider channel bandwidth | <Status> 802.11ac will specify Mandatory 20, 40 and 80 MHz channels Optional 160 MHz and 80+80 MHz channels <Possible Approach> Define 240 MHz channels using three 80 MHz channels, and/or 320 MHz channels using four 80 MHz channels ⇒doubled transmission rate | Simple and feasible way to enhance the data rate | No space to accommodate more than two channels in the current 5GHz band Number of non-overlapping channel decreases Throughput per BSS will seriously degrade by many OBSSs

## Slide 17: Analysis on the possible technologies (2)
Technology | Description | Advantages | Issues
More spatial streams | <Status> 802.11ac specified up to 8 spatial streams. <Possible Approach> Define 16 and/or 32 spatial streams ⇒x2 – x4 transmission rate | Increased maximum data rate as the Nss. Additional degrees of freedom at Tx/Rx antennas offer more diversity gain and/or precise beam steering for transmit beamforming. | Transmission power per antenna decreases inversely proportional to the number of spatial streams  shorter range To support many antennas is difficult for mobile/portable devices. When antenna need to be packed closer together, diversity gain may be spoiled by antenna correlation or coupling effect.

## Slide 18: Analysis on the possible technologies (3)
Technology | Description | Advantages | Issues
OFDMA | <Status> N/A in current 802.11 standard <Possible Approach> Allow 20 MHz sub-channels of an 80 MHz or wider channel to be used by two or more STAs simultaneously. (Reference: 11-10-0317-01) | Increases aggregated throughput per BSS with small overhead. (No CSI feedback is needed.) Simple and efficient way to enhance the spectrum utilization on secondary channels. | Does not increase peak data rate as well as MU-MIMO. Requires precise timing and frequency synchronization and power control among STAs for uplink OFDMA
Advanced SDMA technique | <Status> 802.11ac specified Down link MU-MIMO <Possible Approach> Extend DL MU-MIMO functionality for interference coordination between neighboring BSSs Distributed MIMO Define Uplink MU-MIMO (Reference: 11-09-0852-00) | Increases aggregated throughput per BSS especially when STAs supporting small number of antennas. | Does not increase peak data rate. Need additional overhead due to CSI feedback across BSSs. Requires precise timing and frequency synchronization and power control for uplink MU-MIMO