## Slide 1: Target Wake Times
Date: 2012-07-12
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Introduction
Long-sleeping low power devices need to minimize power consumption
  Call these long-sleepers Z-class devices
Contention for medium at wake time can cause excessive power consumption
  Contention between Z-class devices
  Contention with H-class devices
    H-class = high throughput devices
Propose mechanisms to reduce contention among H and Z class devices
    Minimize wake time for Z-class devices

## Slide 5: Power Consumption
Z-class STA wake to find busy network
  Potentially excessive Listen, Receive, Transmit time
    Wake and wait for access, wait for RX Beacon, wait for other users
  Competition with other waking Z STA and H STA
    Deferral and collision delay
  Causes increased power consumption, decreased battery life
Proposed solutions:
  Minimize probability of Z-Z competition
    Explicitly spread the Z-class devices apart in time using Target Wake Times (TWT)
  Minimize probability of Z-H competition
    Create Z-class-only operating windows of time
      Z-class access windows follow UTIM = Uplink TIM

## Slide 6: Distributing Wake Times
To minimize possibility of busy network upon wake:
  Spread out Z-clients
    Reduced probability of busy medium at wake time
    Minimizes wake to transmit latency
    Also minimizes collision probability
    Minimizes interference between Z class and other classes
Works well when all clients are low traffic and well-spread
  Best when H-class are forced to wait
Need mechanism for spreading out clients
  AP control of wake times
  Propose:
    Requested Wake Time
    Target Wake Time

## Slide 7: Propose a New Element = TWT
RT = Request Type
  Suggestion, Demand, AP accepts, offers alternative for TWT
  Relative vs Absolute TSF reference
  Exponent for WiM
  Flow Direction bit, Flow ID, Flow Type (Request vs NoReq)
TWT = Target Wake Time
  Relates to TSF, i.e. units are usec, 64 bits
    ABSOLUTE or RELATIVE value, depending on RT indication
MWD = Minimum Wake Duration (x32 usec)
WiM = Wake Interval Mantissa
  Mantissa for required wake interval for indicated direction
Exchanged during Association – always initiated by client
  Can also be sent in MGMT Action frame to update during association
  Can send more than one IE, e.g. one for each direction, accommodates multiple phases and periods
Not restricted to use by Z-class STA
1B | 1B | 2B | 8B | 2B | 2B
IEID | Length | RT | TWT | MWD | WiM

## Slide 8: TWT IE RT field
  CRQ = Client Request
    0 = AP Response
    1 = Client Request
  TWTC = TWT Command
    000b = client NULL suggestion (let AP choose wake time)
    001b = client suggestion, AP accepts client suggestion
    010b = client demand, AP accepts client demand
    011b = Reserved
    100b = Reserved
    101b = AP alternative suggestion
    110b = AP alternative demand
    111b = AP Rejects TWT setup
  ABS = Absolute
    0 = Relative TSF value (i.e. NEXT TBTT + TWT value)
    1 = Absolute TSF value
  DIR = Flow Direction
    0 = Client to AP
    1 = AP to Client
  FT = Flow Type
    0 = Request driven – e.g. Client must send POLL or Trigger
    1 = No Request necessary – e.g. AP transmits without first hearing Poll or Trigger, or uplink TX (client transmits)
  FID = Flow ID, RA-TA pair unique (not directionally unique)
  WIEXP = Wi Exponent
    Wake Interval Exponent, i.e. Wi = WiM x 2 ^ WiEXP
0 | 1 3 | 4 | 5 | 6 | 7 9 | 10 15
CRQ | TWTC | ABS | DIR | FT | FID | WIEXP

## Slide 9: Beacon Power Consumption
Z-class power consumption
  Includes time spent waiting for and receiving long slow Beacon
  Prefer to eliminate beacon reception
With TWT, not necessary to wake for Beacon
  STA Wakes at TWT and transmits after cursory CCA check
  Since Beacon was skipped, TSF adjustment needed
  Option 1:
    Create ACK Frame that includes partial TSF value = T-ACK
    E.g. ACK with 3 Bytes of TSF_LSB
      Potentially also signals operating information change
      I.e. suggestion to wake for and receive a beacon for updated information
  Option 2:
    DL Frame contains TSF information

## Slide 10: BA With Management ACK
AMPDU contents rules
  Currently allows MGMT Action NoAck to be included with DATA frames
  Desire ACK-able MGMT Action frame
    E.g. to deliver :
      NEXT TWT
      TSF
      Beacon Change Notification
Add MGMT Action (regular ACK) frame to AMPDU contents
  One frame allowed
  ACK with MGMT ACK bit in BA frame
    Use one of the many reserved bits in the BA frame

## Slide 11: ACK for Mgmt Action frame within AMPDU
A reserved bit within the BA Control field conveys ACK status for the maximum one ACK-able MGMT Action frame in an AMPDU
New Bit MGMT_ACK
B5

## Slide 12: T-ACK vs MGMT TSF
Comparison of location for TSF information for waking device
  Within AMPDU inside of MGMT Action frame
    Allows for maximum information transfer
      E.g. TWT + TSF + Beacon Change notification + other mgmt signaling
    Simple, direct, limited additional PHY or MAC overhead
  Within T-ACK
    Additional information has direct impact on size of ACK
      AP can choose amount of information to include
      Variable sized ACK = DUR estimation problem?
    TSF information can be used by any waking STA

## Slide 13: Power Comparison
Compare:
  PS-Poll /U-APSD (traditional mechanism using TIM signaling)
  TIM-mediated UL slotting
  TWT

## Slide 14: Power Consumption Profiles
Baseline PS-POLL
Slide 14
Beacon
Wake
LM
SM
RM
LM/RM
TM
RM
UL
BA
LM/RM
BA
DL
TM
RM
SM
Sleep
Access delay
Lookup + Access delay
Beacon
LM
SM
RM
?M
TM
RM
UL
BA
BA
DL
TM
RM
SM
Slot delay
Wake
Sleep
LM
SM
TM
RM
UL
BA
BA
DL
TM
RM
SM
Wake
Sleep
Beacon-based access
TWT-based access

## Slide 15: Sensor Battery Life
900 mAh Battery
Chart: MPYLD_500B_APDLY_1ms_MDLY_1085us_SLP0.01mW_DTIM3_TXTCP_PAON_500mW_900GHz_COLL_0%_SCYC_10000
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160
PS_POLL | 470.68 | 470.68 | 470.68 | 470.68 | 470.68 | 414.8387 | 414.8387 | 392.1441 | 366.1064 | 306.597 | 306.597 | 306.597 | 229.5233 | 229.5233 | 229.5233 | 184.3576
BCN_UL | 1045.1191 | 1045.1191 | 1045.1191 | 1045.1191 | 1045.1191 | 978.0882 | 978.0882 | 948.4154 | 912.4271 | 821.3111 | 821.3111 | 821.3111 | 680.8374 | 680.8374 | 680.8374 | 583.5548
TWT | 1332.9079 | 1332.9079 | 1332.9079 | 1332.9079 | 1332.9079 | 1332.885 | 1332.885 | 1332.8729 | 1332.8549 | 1332.7899 | 1332.7899 | 1332.7899 | 1332.6011 | 1332.6011 | 1332.6011 | 1332.3421

## Slide 16: Straw Poll
Do you support adding to the specification framework document an item to include a mechanism to set wake times and intervals for clients?