## Slide 1: Max Idle Period Extension for 802.11ah Power Save Follow Up
Date: 2012-07-15
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Background
Two features of Max Idle Period extension were included in the latest 11ah specification framework (11/1137r9)
4.1 Power Save
R.4.1.C: The draft specification shall support that BSS Max Idle Period shall be able to set to a longer value (~days) by changing the unit of Max Idle Period larger than 1000 TU (1s). The sleep interval unit extension method is TBD [May 2012 meeting minutes].
R.4.1.D: The draft specification shall support that the AP shall be able to support multiple Max Idle Periods. [May 2012 meeting minutes]

## Slide 5: Potential Method Supporting Max Idle Period Extension (1/2)
      Step1: AP advertises its capability of supporting “very long Max Idle Period” in probe response frame and beacon frame as an IE.
      The capability of supporting “very long Max Idle Period” shall be indicated by 11ah AP. It could be a one-bit indication in an IE.
      The IE indicating the support of “very long Max Idle Period” is optionally present in 11ah beacon frame.
      11ah AP could include the indication of supporting “very long Max Idle Period” in probe response frame.
      A “long sleeper” STA can choose to associate with the AP that supports “very long Max Idle Period” .

## Slide 6: Potential Method Supporting Max Idle Period Extension (2/2)
      Step2 : STA includes its preferred Max Idle Period value in the (Re) Association Request frame;
      Step3: The AP selects one of its supported Max Idle Period based on the STA’s preferred Max Idle Period value, and indicates its accepted value to the STA in the (Re)Association Response frame
      The AP may accept the preferred Max Idle Period value the STA requested or select another AP-supported value for the STA close to the requested value from the STA.
      Upon receiving the Max Idle Period value from the AP, the STA can either keep or abort the association.

## Slide 7: Summary
      Two features of Max Idle Period extension were included in the latest 11ah specification framework (11/1137r9)
      Very long Max Idle Period extension
      Multiple Max Idle Period extension
      Propose a method to support Max Idle Period extension
      AP advertises its capability of supporting “very long Max Idle Period” in probe response frame and beacon frame as an IE;
      STA includes its preferred Max Idle Period value in the (Re) Association Request frame;
      The AP selects one of its supported Max Idle Period based on the STA’s preferred Max Idle Period value, and indicates its accepted value to the STA in the (Re)Association Response frame.

## Slide 8: References
[1] 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document
[2] 802.11v-2011
[3] 11-11-0985-01-00ah-performance-evaluation-of-multiple-STAs’-authentication-and-association-process
[4]11-11-1204-01-00ah-power-saving-mechanism-consideration-for-802.11ah-framework
[5] 11-11-0060-01-00ah-low-power-capability-support-for-802-11ah

## Slide 9: Pre-motion 1
Do you support to add in 11ah spec framework that AP advertises its capability of supporting “very long Max Idle Period” in probe response frame and beacon frame as an IE?
  Y:
  N:
  A:
Slide 9

## Slide 10: Pre-motion 2
Do you support to add in 11ah spec framework that STA includes its preferred Max Idle Period value in the (Re) Association Request frame; the AP selects one of its supported Max Idle Period based on the STA’s preferred Max Idle Period value, and indicates its accepted value to the STA in the (Re)Association Response frame?
  Y:
  N:
  A:
Slide 10