## Slide 1: Sensor Only BSS
Date: 2012-09-16
Authors:
Name | Affiliations | Address | Phone | email
George Calcev | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 | +1 (847) 818 1778 x 310 | George.Calcev@huawei.com
Bin Chen | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 | +1 (847) 818 1778 | Bin.Chen@huawei.com
Lin Cai | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 |  | 
Lukasz Krzymien | Huawei | 3601 Algonquin Road, Rolling Meadows, IL 60008 |  | 

## Slide 2: Sensors Only BSS
Name | Affiliations | Address | Phone | email
Minyoung Park | Intel Corp. |  |  | minyoung.park@intel.com
Tom Tetzlaff | Intel Corp. |  |  | thomas.a.tetzlaff@intel.com
Emily Qi | Intel Corp. |  |  | emily.h.qi@intel.com
Thomas Kenney | Intel Corp. |  |  | 
Yong Liu | Marvell |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Sudhir Srinivasa | Marvell |  |  | 
Authors:

## Slide 3
Name | Affiliations | Address | Phone | email
Yongho Seok | LG Electronics |  |  | 
Jinsoo Choi | LG Electronics |  |  | 
Jeongki Kim | LG Electronics |  |  | 
Jinsam Kwak | LG Electronics |  |  | 
ChaoChun Wang | MediaTek |  |  | 
James Wang | MediaTek |  |  | 
Jianhan Liu | MediaTek |  |  | 
Vish Ponnampalam | MediaTek |  |  | 
James Yee | MediaTek |  |  | 
Sayantan Choudhury | Nokia |  |  | 
Chittabrata Ghosh | Nokia |  |  | 
Taejoon Kim | Nokia |  |  | 
Esa Tuomaala | Nokia |  |  | 
Klaus Doppler | Nokia |  |  | 
Authors:

## Slide 4
Name | Affiliations | Address | Phone | email
Matthew Fischer | Broadcom |  |  | 
Eric Wong | Broadcom |  |  | 
Simone Merlin | Qualcomm |  |  | 
Zhi Quan | Qualcomm |  |  | 
Santosh Abraham | Qualcomm |  |  | 
Hemanth Sampath | Qualcomm |  |  | 
VK Jones | Qualcomm |  |  | 
Menzo Wentink | Qualcomm |  |  | 
Sun, Bo | ZTE |  |  | sun.bo1@zte.com.cn
Lv, Kaiying | ZTE |  |  | lv.kaiying@zte.com.cn
Huai-Rong Shao | Samsung |  |  | hr.shao@samsung.com
Chiu Ngo | Samsung |  |  | chiu.ngo@samsung.com
Minho Cheong | ETRI |  |  | minho@etri.re.kr
Jae Seung Lee | ETRI |  |  | jasonlee@etri.re.kr
Heejung Yu | ETRI |  |  | heejung@etri.re.kr
Hyoung Jin Kwon | ETRI |  |  | kwonjin@etri.re.kr
Authors:

## Slide 5: Authors:
Name | Affiliations | Address | Phone | email
Haiguang Wang | I2R |  |  | 
Shoukang Zheng | I2R |  |  | 
Yeow Wai Leong | I2R |  |  | 
Zander Lei | I2R |  |  | 
Jaya Shankar | I2R |  |  | 
Anh Tuan Hoang | I2R |  |  | 
Joseph Teo Chee Ming | I2R |  |  | 
Rojan Chitrakar | Panasonic |  |  | Rojan.Chitrakar@sg.panasonic.com
Ken Mori | Panasonic |  |  | Mori.ken1@jp.panasonic.com

## Slide 6: Sensor Networks vs. Offload Networks
The 11ah targets sensor networks as well as offloading use case scenarios [1,2]
The sensor traffic is very different from the offloading traffic
Sensor traffic:
  Requires low data rate
  Low duty cycle (hours, days)
  Utility operator managed
Offload traffic:
  High data rate
  Bursty
  Cellular operator managed (HS2.0)

## Slide 7: Sensor Only BSS
The likelihood that large sensor networks coexists in the same BSS with the offloading traffic is low
They are usually operated by different entities (utility companies versus cellular operators)
Each type of traffic could require different BSS optimization, signaling and services
  Offloading may require the implementation of HS2.0 features
  Offloading may require the implementation of Lawful Intercept and Emergency Calls
  Offloading may require the use of larger bandwidths 2MHz and above
  Smart Grid and Sensor Networks may require “last gasp” signaling and high volume association after power loss
  Sensor Networks will likely operate only in 1 or 2MHz bandwidth

## Slide 8: Sensor Only BSS
Recently Marvell proposed the introduction of 11u/ HS2.0 features in the short beacon.
These features are not necessary in the BSS serving sensors only, where can be additional overhead
A separation between these modes of operation would offer specific framework for a better design
Identifying what type devices are requesting the association cuts the unwanted overhead related to the probe request/response

## Slide 9: Sensor Only BSS
We propose that a BSS would have three dedicated modes of operation either to allow only sensor traffic or to allow both sensors and offloading or only offloading devices
A STA could declare in the Probe Request message or at the association as Sensor Device Only, Offloading Device Only or Mixed Mode Device
A beacon could carry 2 bits that signal that the BSS accepts Sensor Only Devices, Offloading Only Devices, or Mixed Mode devices
Some potential benefits:
  The beacons sequence (short long) could have different periodicity in Sensor Only BSS
  The Probe Response can be done based on device’s type that sent a Probe Request
  The offload devices would not try to associate with AP in Sensor Only reducing the overhead

## Slide 10: Sensor Only BSS
High performance AP that supports very large number of sensors and smart meters will be configured Sensor Only
When lower performance devices are required such as 11ah for AP for home deployment Mixed Mode will be marked as true
Some private stores, for instance Starbucks, could have Offloading Only BSS for their customers

## Slide 11: References
11-12-905-04ah-TGah functional requirements and evaluation methodology
11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document

## Slide 12: Straw Poll/ Pre-Motion 1
Do you support the separation between BSS Sensor Only, Offloading Only and Mixed Mode as presented above?
Yes 32
No 0
Abstain 3

## Slide 13: Straw Poll/ Pre-Motion 2
Do you support the identification of STA device types as Sensor Only, Offloading Only and Mixed Mode STAs ?
Yes 29
No 0
Abstain 2

## Slide 14: Straw Poll/Pre-Motion 3
Do you support that the Sensor/Offload/Mixed BSS type is provided in beacons /Probe Response?
Yes
No
Abstain

## Slide 15: Motion 1
Move to accept the separation between BSS Sensor Only, BSS Offloading Only and BSS Mixed Mode ?
Yes
No
Abstain

## Slide 16: Motion 2
Move to accept the identification of STA device types as Sensor Only, Offloading Only and Mixed Mode STAs ?
Yes
No
Abstain

## Slide 17: Motion 3
Move to accept that the Sensor Only/Offload Only/Mixed BSS type is provided in beacons /Probe Response?
Yes
No
Abstain