## Slide 1
Using saved IP to make a connection
Date: 2012-11
Authors:
Name | Affiliations | Address | Phone | email
Chen Yanming | China Mobile | 16A,Danling Street, Haidian District, Beijing, China, 100080 | +86 10 52696688-3045 | chenyanming@cmdi.chinamobile.com
CHEN Yanming, CMCC
Slide 1

## Slide 2: Topics
Background
Problem
Proposal
CHEN Yanming, CMCC
Slide 2

## Slide 3: Background
When a new connection begin, STA should send DHCP requests by using its saved IP, which is workable at last time.
  This method comes from wired network, which is usable because of less mobility of the wired terminal.
No unitized way to standardizing the time of using last IP when connecting.
Device vendor has its own method to deal with this process.
  Different devices allowed different time spending for DHCP requests with old IP.
CHEN Yanming, CMCC
Slide 3

## Slide 4: Problem
  The nonstandard way of using saved IP for connection will cause the following results:
  Terminal will wait a long time to gain a valid IP because of trying the old IP too much times.
  Too long to get a valid IP because of using the unchanged old IP all the time.
    Get back ”can not get the IP address”
    The terminal even stop working
CHEN Yanming, CMCC
Slide 4

## Slide 5: Problem
  Evaluation problem
  Operators want to analyze the network DHCP request success rate by using the following formula:
    DHCP Request Success Rate=DHCP Request Success Time / DHCP Request Times
      DHCPReqSucRate=DHCPReqSucTimes/ DHCPReqTimes
  Try too much time to gain a valid IP will increase the value of “DHCPReqTimes” and then finally reduce the value of “DHCPReqSucRate” .
    Even if there is no problem of the AP/AC, or the network situation.
CHEN Yanming, CMCC
Slide 5

## Slide 6: Proposal
Describe
  Unify the time range of using last IP by AP controlling.
  An estimate can be made when the time out of using last IP happened.
  The number of the time out events is an important indicator to analyze the reason of DHCP request failures.
    Which can discriminate the true problems of AP.
  Realization
  A new counter is proposed to add into AP MIB, called
  dot11timeoutofusinglastIP
  And then, the formula of DHCP request success rate can change to:
  DHCPReqSucRate=DHCPReqSucTimes/
  (DHCPReqTimes - dot11timeoutofusinglastIP)
CHEN Yanming, CMCC
Slide 6

## Slide 7: Straw Poll
  Do you think it meaningful to put the TimeoutofusinglastIP counter into the MIB to estimate the connection capability of AP more factually?
- Y
- N
- A
CHEN Yanming, CMCC
Slide 7