## Slide 1: IEEE 802.11 Accounting Extensions
Date: 2013-05-10
Authors:

## Slide 2: Abstract
This presentation proposes extensions to the existing RADIUS accounting attributes to retrieve and forward to service providers better information about the service delivered by an IEEE 802.11 wireless link.

## Slide 3: What is RADIUS Accounting?
RADIUS accounting reports about the usage of an IEEE 802.11 session
Association
EAP Identity Request
EAP Identity Response
EAP Request
EAP Response
EAP Success
Access Request
Access Challenge
Access Request
Access Accept
AAA Server
Internet
Master-Key
Key Management & Data Encryption
Disassociation
RADIUS Authentication Authorization
User Data Session
RADIUS Accounting
Accounting Request - Start
Accounting Request - Interim
Accounting Request - Interim
Accounting Request - Stop

## Slide 4: Where is RADIUS Accounting used?
Subscriber specific service monitoring in IEEE 802.11
Usage information for Wi-Fi roaming business
Hotspot Operators
Subscriber
Access
Control
HSS
AAAH
Mobile Operator
HLR
AAAH
Mobile Operator
AAAH
Home
ISP
Roaming
Broker
Service Providers

## Slide 5: What kind of information is available today?
RFC 2866 |  |  | RFC 2869 | 
Type | Attribute |  | Type | Attribute
40 | Acct-Status-Type |  | 52 | Acct-Input-Gigawords
41 | Acct-Delay-Time |  | 53 | Acct-Output-Gigawords
42 | Acct-Input-Octets |  |  | 
43 | Acct-Output-Octets |  |  | 
44 | Acct-Session-Id |  | RFC 5580 | 
45 | Acct-Authentic |  | Type | Attribute
46 | Acct-Session-Time |  | 127 | Location-Information
47 | Acct-Input-Packets |  | 128 | Location-Data
48 | Acct-Output-Packets |  | 129 | Basic-Location-Policy-Rules
49 | Acct-Terminate-Cause |  | 130 | Extended-Location-Policy-Rules
50 | Acct-Multi-Session-Id |  |  | 
51 | Acct-Link-Count |  |  | 
RADIUS Accounting attributes are specified in RFC2866 and RFC2869 with IEEE 802 specific interpretations in RFC 3580.
Location information within RADIUS Accounting is specified in RFC 5580.

## Slide 6: What is the Issue with the current Accounting Attributes?
All bits are treated equally!
… which may be valid for wired links.
However there is a huge variation of link behavior in IEEE 802.11
From a user perspective (and from a business perspective) it makes a difference, whether bits are delivered over an error-prone 1 Mbps link or an error-free 300 Mbps link.
RADIUS Accounting currently is not able to report anything about the IEEE 802.11 link characteristics.
It would be desirable to include IEEE 802.11 link attributes into accounting records.
  Which ones?

## Slide 7: IEEE 802.11 Link Information available at the Linux OS Interface (iw)
root@OpenWrt:/# iw dev wlan0 station dump
Station 00:1c:b3:46:59:14 (on wlan0)
inactive time: 620 ms
rx bytes: 20671
rx packets: 127
tx bytes: 22716
tx packets: 93
tx retries: 1
tx failed: 0
signal: -57 [-69, -57] dBm
signal avg: -57 [-69, -57] dBm
tx bitrate: 36.0 MBit/s
rx bitrate: 54.0 MBit/s
authorized: yes
authenticated: yes
preamble: long
WMM/WME: no
MFP: no
TDLS peer: no
root@OpenWrt:/#
BusyBox v1.19.4 (2012-11-18 02:19:39 UTC) built-in shell (ash)
Enter 'help' for a list of built-in commands.
_______ ________ __
| |.-----.-----.-----.| | | |.----.| |_
| - || _ | -__| || | | || _|| _|
|_______|| __|_____|__|__||________||__| |____|
|__| W I R E L E S S F R E E D O M
-----------------------------------------------------
ATTITUDE ADJUSTMENT (12.09-rc1, r34185)
-----------------------------------------------------
* 1/4 oz Vodka Pour all ingredients into mixing
* 1/4 oz Gin tin with ice, strain into glass.
* 1/4 oz Amaretto
* 1/4 oz Triple sec
* 1/4 oz Peach schnapps
* 1/4 oz Sour mix
* 1 splash Cranberry juice
-----------------------------------------------------
root@OpenWrt:/#

## Slide 8: Link Information in IEEE 802.11
(Much) More comprehensive information would be available in IEEE 802.11 by making use of the defined MAC counters
Even more when taking into account the STA Statistics Report, introduced by IEEE 802.11k and IEEE 802.11v
Probably much too much to make an appropriate choice easy.

## Slide 9: Practicalities of Defining RADIUS Attributes
RADIUS Attributes are usually defined by the IETF
  …when the attributes do not touch MAC or PHY layer issues, or specific network knowledge is required.
RADIUS Attributes may be defined by other SDOs, making use of the vendor-specific extension fork.
When defining IEEE 802.11 link specific RADIUS Attributes, both approaches would be possible
  Using a ‘vendor-specific’ extension to the attribute space
  Cooperating with IETF RADEXT on creating an RFC on it

## Slide 10: Conclusion
IMHO, it would make sense to define a couple of IEEE 802.11 link specific accounting attributes to get better reporting of service quality in Wi-Fi hotspots.
Open issue: how to select the small number of attributes, which really make sense from a service quality perspective?
Questions and Comments?