## Slide 1: Relay Flow Control
Date: 2013-05-13
Authors:

## Slide 5: Outline
A relay may service multiple STAs at a single time, and have limited memory buffer to frames that are not yet forwarded
The concept of a flow control mechanism has been presented in [1]
This presentation presents the details for flow control signaling and operation
Propose that Relay use two new Relay Action frames as a signaling for flow suspend and resume
Note: The protocol proposed here for Relay Flow Control is separate from the rules for Relay TXOP sharing

## Slide 6: New Relay Action Frames
Field Value | Meaning
0 | Reachable Address Update
1 | Relay Flow Suspend
2 | Relay Flow Resume
3-255 | Reserved
Table 8-295as—Relay Action field values
Order | Information
1 | Category
2 | Relay Action
3 | Suspend Duration (usec)
Table 8-295ax—
Relay Flow Suspend frame format
Order | Information
1 | Category
2 | Relay Action
Table 8-295ay—
Relay Flow Resume frame format

## Slide 7: Flow Control Procedure
To suspend frame transmissions to Relay, a Relay may send a unicast or broadcast Relay Flow Suspend action frame, and Suspend Duration > 0
  STAs shall not transmit data frames to the STA addressed in the TA for the amount of time indicated in Suspend Duration field
  STAs may resume normal procedure for data frame transmission when the Suspend Duration time has expired
To restart frame transmissions to Relay, a Relay may send a unicast or broadcast Relay Flow Resume action frame
  STAs shall cancel the flow suspend time, and resume normal procedure for data frame transmissions to the STA addressed in the TA
  The sending of Relay Flow Resume action frame by the Relay is optional, and may be used by the Relay to cancel an existing Suspend Duration

## Slide 8: Example of Flow Control Operation
ACK
Relay is unable to forward this data frame in the current TXOP, and storing causes the buffer capacity threshold to be met . Relay sends Relay Flow Suspend action frame to suspend all DATA transmission for Suspend Duration time.
DATA
RELAY
STA1
FLOW SUSPEND
RA = Broadcast
Suspend Duration> 0
FLOW RESUME
DATA
STA2
ACK
STAs that receives the Relay Flow Suspend action frame shall not transmit to the STA addressed in the TA for Suspend Duration time.
STAs that receives Relay Flow Resume action frame shall resume normal procedure for frame transmissions to the STA addressed in the TA.
TX Resume
TX Suspend
RA = Broadcast

## Slide 9: Conclusion
Proposed that Relay use two new Relay Action frames as a signaling for flow suspend and resume

## Slide 10: Straw Poll 1
Do you support to define two new Relay Action frames in slide 6 for Relay flow control signaling, and the flow control operation in slide 7?
  Yes
  No
  Abstain

## Slide 11: Straw Poll 2
Do you support to define a 1-bit field in FC in one of the S1G control response frame which includes a time field for Relay flow control signaling?
  Yes
  No
  Abstain

## Slide 12: References
[1] E. Wong et al., “Two-Hop Relay Function,” IEEE 11-12/1330r0
[2] IEEE 802.11 REVmb D12.0