## Slide 1: The New Public Phone Service -Non Contact Ultra High Speed Contents Download
Date: 2014/01/21
Authors:
Name | Affiliations | Address | Phone | email
Masashi Shimizu | NTT Corporation | Hikarinooka 1-1, Yokosuka 239-0847 Japan | +81-46-859-3339 | shimizu.masashi@lab.ntt.co.jp
Ken Hiraga | NTT Corporation | Hikarinooka 1-1, Yokosuka 239-0847 Japan | +81-46-859-3339 | hiraga.ken@lab.ntt.co.jp
Kazumitsu Sakamoto | NTT Corporation | Hikarinooka 1-1, Yokosuka 239-0847 Japan | +81-46-859-3339 | sakamoto.kazumitsu@lab.ntt.co.jp
Tomohiro Seki | NTT Corporation | Hikarinooka 1-1, Yokosuka 239-0847 Japan | +81-46-859-3339 | seki.tomohiro@lab.ntt.co.jp
Toshimitsu Tsubaki | NTT Corporation | Hikarinooka 1-1, Yokosuka 239-0847 Japan | +81-46-859-3339 | tsubaki.toshimitsu@lab.ntt.co.jp
Hideki Toshinaga | NTT Corporation | Hikarinooka 1-1, Yokosuka 239-0847 Japan | +81-46-859-3339 | toshinaga.hideki@lab.ntt.co.jp
Tadao Nakagawa | NTT Corporation | Hikarinooka 1-1, Yokosuka 239-0847 Japan | +81-46-859-3339 | nakagawa.tadao@lab.ntt.co.jp

## Slide 2: Abstract
This contribution will present the non-contact ultra high speed transmission service over 60-GHz band. With this contribution, it is considered that the 60-GHz band will be useful in non-contact file download kiosk system with up to 24 G bit/s and with over 100 G bit/s using MIMO.
Purpose: Input for discussion on utilizing MIMO over line-of-sight channel for download kiosk application in “beyond ad”.

## Slide 3
Real WLAN Speed Measurements
9:00 AM at Tokyo Station
LTE Tethering 802.11g
Real Speed was estimated as 2.1Mbps

## Slide 4: High Speed Data Download Service
NTT must provide carrier grade services.
P-to-P is mandate to keep high transmission rate.
Book
4K Images
Photo and Cam
Big Data
Point-to-Multipoint
Point-to-Point
High speed
Data size is growing up
LTE/3G, WiFi, WiMAX, etc
Optical NW
Crowd server
Music
Movie
Game
High Speed
Reliable communication
(guaranteed quantity)
Data rate was defined by the number of users.

## Slide 5: Service roadmap
NW
Contents Provider
Crowd Server
Rental Video
Platform
Any Where!!
Step１
Contents Provider
(Rental Video)
Step ２
（Convenience Store:48,000、Station:9300
Public Phone 210,000)
Contents Provider
Stations
Public phone
Gas station
Convenience Store
Step３
57,000,000
Subscriber
・At first, Solution for contents provider will launch at 2015.
・Services will expand to public space application.
・Finally we will these services contain anywhere.
Cash Files
Cash Files
Cash Files
Public
Space
Stations
Convenience Stores

## Slide 6: Number of Public Phone
Analog
Digital
Digital (IC-card payment)
2000~2013
FY 2012
FY 1999
FY 2000
FY 2001
FY 2002
FY 2003
FY 2004
FY 2005
FY 2006
FY 2007
FY 2008
FY 2009
FY 2010
FY 2011

## Slide 7
We focus on the usage of millimeter wave communications with ultra short range communication (non contact).
Not only ultra high speed. The Total Contact Time must be less than 1 Second.
Our Target Usage Models
【 Rapid Download / Upload】
Content Holder
Kiosk
Home GW
movie
Authentication
Audio and Video equipment
⇔ mobile terminal
Public use
Local use
Throughput :
> 2Gbps
Range :
< 5cm
Throughput :
> 2Gbps
Range :
< 5cm

## Slide 8
    Standard Comparison
Communication Range
Throughput (Bps)
1m
100M
1G
10G
Near field Communication
10cm
Transfer Jet
802.11ad
New standard
10m
～
～
～
～
Target
Our target system concept is similar to TransferJet.
  But data rate is less than 1 Gbps.
TrasferJet Consortium
Promoters (9 Companies)
Sony Corporation
Toshiba Corporation
etc.
Adopters(36 Companies)
NTT Docomo, INC.
KDDI Corporation
etc.
ISO15693
ISO14443

## Slide 9
Standard Specifications
 | Frequency band | Modulation | Range | Beamforming | IP | Topology | DRM
TransferJet | 4.5 GHz | UWB 560Mbps (max) | < 5cm | Not Required | Not support | P to P | Support ( CPRM etc.)
IEEE 802.11ad | 60 GHz | 1.115Gbps（SC, BPSK） Option: 6.756Gbps（OFDM, 64QAM） | In room gaming,…5m Rapid sync-n-go file transfer…8m Projection to TV or projection in conf. room…8m | Mandatory | Support | AP-based BSS (Basic Service Set) PBSS (Personal BSS)…P to P | Support over IP (DTCP-IP)
Target | 60 GHz | >2Gbps OFDM or SC+FDE | < 5cm | Not Required | Support | P to P | Support

## Slide 10
Discussion
  We need a fast link establishment. (about 100 msec or less)
WiGig: Association/Authentication
About 1 sec
SD: File System Mount
About 3 sec
Data transmission
Target time
100 msec or less

## Slide 11
Surveillance of Waiting Time for Web Site Response
 | Average | Men | Women | Age 20’s | Age 30’s | Age40’s
3Sec | 17.0 （17.0） | 20.9 | 12.2 | 22.8 | 14.0 | 14.9
5Sec | 23.8 （40.8） | 25.5 | 21.7 | 18.9 | 23.8 | 29.7
8Sec | 7.5 （48.3） | 5.0 | 10.6 | 7.1 | 7.6 | 7.9
10Sec | 25.0 （73.3） | 25.9 | 23.9 | 26.8 | 27.9 | 17.8
15Sec | 13.3 （86.6） | 11.8 | 15.0 | 12.6 | 11.0 | 17.8
30Sec | 8.0 （94.6） | 7.3 | 8.9 | 6.3 | 10.5 | 5.9
More than 30Sec | 5.5 （100） | 3.6 | 7.8 | 5.5 | 5.2 | 5.9
(%)
http://www.citizen.co.jp/research/index.html
How long can you wait a response on the web site without stress ?

## Slide 12: Download Time Comparison
Contents | File size | Download time (Sec) |  |  | 
 |  | First Step | Second Step | Transfer Jet | 802.11ac (Draft)
 |  | Read Speed 2 Gbit/s | Read Speed 4 Gbit/s | Real Speed 375 Mbit/s | Read Speed 530 Mbit/s
Book | １ MByte | 0.004 | 0.002 | 0.021 | 0.015
Comic | 30 MByte | 0.12 | 0.06 | 0.64 | 0.45
Magazine | 300 MByte | 1.2 | 0.6 | 6.4 | 4.5
CD | 700 MByte | 2.8 | 1.4 | 14.9 | 10.6
Movie (1hour) | 1.8 GByte | 7.2 | 3.6 | 38.4 | 27.2
Movie (2hour) | 3.6 GByte | 14.4 | 7.2 | 76.8 | 54.3

## Slide 13
Realization of “Real touch-and-get”
“Real touch-and-get” within 0.5 sec
download with toll-gate
<0.5-sec download
4 newspapers
1 Magazine
1 CD
1-hr Video
(MPEG2)
1 DVD
Transmission rate [Gbit/s]
File size [GBytes]
2
4
40
100
10
400
1000
1
0.1
10
100
100Gbit/s
Blu-ray Disc
  With 100 Gbit/s, data sizes of up to a DVD (4.7 GBytes) are downloaded within 0.5 sec.
Maximum file sizes allowed in 0.5-sec download
Video: Busy toll-gates in the train station
e.g., “http://youtu.be/_r5rjvjquzY”

## Slide 14
Rate | Download time for DVD data (4.7 GBytes) | Modulation | No. of frequency channels | MIMO
4.5 Gbit/s | 8.4 sec | 16QAM | 1 | - (SISO)
6.8 Gbit/s | 5.5 sec | 64QAM | 1 | 
27 Gbit/s | 1.4 sec | 64QAM | 4 | 
100 Gbit/s | 0.4 sec | 16QAM | 2 | 16x16
 |  | 64QAM | 1 | 
Transmission rates over 60-GHz band
IEEE802.11ad OFDM PHY
MCS#17: 2.1 Gbit/s (QPSK, Code rate=3/4)
MCS#21: 4.5 G bit/s(16QAM,Code rate=13/16)
MCS#24: 6.8 G bit/s (64QAM,Code rate=13/16)
100 Gbit/s rates are attainable using MIMO
・
・
・
・
・
・
TX
RX
#1
#2
#M
#1
#2
#M
Line-of-sight
environment
Short-Range MIMO (SR-MIMO)

## Slide 15
100 Gbit/s performance estimation
d
d= 4.1 mm
D = 10 mm
Electromagnetic simulation model of transmission channel [1]
Tx array
Rx array
OFDM transmission simulation
Parameter | Value
Frequency channel | Ch2 (fc=60.48 GHz), Ch3 (fc=62.64 GHz)
No. of branches | 16 x 16
Transmission distance | D = 10 mm
Element spacing | d = 4.1 mm = 0.82 λ0 (Optimized for this transmission distance)
MIMO detection | Zero Forcing (ZF)
No. of data subcarriers | 336
Subcarrier spacing | 5.15625 MHz
Modulation | QPSK, 16QAM, 64QAM
Frequency channels
66 GHz
57 GHz
Ch1
Ch2
Ch3
Ch4
60.48
62.64
Microstrip antenna
23mm

## Slide 16
  Over 100 Gbit/s is attainable with 16x16 MIMO using small (23 mm x 23 mm) antenna arrays that can be installed on portable devices.
100 Gbit/s performance estimation
Frequency channels in 60-GHz band
Ch1
Ch2
Ch3
Ch4
60.48
62.64
[GHz]
Modulation | No. of frequency channels | Transmission rate
QPSK | 1 | 33 Gbit/s
 | 2 | 67 Gbit/s
16QAM | 1 | 72 Gbit/s
 | 2 | 144 Gbit/s
64QAM | 1 | 108 Gbit/s
 | 2 | 216 Gbit/s
Transmission rates with each modulation
16 x 16 MIMO
Simulated bit error rate (BER)

## Slide 17
Chart: Number of elements M
| 1 | 4 | 9 | 16 | 25
素子数特性 | 16.0075 | 56.0794 | 115.8111 | 192.5984 | 284.4601
Calculation conditions
Transmission distance: D=1 mm
Element spacing: d = 2.5 mm
16x16 MIMO
193bit/s/Hz
9x9 MIMO
115 bit/s/Hz
25x25 MIMO
284 bit/s/Hz
Capacity enhancement with SR-MIMO
With short-range MIMO transmission, channel capacity is almost in proportion to the number of MIMO branches.
Further capacity is expected.

## Slide 18: SR-MIMO Channel Measurement (with 25-GHz scale model)
Rx array
Tx array
Rx#1
Rx#2
Tx#1
Tx#2
2.0 λ0
d
Rx array
Tx array
Frequency: 24.0GHz - 26.0GHz (The scale model of 2-ch bonding of 60-GHz; Its relative bandwidth is the same as that in 60-GHz.)
Element spacing: d = 0.500 λ0, 0.750 λ0, 1.000 λ0, 1.125 λ0, 1.250 λ0, 1.500 λ0 (λ0 is the wavelength, 12.0mm)
Transmission distance: D = 2.00 λ0
Antenna element: Square microstrip antenna (Gain = 5.5 dBi, Beamwidth 74.8°at 25.0 GHz)
Measurement setups
Notes: Short-range MIMO channel was measured using network analyzer.
Frequency was 25-GHz band as the scale model of 60-GHz band.
Bandwidth is 8 percent, as the scale model of two frequency channels of 802.11ad band.
smoothing 6 %
averaging 128 times

## Slide 19: SR-MIMO Channel Measurement (with 25-GHz scale model)
Modem simulation using the measured SR-MIMO channel shown in the previous page clarified the BER of the short-range MIMO.
Simulation setups
Modulation：OFDM（QPSK，16QAM，64QAM）
Subcarrier spacing：2.13MHz
No. of subcarriers：355
Center frequency: 24.6 GHz (Ch1) and 25.4 GHz (Ch2)
Chart: SNR [dB]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
QPSK | 0.1791 | 0.15101 | 0.12131 | 0.094064 | 0.069 | 0.048113 | 0.03093 | 0.017972 | 0.009641 | 0.00438 | 0.001806 | 0.0005455 | 0.000106 | 3.15e-05 | 3.5e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0.30514 | 0.27973 | 0.25426 | 0.22678 | 0.20257 | 0.17834 | 0.15448 | 0.13173 | 0.10914 | 0.088564 | 0.068653 | 0.051591 | 0.035292 | 0.02313 | 0.013652 | 0.0072025 | 0.0034665 | 0.001257 | 0.0004365 | 7.2e-05 | 2.65e-05 | 5.5e-06 | 2e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0.37136 | 0.35348 | 0.33592 | 0.31594 | 0.29525 | 0.27479 | 0.25196 | 0.22956 | 0.20664 | 0.1853 | 0.16381 | 0.14398 | 0.12384 | 0.10707 | 0.088962 | 0.073043 | 0.057479 | 0.042325 | 0.030629 | 0.020181 | 0.012236 | 0.006667 | 0.0033 | 0.0012805 | 0.0005115 | 0.0001515 | 2.95e-05 | 1e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SNR required for BER < 10-3
BER curve (d = 1.000 λ0)
Optimum element spacing is d = 1.000 λ0
Notes: Scale model of
QPSK: 2.1 Gbit/s * 2channels * 2branches = 8.4 Gbit/s
16QAM: 4.5 Gbit/s * 2channels * 2branches = 18 Gbit/s
64 QAM: 6.8 Gbit/s * 2channels * 2branches = 27.2 Gbit/s
Actual bitrate
QPSK: 2.1 Gbit/s * 2channels * 2branches *25/60 = 3.5Gbit/s

## Slide 20: Summary of 100 G bit/s over 60-GHz band using short-range MIMO
Channel capacities of over 100 Gbit/s are attainable using MIMO at 60-GHz band
With 100 Gbit/s, data sizes of up to a DVD (4.7 GBytes) are downloaded within 0.5 sec.
  → “Real touch-and-get” will be realized.

## Slide 21: References
[1]Hiraga, K.; Seki, T.; Nishimori, K.; Nishikawa, K.; Uehara, K., "Ultra-high-speed transmission over millimeter-wave using microstrip antenna array," Radio and Wireless Symposium (RWS), 2010 IEEE , vol., no., pp.673,676, 10-14 Jan. 2010.

## Slide 22: Backup

## Slide 23: Regulation will be Changed
EIRP
  47dB antenna with 10mW output power. Low gain antenna was not assumed. It will be changed keeping same EIRP.
Channel Bonding
  Now, channel band width was less than 2.15GHz. It is not arrowed Channel bonding. It will be changed.
Certifications formulation
  More easy process to have certification

## Slide 24
Public kiosks with downloadable movies, such as at an airport, are a great way.
to make movies available to users with portable devices
• At multi-gigabit download speeds, a user can download an uncompressed, HD movie in one minute, or on the way to an airport gate before boarding.
• The kiosk can support multiple simultaneous transfers, which means even less time waiting in line.

## Slide 25
Concept of short-range MIMO (SR-MIMO)
・
・
・
・
・
・
TX
RX
#1
#2
#M
#1
#2
#M
Multipath-rich
environment
・
・
・
・
・
・
TX
RX
#1
#2
#M
#1
#2
#M
Line-of-sight
environment
(a) General MIMO
(b) SR-MIMO
Low spatial correlation is achieved without multipath propagation
because path length differences is exploited

## Slide 26: Further advantage of SR-MIMO
We have clarified that the channel capacity obtained by zero forcing (ZF) at the receiver which does not use beam forming at the transmitter and channel state feedback is almost the same as that using eigenmode transmission when the element spacing is optimized.[1]
Hence transceiver’s transmission signal processing cost for MIMO detection will be reduced compared with eigenmode transmission.

## Slide 27: SR-MIMO Channel Measurement (with 25-GHz scale model)
Measured frequency response (d = 1.000 λ0)
Chart: Frequency [GHz]
Chart: Frequency [GHz]
Ch1
Ch2
Ch1
Ch2

## Slide 28: Frequency of scale model measurement
Scale model
at 25-GHz band
25.0GHz
24.561GHz
25.439GHz
2-ch bonding
Actual 60-GHz band