## Slide 1: Scalable Location
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Peter Thornycroft | Aruba Networks |  | 
Mark Rison | Samsung |  | 

## Slide 2: Location in High Density Environments
  We are seeing that contextual/support applications involve continuous location determination
  The Fine Timing Measurement protocol is a powerful protocol that will address such use cases in most environments.
  Yet, when people congregate in stadia and similar environments, the overheads multiply hundreds of times
  The Fine Timing Measurement protocol is a unicast protocol, and adds a minimum of 6 PPDUs per client per AP per immediate location fix
    FTM Request/Ack: 124us
    Initial FTM/Ack: 132us
    FTM/Ack: 128 us
    So 384 us is the minimum per exchange; if 1000 clients in range of an AP seek 0.5Hz updates, then this consumes 19% of the medium time on that AP’s channel … uncomfortably high
    If there are N co-channel APs, then the overhead on that channel gets N-fold worse (N╳19%)
  A more scalable protocol for dense environments is preferred
    More GPS-like (infrastructure broadcasts only)
Notes: FTMR: Assume 80MHz, 29.3 Mbps, preamble as 20+8+4+4+4=40us; payload as (28+3+11)*8/29.3 bytes (12us); so 52 us.
Ack: Assume duplicated 20MHz, 6Mbps, preamble as 20us; payload as 14*8/6Mbps (20 us); so 40 us.
FTMR+SIFS+Ack+SIFS = 52+16+40+16 = 124us
Initial FTM: Assume 80MHz, 29.3 Mbps, preamble as 20+8+4+4+4=40us; payload as (28+20+11)*8/29.3 bytes (20us); so 60 us.
Ack: 40 us.
FTMR+SIFS+Ack+SIFS = 60+16+40+16 = 132us
FTM: Assume 80MHz, 29.3 Mbps, preamble as 20+8+4+4+4=40us; payload as (28+20)*8/29.3 bytes (16us); so 56 us.
Ack: 40 us.
FTMR+SIFS+Ack+SIFS = 56+16+40+16 = 128us
See also:
  * 11-12-1249-04-000m-802-11-2012-cid-46-47-48 by Carlos Aldena et-al.
  * 11-13-0072-01-000m-client-positioning-using-timing-measurements-between-access-points by Erik Lindskog, Naveen Kakani et-al.