## Slide 1: Integrated Long Range Mode
Date: 2015-05-13
Author:

## Slide 2: Longer Range in 2.4 GHz band
Develop new MCS or PHY Mode for longer range
  Integrated in air interface: Able to operate concurrently with existing network without adverse effect on existing devices
  Integrated into mainstream devices: Does not require additional hardware and components for implementation.
  More than a “firmware upgrade” for existing products
Use Cases
  Connected devices (IoT, energy management, sensors)
    Fixed location
    Out of way location (hot water heater, pool pump)
    Poor propagation – e.g. side of White Goods appliance
  Indoor and outdoor applications
  Applications focused on M2M and IoT - not bulk data transfer
  General User – maybe for marginal connection conditions, rate not important

## Slide 3: Why is this needed when we have 802.11ah?
Additional band support has some incremental cost
  RF components, antennas, etc.
  This Long Range mode involves only coding and MAC changes
This capability is intended for standard, broad-market implementations
  Would operate on existing network, on standard APs and routers
  Energy and M2M desire to leverage existing customer broadband
Although targeting 2.4 GHz, mode should be band-agnostic
  Could be used with S1G PHYs as well
Objective: mode would eventually become available on all mainstream consumer and enterprise WLAN devices
  Ideally every AP would support this capability in "next generation" silicon

## Slide 4: PHY Support for LR mode
Name | Clause | Supported
High Throughput (HT) PHY | 20 | Yes
Directional multi-gigabit (DMG) PHY | 21 | No
Very High Throughput (VHT) PHY | 22 | No
Television Very High Throughput (TVHT) | 23 | Yes
Sub 1 GHz (S1G) PHY | 24 | Yes
High Efficiency (HE) PHY | -- | Yes 
changes to be compatible with HE PHY changes in 2.4 GHz band

## Slide 5: Functionality Summary
Longer range, lower rate.
  Primarily implemented by coding
Operates in “basic” channel size (20 MHz in 2.4 GHz)
  Take advantage of wider if available: E.G. Duplicate Mode
Applicable to both 2.4 GHz band and 915 MHz band
  In theory 5 GHz too, but likely less applicability (not DMG)
Possible to define “LR only” STA with ability to be implemented a lower cost: similar to S1G sensor STA

## Slide 6: Mitigation of Impact on Network
Low rates take a disproportionate time on air
  Overall network throughput can be significantly reduced
  First demonstrated in transition from 802.11b to 802.11g
Specify Medium Occupancy Limit for Low Rate
  Comparable to full rate packets
  Additionally, a maximum average time on air (duty cycle).
Intended applications are focused on M2M and IoT
  Not bulk data transfer, relatively low duty cycle
  Low aggregate data volume, could be low rate but doesn’t have to be

## Slide 7: Open Issues
How can the existing functions in the VHT PHY family be “reconfigured” to optimize for range rather than rate?
What types of coding are best suited for these applications and use cases?
  High coding gain? Redundancy in time or frequency?
  Hybrid ARQ? Interleaving across time (packets)?
  Changes to PHY header?
  While maintaining backward compatibility….
How to support operation in mixed BSS environments (LR and Legacy) ?
  New basic rates?
  Protection mechanisms?

## Slide 8: Summary
Longer Range operation
  Primarily in 2.4 GHz band, but not exclusively
Integrated with mainstream networks
  Backward compatible & interoperable in mixed BSS case
Integrated with mainstream products
  Negligible incremental cost for implementation
Intended for M2M – managed impact on existing network.
  Medium Occupancy Limit, average occupancy limit
  Other mechanisms as appropriate

## Slide 9: Straw Poll
Would you support the formation of a Study Group to develop a PAR for Long Range mode intended for broad-market 802.11 products?