## Slide 1: Low-Power Wake-Up Receiver (LP-WUR) for 802.11
Date: 2015-11-10
Authors:

## Slide 2: Abstract
This presentation introduces a low-power wake-up receiver (LP-WUR) design that enables low power consumption and low latency for 802.11.

## Slide 3: Problem: Escaping the Duty-Cycle Trap
With duty-cycled operation, low power consumption and low latency are conflicting goals
  To increase battery life, a device needs to sleep more  increased latency
  To receive data with low latency, a device needs to sleep less  shorter battery life
Low latency
(but short battery life)
Long battery life
(but long latency)
Sleep less
Sleep more
Goal
latency
battery
life

## Slide 4: Problem: Internet-of-Things (IoT) Use Case
Today without LP-WUR
  User cannot access the IoT device while the IoT device is off to save power
IoT device
Access Point
Access Point
Configuration change command
(e.g. collect data every 10 min)
Internet
User
command
Waits until IoT device wakes up
(worst case = 1 hour)
OFF
(wakes up every 1 hour)
ON

## Slide 5: Solution: Low-Power Wake-Up Receiver (LP-WUR) as Companion Radio for 802.11
Comm. Subsystem = Main radio (802.11) + LP-WUR
  Main radio (802.11): for user data transmission and reception
    Main radio is off unless there is something to transmit
    LP-WUR wakes up the main radio when there is a packet to receive
    User data is transmitted and received by the main radio
  LP-WUR: not for user data; serves as a simple “wake-up” receiver for the main radio
    LP-WUR is a simple receiver (doesn’t have a transmitter)
    Active while the main radio is off
    Target power consumption < 100 µW in the active state
      Simple modulation scheme such as On-Off-Keying (OOK)
      Narrow bandwidth (e.g. < 5 MHz)
    Target transmission range: LP-WUR = Today’s 802.11

## Slide 6: Design and Operation of LP-WUR
802.11
802.11
802.11
802.11
LP-WUR
ON
Wake-up Packet
Data
Packet
Wake-up signal
Transmitter
+
Payload modulated with On-Off Keying (OOK)
Payload = [Wakeup preamble | MAC header (Receiver address) | Frame body | FCS]
OOK modulation can be done using OFDM transmitter with modification (OFDM: orthogonal frequency division multiplexing; FCS: frame check sequence)
802.11 preamble for coexistence
Use L-SIG to protect the packet
This is for 3rd party legacy stations
This is not decoded by LP-WUR
(L-SIG: legacy SIGNAL field)
Extremely low power receiver design (< 100 uW)
- Small and simple OOK demodulator
Receiver
Transmission range
802.11 = LP-WUR
ON
OFF
ON
OFF
Wake-up Packet
or
802.11

## Slide 7: IoT Use Case
Proposed scheme using LP-WUR
  User can access the IoT device with low latency and the IoT device can have long battery life
IoT Device
Access Point
Access Point
Configuration change command
(e.g. collect data every 10 min)
Internet
User
command
Wake-up Packet
OFF
ON
(wakes up every 1 hour)

## Slide 8: LP-WUR Designs from University and Industry
References:
CICC [2007] : N. Pletcher, S. Gambini, and J. Rabaey, “A 65μW, 1.9 GHz RF to Digital Baseband Wakeup Receiver for Wireless Sensor Nodes,” IEEE Custom Integration Circuits Conference (CICC), 2007.
ISSCC [2008]: N. Pletcher, S. Gambini, and J. Rabaey, “A 2 GHz 52 μW Wake-Up Receiver with -72 dBm Sensitivity Using Uncertain-IF Architecture,” IEEE International Solid-State Circuits Conference, 2008.
VLSI [2014]: T. Abe, and et. al., “An Ultra-Low-Power 2-step Wake-Up Receiver for IEEE 802.15.4g Wireless Sensor Networks”, Symposium on VLSI Circuits Digest of Technical Papers,” 2014.
JSSC[2014]: X. Huang, and et. al., “A 780-950 MHz, 64-146 μW Power-Scalable Synchronized-Switching OOK Receiver for Wireless Event-Driven Applications,” IEEE Journal of Solid-State Circuits, Vol.49, No.5, May 2014.
Publications | Frequency (GHz) | Modulation | Power (µW) | Sensitivity (dBm) | Rate (kbps) | Tech CMOS (nm) | Active area (mm2)
CICC [2007] – UC Berkeley | 1.9 | OOK | 65 | -50 | 40 | 90 | 0.16
ISSCC [2008] – UC Berkeley | 2 | OOK | 52 | -72 | 100 | 90 | 0.1
VLSI[2014] – Panasonic | 0.925 | OOK/FSK* | 45.5 | -87 | 50 | 65 | 1.27
JSSC[2014] - IMEC | 0.78-0.915 | OOK | 123 | -86 | 10 | 90 | 1.27
*) FSK: frequency-shift keying

## Slide 9: Usage Model 1: Quick Message/Incoming Call Notification Scenario
(1) Without LP-WUR
or
Sleep/wake periodically
Internet
message
AP buffers data until the client wakes up
Main radio needs to wake up periodically to receive a notification within a latency requirement
or
message
802.11
(2) With LP-WUR
Internet
message
message
Wake-up packet
+
or
Sleep until wake-up packet is received
Wake-up upon reception of wake-up packet and receive message
802.11+LP-WUR

## Slide 10: Usage Model 2: Quick Status Query/Report, Configuration Change Scenario
(1) Without LP-WUR
(2) With LP-WUR
AP
Sleep/wake periodically
Internet
Status query command
Status query command
IOT device
802.11
AP buffers data until the IOT device wakes up
Configuration change command
or
IOT device
802.11+LP-WUR
AP
Sleep
Internet
Wake-up packet
Status query command
Status query command
+
Status report
Configuration change command
or

## Slide 11: Comparisons: Legacy 802.11 Power Save Modes versus LP-WUR
Scenario: data packet interval > polling interval (=latency requirement)
Legacy 802.11 power save modes
Proposed LP-WUR
(U-APSD: unscheduled automatic power save delivery)
2mS
Notes: (1) PS-Poll: STA wakes up periodically to receive beacon frames to see if there is data to receive
(2) U-APSD: STA wakes up periodically and transmits a trigger frame to see if there is data to receive
(3) Target Wake Time (TWT): AP/STA schedules a next target wake time during the current packet exchange
(4) Proposed LP-WUR: doesn’t need to receive beacons nor transmit triggering frames nor schedule TWT
(5) Proposed LP-WUR with scheduling: consumes even less power by waking up at scheduled times (e.g. TWT)

## Slide 12: TGax Power Consumption Model
Doc. 11-14/1444r2 [C. Yu, MediaTek]
Doc. 11-15/1100r2 [C. Ghosh, Intel]

## Slide 13: Comparison Using TGax Power Consumption Model
Latency requirement: 100mS
LP-WUR always on
LP-WUR duty-cycled
(2 mS active every 100 mS)
~224x
7 µW
105 µW
1.6 mW
~15x
Legacy power save modes
Parameters | Values
Wake-up packet length | 500 µS
LP-WUR power consumption in active state | 100 µW
LP-WUR active time duration | 2 mS
Channel access delay | 1.5 mS
802.11 PHY rate (data/control) | 6.5 Mbps
Data packet size | 238 bytes
Beacon/polling interval | 100 mS

## Slide 14: Comparison Summary
LP-WUR shows significant power saving over legacy power save modes
  Power saving gain : 7x (@5sec latency)~224x (@100mS latency)
LP-WUR enables a long battery life and low latency with a small battery

## Slide 15: Overview of LP-WUR for 802.11
[LP-WUR receiver design]
Small and simple OOK demodulator – only decodes OOK modulated payload
Active power consumption < 100 uW
Meet 802.11 receiver performance requirements: e.g. minimum sensitivity = -82dBm (MCS0), PER<=10%
[Wake-up packet design]
(1) Designed to coexist with 802.11
(2) Simple modulation scheme (OOK) for low power receiver design
(3) New packet format design
[Wake-up packet transmitter]
(1) Transmit a wake-up packet

## Slide 16: Comparison between LP-WUR and LRLP
 | LP-WUR | LRLP (long-range low-power)
User data transmission and reception | LP-WUR wakes up the 802.11 radio when it receives a wake-up packet User data is transmitted and received by the 802.11 radio | User data is transmitted and received by a new LRLP PHY/MAC
Metrics | Average power consumption Latency | Data transmission rate Peak/average power consumption Transmission range

## Slide 17: Summary
Today’s 802.11 makes trade-offs between low power consumption and low latency
The proposed LP-WUR technique can enable low power consumption and low latency at the same time
  A simple modulation scheme such as OOK can enable a low power receiver design
  Our study shows significant gain can be achieved using LP-WUR over legacy 802.11 power save modes

## Slide 18: Straw Poll
Do you support the basic concept of the LP-WUR technique in this presentation for standardization in the 802.11WG?
  Y: 65
  N: 1
  A: 51