## Slide 1: 11ax derived functional requirements
Date: 2016-04-03
Authors:

## Slide 2: Abstract
In this presentation we describe new functional requirements for positioning protocols that are derived from the 11ax protocol.

## Slide 3: Why 11ax functional requirements?
11ax presents new medium allocation methods including OFDMA and UL-MU-MIMO which are substantially different than these of 11ac.
  These allows for better spectral efficiency as medium is shared by multiple STAs during data transfer.
  For location should be in par with this requirement. Thus, multiple STAs should be able to perform positioning measurements concurrently, reducing the medium overhead.
11ax protocol is defined for dense environment with scheduling and little time remaining for SU operation.

## Slide 4: An example of an HE MU Tx OP

## Slide 5: Functional Requirements
The location protocol shall support positioning measurement of unassociated and associated STAs in the HE MU mode.
The 11az amendment shall have a mode supporting concurrent positioning measurements of multiple STAs, in both associated and unassociated states in the HE MU mode.
The 11az amendment shall have a mode supporting concurrent measurement from several transmit chains of an AP in HE operation mode. The same requirement shall also apply to VHT operation mode.
The 11az amendment shall have a mode supporrting concurrent measurement from several transmit chains of each non-AP STA in the HE operation mode. The same requirement shall also apply to the VHT operation mode.
The 11az amendment shall have a mode enabling positioning measurements on all supported channel bandwidths.

## Slide 6: Straw Poll
Do you support adding the functional requirements in Slide 5 of this presentation to the functional requirements document.
Yes/No/Abstain