## Slide 1: Issue of Congested Primary Channel in 802.11 WLAN
Date: 2017-01-16
Authors:

## Slide 2: Abstract
This presentation:
  raises an issue of current IEEE 802.11 wireless LAN when the primary channel is congested,
  shows a possible way to overcome this issue.

## Slide 3: Background
IEEE 802.11 wireless LAN has been widely and densely deployed, and now it needs to provide enough QoS to various kinds of applications such as huge-size file transfer and real-time application.
On the other hand, heavy congestion may occur due to interference from OBSS and/or other wireless system such as non-802.11 system and LAA in future in some frequency bands.
Amount of arrival interference will vary dynamically and instantaneously.

## Slide 4: Issue of current IEEE 802.11 wireless LAN on congested primary channel
A BSS sets one primary channel on which each STA invokes the backoff procedure to transmit its data [1].
If the primary channel is congested, the STA hardly transmits its data even if other channels are vacant [2].
A BSS can change its primary channel by using the procedure of DFS or FST in several TBTTs, however it is not agile so as to provide enough QoS, especially for real-time data traffic.
ch a
ch b
ch c
ch d
ch e
ch f
busy
idle
idle
idle
idle
idle
primary channel
Any STA cannot transmit its data if the primary channel is busy.
…
…

## Slide 5: To overcome this issue
One or some vacant channels may continuously or temporarily exist in the same frequency band with the primary channel or in another frequency band.
This issue on the congested primary channel would be overcome if a STA can quickly obtain enough transmission opportunity from such vacant channels.
ch a
ch b
ch c
ch d
ch e
ch f
busy
idle
idle
idle
idle
idle
primary channel
…
…
QoS will be improved if transmission opportunity can be obtain from other channel.

## Slide 6: Summary
In IEEE 802.11 wireless LAN, a BSS sets one primary channel on which each STA invokes the back-off procedure
If the primary channel is congested, the STA hardly transmits its data even if other channels are vacant.
This issue would be overcome if a STA could quickly obtain enough transmission opportunity from such a vacant channel.

## Slide 7: Straw Poll
Do you think that IEEE 802.11 wireless LAN should have a way to overcome the situation that the primary channel is heavily congested?
  Y:
  N:
  A:

## Slide 8: References
[1] IEEE 802.11-2012.
[2] doc. IEEE 802.11-14/1473r1.