## Slide 1: Orchestrator pilot signal
Date: 2017-07-11
Authors:

## Slide 2: Abstract
Proposal of a new Orchestrator pilot signal mechanism that improves the efficiency of spectrum sharing among 802.11 devices in unlicensed band.

## Slide 3: Problem statement
Current sharing mechanism on un-licensed band not efficient
Energy detection
Different RAT use different approaches of energy detection to assess if the media is available
Consumes in-band capacity (i.e.: waiting time to detect & response time to react)
Common Data Base for (secondary) spectrum usage
11af provides access to data base (i.e.: grant access to a given band)
11af does not coordinate spectrum usage (per transmission) among secondary users
We will see a multiplicity of upcoming unlicensed shared spectrum (large amount of potential frequencies to operate on)

## Slide 4: What we want
Reduce the consumption of in-band spectrum resources for arbitration.
Reduce the waiting and reaction times.
Reduce the time to find
potential communication partners on different channels
channels available to operate in
Escape the 5G prisoner’s dilemma
Provide a WiFi-specific, optional mechanism for improved and controlled channel usage
While not competing with 3GPP approaches
Autonomous operation is the still the key of IEEE 802.11

## Slide 5: Potential solutions
Use existing mechanisms on “dedicated coordination channels” to optimize WiFi behavior
  Enhanced neighbor reports
  Optimized, dynamic adjustments of contention window or energy detection
Common pilot signal for arbitration
This proposal focuses on this aspect as one potential solution

## Slide 6: Propose to create new arbitration mechanism
  Create new arbitration mechanism by using common pilot signal
    in dedicated spectrum or
    In a dedicated channel
  Dedicated frequency shall be allocated to every single system that is an entity of sharing spectrum.
  The pilot signal is transmitted by every single system by using common PHY modulation.
  The pilot signal contains the information improving the arbitration to avoid conflicts of the in-band signal such as,
    Geographical location of station
    Transmit power
    Required D/U
    Time interval of transmitting
    Etc,.
  Every single system controls their transmission timing and power by using information received by the pilot signal
  Try to be as much as possible technology-agnostic
Wi-Fi
xxx
DSRC
xxx

## Slide 7: Two potential approaches for Orchestration
Use in-band spectrum
Very narrow band signal
Transmitted in channel gaps
Avoiding interference with active channels
Use of dedicated channels
In-band channel
Out-of-band (new) channel
Why not try to get this from our DSRC friends?
Pilot Signal
Pilot channel

## Slide 8: DSRC candidate spectrum that can be use for the pilot signal
5MHz ch in 5.9GHz is “Reserved” for harmonization with potential extension of the UNII band
IEEE 1609 might have an interest to proactively discuss this approach to ensure in the long-term the spectrum and channel assignment is kept intact

## Slide 9: Q & A

## Slide 10: Straw Poll (1)
Would you like to receive more information on use of a common signal for orchestration?
  Result:
  Yes: 33 /
  No: 1 /
  Abstain: 48

## Slide 11: Straw Poll (2)
Should IEEE 1609 be approached to discuss the potential of using the existing, reserved “harmonization channel” for arbitration / orchestration of 802.11 devices?
Yes:
No:

## Slide 12: Straw Poll (3)
Would you like to receive more information on how to use the in-band pilot signal for orchestration?
  Result: Yes: 35 / No: 0

## Slide 13: Straw Poll (last)
Should further discussion of this topic occur
Within a (new) Study Group with the goal of creating a PAR
Within WNG
A: xxx
B: xxx