## Slide 1: Wi-Fi Time Sensitive Networking
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Evgeny Khorov | NRU HSE; IITP RAS |  |  | khorov@frtk.ru

## Slide 2: Motivation
On Tutorial session, Wi-Fi as a 5G technology was discussed
5G requirements include not only throughput, but also delay
For low latency communications, delay should not exceed 1ms
Applications
Gaming
Wireless Remote Control
Robotics
V2X
The aim of this presentation is to discuss how we can meet delay requirements with 802.11

## Slide 3: IEEE 802.1 Activities
Published Standards for Time-Sensitive Networking:
IEEE Std 802.1Qbu-2016 - IEEE Standard for Local and Metropolitan Area Networks -- Bridges and Bridged Networks -- Amendment 26: Frame Preemption. It allows a Bridge Port to suspend the transmission of non time critical frames while one or more time critical frames are transmitted.
IEEE Std 802.1Qbv-2015 - IEEE Standard for Local and Metropolitan Area Networks -- Bridges and Bridged Networks -- Amendment 25: Enhancements for Scheduled Traffic. It specifies time aware queue draining to schedule the transmission of frames relative to a known time scale.
IEEE Std 802.1Qca-2015 - IEEE Standard for Local and Metropolitan Area Networks -- Bridges and Bridged Networks -- Amendment 24: Path Control and Reservation. It extends the application of Intermediate System to Intermediate System (IS-IS) to bridged networks in order to provide explicit trees for data traffic.
They are being rolled into 802.1Q by the ongoing P802.1Q-REV project.

## Slide 4: What makes Wi-Fi not Time Sensitive
Packet Delay = Queueing Delay + Packet Transmission Time
A TSN packet shall wait while at least the head-of-line packet is being transmitted
Maximal PPDU duration in 11ax exceeds 5 ms
Packet Transmission Time includes channel access time and PPDU duration (plus retries, if any)
Because of unlicensed spectrum, the channel may be busy with transmission of other devices

## Slide 5: Reducing Queueing Delay
Main idea: Stop transmitting a non-TSN frame when a TSN frame arrives.
This is similar to IEEE Std 802.1Qbu-2016
A STA can easily stop its own frame, but how to stop other frame transmissions

## Slide 6: Reducing Packet Transmission Time
Main idea: reduce channel access time using another radio, adaptively choose robust MCS and protect transmission from collisions

## Slide 7: Reducing Channel Access Time
Main idea: use dual radio, similarly to WUR (802.11ba)
The main radio is used for usual transmission.
The auxiliary radio is used to ask neighboring STAs to stop ongoing non-TSN transmissions.
Radios operate in different bands
The auxiliary radio cannot be used for data transmission.
It can be combined with WUR or extend WUR idea.
It can be also used to wake-up the intended receiver from microsleep or doze state.

## Slide 8: Simple Example of WTSN Handshake
Backoff
STA2 Receives TSN Notification and stops its transmission
TSN Frame arrives in the queue
STA1
TSN Notification
TSN Frame
STA2
Ongoing Transmission
Cancelled Transmission
AIFS
Sent with auxiliary radio
AP
ACK

## Slide 9: Open Issues
Shall the transmission of the non-TSN frame be considered as unsuccessful transmission attempt?
How to save partially transmitted data?
How can the receiver of the TSN frame microsleep during non-TSN transmissions for other STAs?

## Slide 10: Straw Poll
Is the problem of Time Sensitive Networking with 802.11 interesting to you?
Yes
No
Abstain