## Slide 1: EXtreme Throughput (XT) 802.11
Date: 2018-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Laurent Cariou | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-712-5560 | laurent.cariou@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Xiaogang Chen |  |  |  | Xiaogang.chen@intel.com
Po-Kai Huang |  |  |  | Po-kai.huang@intel.com
Yusuke Tanaka | Sony |  |  | Yusuke.YT.tanaka@sony.com
William Carney |  |  |  | William.carney@sony.com
Yuichi Morioka |  |  |  | Yuichi.morioka@sony.com
Sigurd Schelstraete | Quantenna |  |  | sschelstraete@quantenna.com
Huizhao Wang | Quantenna |  |  | hwang@quantenna.com
Chuck Lukaszewski | HPE |  |  | chuck.lukaszewski@hpe.com
Eldad Perahia |  |  |  | Eldad.perahia@hpe.com
Minyoung Park | Samsung |  |  | Minyoung.p@samsung.com
Tianyu Wu |  |  |  | tianyu.wu@samsung.com
Wook Bong Lee |  |  |  | wookbong.lee@samsung.com

## Slide 2
Name | Affiliation | Address | Phone | Email
Stephane Baron | Canon |  |  | Stephane.baron@crf.canon.fr
Patrice Nezou |  |  |  | Patrice.nezou@crf.canon.fr
Pascal Viger |  |  |  | Pascal.viger@crf.canon.fr
Sean Coffey | Realtek |  |  | coffey@realtek.com
VK Jones | Qualcomm |  |  | vkjones@qti.qualcomm.com
Rolf De Vegt |  |  |  | rolfv@qti.qualcomm.com
Hemanth Sampath |  |  |  | hsampath@qti.qualcomm.com
Sameer Vermani |  |  |  | svverman@qti.qualcomm.com
Tian Bin |  |  |  | btian@qti.qualcomm.com
Yasuhiko Inoue | NTT |  |  | Inoue.yasuhiko@lab.ntt.co.jp

## Slide 3: Key messages
It is time to start a new study group for next generation Wi-Fi, following 802.11ax
The objective of this group should be focused on increasing peak throughput and capacity
Laurent Cariou, Intel
Slide 3

## Slide 4: Content
Rational for the proposed scope/objectives for next generation Wi-Fi
Prioritized technical solutions to meet the objectives
Laurent Cariou, Intel
Slide 4

## Slide 5: Defining the objectives for next generation Wi-Fi
How to define the objectives:
  Evaluate what low complexity technical solutions are exploitable
  Evaluate what objectives will benefit the large majority of market segments targeted by Wi-Fi
Historically, all PHY generations were focused on peak throughput and capacity.
  For 802.11ax, low complexity solutions were not exploitable for peak throughput increase, so we moved to a more elaborated objective: improve efficiency for multi-user operations and dense environments
We’ll show in the following slides that the conditions are now ripe for defining the objectives for next generation Wi-Fi as:
  EXtreme Throughput (XT) Wi-Fi to provide
  Significant (at least 4x) peak throughput and capacity increase over 11ax
Laurent Cariou, Intel
Slide 5

## Slide 6: New unlicensed spectrum at 6GHz as the enabler for throughput increase
Throughput increase at 2.4 and 5GHz require more and more complex solutions
But more than 1GHz of additional unlicensed spectrum may be available around 2020 timeframe
  802.11ax will be the first technology to be deployed at 6GHz, XT 802.11 will follow
  Most APs and STAs will soon become tri-band devices supporting 2.4/5/6GHz
This new spectrum enables peak throughput and capacity improvements for next generation:
  Exploiting multi-band and larger spectrum
Laurent Cariou, Intel
Slide 6

## Slide 7: 6 GHz band (US)
Laurent Cariou, Intel
Slide 7
Exclude 6975-7025
CC, OFS (7025-7125)
Extended C-band FSS Uplink
C-band FSS Uplink + ESV (5925-6425)
CC, OFS (6525-6975)
CC, OFS (5925-6425)
Local Television Transmission Service (LTTS) (5925-6525)
Fixed
BAS
television broadcast auxiliary service stations (BAS)
cable television relay service stations (CARS)
CARS
C-band Uplink Planned Band (6725-7025)
Federal (7125-7250)
BAS (6875-7125 MHz)
CARS (6875-7125 MHz)
Part 15
Ultra Wideband; Level Probing Radars (5925-7250)
LTTS
Excl. Mobile
3
11
19
35
91
99
115
131
139
163
179
7
23
71
87
167
109
105
101
97
93
89
85
81
77
73
69
65
129
125
121
117
113
29
25
21
17
13
9
5
1
147
103
79
51
59
75
83
39
55
47
5935
MHz
6095
MHz
6255
MHz
6415
MHz
61
57
53
49
45
41
37
33
183
111
187
195
133
137
141
6575
MHz
6735
MHz
15
143
175
211
227
423
419
153
149
145
177
173
169
165
161
215
435
431
439
181
185
189
219
157
6895
MHz
7055
MHz
207
427
119
151
135
199
27
43
67
107
123
155
171
203
7215
MHz
193
197
201
205
217
213
209
241
237
233
229
225
245
249
253
221
Potential WLAN Plan?
XM-Sirius Feeder Uplink 7025-7075
OFS
Private Operational Fixed Point to Point Microwave
186
BAS (6875-7125 MHz)
FSS DL Limited to NGSO Feeder Links for MSS (6700-7075)
Passive Sensor (Measurements over Ocean) (6425-7075)
Passive Sensor (7075-7250)
RAS (6650-6675.2)
Radio Astronomy Service
SRS UL (7145-7235)
TT&C UL (7125-7155)
UNII-5
UNII-6
UNII-7
UNII-8

## Slide 8: High level objectives for EXtreme Throughput XT 802.11
Similarly to 11ac, focus on a very limited set of main innovations for 2.4/5/6GHz and on some simplifications from previous standard
1 – Throughput increase
    Larger BW (320MHz)
    Multi-band aggregation (multi-channel/multi-band)
    16 spatial streams
2 – Tuning 11ax MU features based on experience from the field for all bands
Laurent Cariou, Intel
Slide 8

## Slide 9: Larger Bandwidth
Getting Higher bandwidth is the most straightforward solution:
  Demonstrate higher peak throughput
    Or increase capacity that can be shared among multiple users thanks to 11ax MU features
320MHz bandwidth already doubles the throughput
  Likely to have multiple 320MHz available at 6GHz or across 5 and 6GHz
Laurent Cariou, Intel
Slide 9

## Slide 10: Benefiting from devices being multi-band
HE and XT devices will be multi-band devices (non-concurrent/single radio or concurrent/multi-radio)
Efficiency benefits can be achieved in revisiting the management of operation over multiple bands
  Load balancing, traffic steering…
Further peak throughput increase can be achieved by enabling
  Multi-band aggregation (at layer 1 and/or layer 2)
    More chances to get 320MHz bandwidth
    Or ability to get even higher bandwidth
Laurent Cariou, Intel
Slide 10

## Slide 11: 16 spatial streams
Increasing number of spatial streams from 8 to 16 allows 2x peak throughput or capacity increase
  The benefits are expected to be more important in a multi-user scenario
Laurent Cariou, Intel
Slide 11

## Slide 12: Structure/procedure changes in 802.11 for main PHY projects
Our objective is to get to a 2 year cadence on major PHY amendment releases from 802.11, to map product roadmaps, and to better respect their release dates.
At high level, the concept would be:
  Define fixed dates for each release
  Task group focuses on the spec development for the current release on a limited list of features to meet the release date
    What is not mature is pushed to next release
  After some time, work in parallel on scope for next release
One objective of the study group will be to define the procedure changes that are required to enable this:
  Multiple releases within a single task group … or one release per task group, with a seamless task group creation for the following release? … Multiple SFDs? ...
The list of features proposed in the deck are for the first release
Release 2021 spec development
Release 2023 spec development
Release 2023 scope decision
Release 2025 scope decision
Time
Release 2021 Drafts
Laurent Cariou, Intel
Slide 12

## Slide 13: Conclusion
It is time to start a new study group for next generation Wi-Fi, following 802.11ax
The objective of this group should be focused on increase peak throughput and capacity
We propose a limited set of features to further focus the group
Laurent Cariou, Intel
Slide 13

## Slide 14: Straw Poll
Do you agree to start a study group to define XT 802.11 with the objective to increase 802.11 peak throughput on bands between 1 and 7.125 GHz with the following key features: 320MHz bandwidth, enhanced multiband operation and 16 spatial streams?
Laurent Cariou, Intel
Slide 14