## Slide 1
Inconsistent STA range and channel support indications
Date: 2021-12-07
January 2022
Andersdotter, Muir, Sky UK Group
Authors:
Name | Affiliation | Phone number | E-mail address
Amelia Andersdotter | Sky UK Group | +46764266862 | Amelia.andersdotter@sky.uk
Sean Muir | Sky UK Group | +447809419789 | sean.muir@sky.uk
Notes: doc.: IEEE 802.11-21/1540r0
September 2021
Stephen McCann, Huawei
Page <nummer>

## Slide 2
Abstract
This presentation covers differences between STAs in their indication of operating channel ranges and the consequences this might have for network operators when determining how to ensure consistent quality of service by means of efficient spectrum management.
January 2022
Andersdotter, Muir, Sky UK Group
Notes: doc.: IEEE 802.11-21/1540r0
September 2021
Stephen McCann, Huawei
Page <nummer>

## Slide 3
STA Range parameters
When a STA connects to a network, it may or may not indicate on which channels it is capable of operating.
Even when STA indicates the channels on which it is capable of operating, these indications are not consistent.
The lack of consistent indications among STA makes it difficult for network operators to adequately steer STA to the best connection point by making use of the appropriate channels available
In the following slides, we will present some examples from residential settings where this can create a degradation in connection quality for consumers.
Andersdotter, Muir, Sky UK Group
January 2022

## Slide 4
Example
DFS:
  AP undertakes CAC on Channel 100
  CAC determines channel is clear
  CSA packets sent by AP to connected non AP-STA’s
    60% of the 5GHz non AP-STA’s have no channel 100 support and join the 2.4GHz radio.
Andersdotter, Muir, Sky UK Group
January 2022

## Slide 5
January 2022
Andersdotter, Muir, Sky UK Group
Ideal Outcome
Reality
2.4GHz
5GHz
6GHz
Example

## Slide 6
January 2022
Andersdotter, Muir, Sky UK Group
Inconsistency of wlan.supchan first and range

## Slide 7
Suggestions for moving forward
Users of .11 technologies would benefit from standardised indications of ranges and channels.
The ideal outcome is predictability both for the AP and for non-AP STAs when a network is being set up.
January 2022
Michael Montemurro, Huawei
Andersdotter, Muir, Sky UK Group

## Slide 8
Questions? Comments?
Andersdotter, Muir, Sky UK Group
January 2022