## Slide 1: Looking ahead to next generation: follow-up
Date: 2022-02-28
Authors:

## Slide 2: Background (1)
In the January WNG meeting, we initiated a discussion for next generation beyond 802.11be together with other individuals [1][2][3][4]
  Provide high level requirements for next generation
  Propose to form a TIG/SG for next generation in 2022
 | 22/0030r1[1] | 22/0032r0[2] | 22/0046r1[3] | 22/0059r0 [4]
Requirements | Hundred gigabit throughput (new spectrum requirement) Low latency improvement Full Wi-Fi coverage (including roaming and mesh) Intelligent/Capable of Machine Learning | Throughput (>2x 11be) Latency (< 1 ms, possibly < 0.1 ms) System efficiency Power consumption Better 6GHz spectrum usage | Increased throughput (10Gbps on client with 2 SS, requiring new spectrum) Deterministic operation and reduced latency (better than 0.1ms) Improved mobility Improved coordination of P2P traffic | Increase reliability of Wi-Fi connectivity Reduce latency for critical applications Enhance manageability of Wi-Fi networks Reduce device level power consumption Enhance device roaming Experience Improve performance in spectrum congested environments

## Slide 3: Background (2)
An observation during the discussion in the January WNG meeting is about the lack of new spectrum (e.g., 6 GHz) in some geographic markets.
Mmwave was proposed to be taken into account together with sub 7 GHz in [1] [3] so that one device can operate on more bands, which to some extent is aligned with [4] on the spectrum related issue.

## Slide 4: Background (3)
Another observation from the discussion is the possible use cases for beyond 11be, which is the focus of this contribution.
In this contribution, we focus on two possible areas from our previous submission [1]:
  Use cases that would benefit from AI
  Latency related use cases

## Slide 5: Use cases that would benefit from AI (1)
As discussed in [1], our Wi-Fi community is currently developing and deploying many new exciting technologies (e.g., multi-user transmission, multi-link operation) that, on the other hand, increases the complexity.
Dependencies between the system parameters and their joint optimization usually have a non-linear impact on network performance. Many of these non-linear impacts cannot be easily modeled and optimized without ML (machine learning).

## Slide 6: Use cases that would benefit from AI (2)
Taking the channel access as an example, the intrinsic random deferment feature of CSMA/CA
  makes it upper-bounded by a relative low MAC efficiency [5]
  suffers from fairness and latency issues in many realistic scenarios

## Slide 7: Use cases that would benefit from AI (3)
AI is also getting attention in other SDOs, for example, 3GPP [6]
Delay insensitive use cases | Delay sensitive use cases
Multi-RAT (including mobility, load balancing, RAT selection, PCI selection ,etc) | Massive MIMO beamforming optimization (flexible and configurable beam pattern)
QoS based resource optimization (at RAN level to fulfill SLS) | Channel estimation and channel modelling
QoE optimization | Link adaptation
Traffic steering (guide carrier/band/access preference at per-UE or group of UE granularity) | Beam selection (quick beam selection based on location, etc.)
Long-term traffic forecasting and classification – can be used in multiple cases, such as flow control, RACH, load balance, etc | Massive MIMO MAC scheduling (user selection and resource allocation)
BS and UE energy optimization | CSI compression
IAB topology adaption (congestion and RLF prediction, load balance, etc) | MIMO detection
Flow control (traffic and UE access prediction) | 
Handover | 
Positioning | 
RRM resource ICIC | 

## Slide 8: Use cases that would benefit from AI (4)
The following areas that would benefit from AI are identified for next generation beyond 11be:
Delay insensitive use cases | Delay sensitive use cases
Enhanced roaming/mobility | Distributed channel access
Multi-RU/channel allocation (preamble puncture, channel bonding, channel assignment) | Channel estimation
Latency/QoS optimization | Link adaptation
Traffic prediction | Beam management
Device level power consumption | MU-MIMO MAC scheduling (user selection and resource allocation)
Spatial reuse | CSI compression and feedback
 | MIMO detection

## Slide 9: AI-enabled use cases (1)
Use case 1: Channel Access [7]
  Justification: Reduce access delay and jitter to further improve channel efficiency
  Input: historical carrier sensing results, historical transmission results, the time duration since last successful transmission, PER, etc.
  Output: channel access decision (e.g., whether to transmit PPDU or not, PPDU length)
  Potential ML algorithm: supervised learning, reinforcement learning (like Q learning)
Use case 2: User selection for MU-MIMO scheduling [8]
  Justification: reduce complexity (considering correlation and interference between users) in real-time user selection
  Input: historical channel matrix, throughput, reported CQI, QoS traffic statistics (latency, packet loss rate), etc.
  Output: predicted MCS, spatial streams to certain non-AP STA
  Potential ML algorithm: reinforcement learning

## Slide 10: AI-enabled use cases (2)
Use case 3: Roaming [9]
  Justification: transition delay for roaming in an enterprise network scenario
  Input: BSS transition parameters (e.g., transition threshold), whether previous transition is successful or not, occurrence of ping-pong after a successful transition, transition failure rate
  Output: transition decision, new transition parameters (e.g., transition threshold)
  Potential ML algorithms: supervised learning, reinforcement learning
Use case 4: Traffic Steering [10]
  Justification: Load balancing among multi-link and QoS (latency, reliability) enhancement
  Input: measurement reports (CQI/BSRP), BSS load statistics, QoS traffic performance statistics (latency, packet loss rate), etc.
  Output: link transition, enable or disable some links.
  Potential ML algorithm: supervised learning, reinforcement learning

## Slide 11: Latency related use cases
As discussed in [1], the Wi-Fi community needs further optimization on latency because of the many delay-sensitive emerging applications and the increasing deployment of smart IoT, e.g., at home and in factories.

## Slide 12: Latency related use cases in industrial Wi-Fi
Level 1-Non-Real Time: >10ms@99.999%
Level 2-Real Time: [2ms,10ms]@99.9999%
Level 3-Isochronous Real Time: <1ms @99.9999%
high-end terminals
Production line PLC (level-1 control)
Robot PLC (Level 2 Control)
Servo Driver/Motor
Gripper/Soldering Gun I/O
Industrial PLC control logic ：
Level 1
Level 1/2
Level 2
Level 3
PLC density: 30 sets/100 square meters
Besides the interaction among different video screens as mentioned in [1], there are other latency related use cases, such as an industrial network as shown on the right.
Now NR is going to be widely deployed in these scenarios.
However, there still exists a gap between latency requirements with high reliability and the existing Wi-Fi performance.

## Slide 13: Conclusion
While continuing pursuing high throughput and low latency for Wi-Fi, like adding mmwave to multi-link framework, it is also important to make Wi-Fi intelligent
In this contribution, a few AI-enabled use cases and low latency use cases in Wi-Fi are provided.

## Slide 14: References
[1] 11-22-0030-01-0wng-look-ahead-to-next-generation
[2] 11-22-0032-00-0wng-next-gen-after-11be
[3] 11-22-0046-01-0wng-next-generation-after-802-11be
[4] 11-22-0059-00-0wng-beyond-be
[5] Giuseppe Bianchi, Performance analysis of the IEEE 802.11 distributed coordination function, 2000
[6] https://www.3gpp.org/ftp/TSG_RAN/WG3_Iu/TSGR3_110-e/Docs/R3-206403.zip
[7] Yiding Yu, Soung Chang Liew and Taotao Wang, Non-Uniform Time-Step Deep Q-Network for Carrier-Sense Multiple Access in Heterogeneous Wireless Networks, IEEE TRANSACTIONS ON MOBILE COMPUTING, VOL. 20, NO. 9, SEPTEMBER 2021
[8] Raja Karmakar, Samiran Chattopadhyay and Sandip Chakraborty, Intelligent MU-MIMO User Selection With Dynamic Link Adaptation in IEEE 802.11ax, IEEE TRANSACTIONS ON WIRELESS COMMUNICATIONS, VOL. 18, NO. 2, FEBRUARY 2019
[9] Ismail AlQerm and Jianli Pan, I-HARF: Intelligent and Hierarchical Framework for Adaptive Resource Facilitation in Edge-IoT Systems, IEEE Internet of Things Journal, 2022 Feb 16.
[10] Cezary Adamczyk and Adrian Kliks, Reinforcement Learning Algorithm for Traffic Steering in Heterogeneous Network, 17th International Conference on Wireless and Mobile Computing, Networking and Communications (WiMob) 2021 Oct 11 (pp. 86-89).