## Slide 1: Thoughts on Next Gen WLAN
Date: 2022-05-10
Authors:

## Slide 2
Abstract
In this contribution we propose some potential requirements and technologies for the next generation of 802.11 PHY/MAC specifications as well as share some thoughts on the specification process.

## Slide 3: Introduction
  A number of contributions have been discussed in WNG regarding the next generation of major PHY/MAC revisions of the 802.11 spec [1][2][3][4][5]
  Some common requirements are:
    Improved latency (< 1ms [2], <0.1ms [3])
    Improved throughput (>100 Gbps [1], > 2x 11be [2], 10 Gbps [3])
    Improved mobility and coverage [1][3][4]
  In this contribution, we share our views on some of the requirements and thoughts on potential technologies that may meet these requirements

## Slide 4: QoS Improvement (1)
Need for low latency
  The need for low latency has been discussed frequently regarding the next gen of WLAN
  Use cases such as AR/VR/XR, industrial control and IoT may push the low latency requirements to 0.5 ms in 2025 for beyond 6G [6]
Low latency support requires overall QoS improvement
  Low latency traffic inherently requires high reliability
    Reliability requirement may surpass 99.999999% in 2025 [6]
  High reliability will be required by other use cases, such as industrial IoT
QoS improvement needs multi-faceted solutions which may include:
  Network efficiency improvement
  Reliability improvement
  Overhead reduction
  Machine Learning (ML) optimization

## Slide 5: QoS Improvement (2)
Network efficiency improvement
  11ax and 11be have improved network efficiency significantly:
    Multi-User, Multi-link protocols
    Spatial reuse
  Further efficiency improvement may be achieved by:
    Multi-AP/Multi-MLD coordination, e.g.:
      Coordinated transmission: OFDMA, beamforming, joint transmission
      Coordinated multi-link
      Coordinated spatial reuse
Reliability improvement
  Restriction of traffic rather than prioritization of high priority traffic
  Better usage of 6GHz
  Hybrid ARQ
    /

## Slide 6: QoS Improvement (3)
Overhead reduction
  PHY Design improvement: e.g., preamble design
  16 SS requires significant training overhead
    Better sounding protocols and PPDU designs to reduce overhead
  More efficient UL traffic indication
Use Machine Learning (ML) for optimization
  Channel access, traffic steering
  Low latency traffic/general traffic pattern prediction
  MAC/PHY design to support ML algorithms at TX and/or Rx

## Slide 7: Per link Throughput Improvement
Demand for higher throughput is ever growing
  High resolution video related applications requires higher and higher peak throughput
    AR/VR/XR, 4K/8K video streaming, etc.
Studies predict that in 2025, throughput requirement could reach 1 Gbps per user for beyond 5G and 2 Gbps per user in 2030 [6]; peak throughput will depend on the number of users in a given coverage area
  Total peak throughput will depend on the use cases developed for Next Gen WLAN
In order to be competitive, Next Gen WLAN should target similar peak throughput
Some potential technologies that may meet such demand:
  16 spatial streams
  Hybrid ARQ
  Even wider bandwidth in 6GHz
  Full-duplex radio

## Slide 8: Better Integration of various 802.11 amendments
WLAN systems are used to support a larger variety of services and devices
  802.11ba provides power saving using Wake Up Radios
  802.11bf is drafting specifications for wireless sensing
It would be desirable to have the same AP/MLD to provide multiple functionalities concurrently to meet diverse demands
  Next Gen WLAN can provide better integration of various services, such as protocol designs and PHY designs

## Slide 9: Thoughts on Specification Process
Long term project planning
  Next Gen planning should be continuous and may want to look beyond one generation
Clearly defined features in PAR or at the beginning of TG
  More deliberation and consensus on a fixed set of features in the beginning may save time in the long run and create a focused project
Considerations for phased releases
  Next Gen SG/TG should have a discussion whether phased releases will be suitable
More deliberation on achievable timeline
  We suggest that the SG spends sufficient time to define an achievable timeline for the agreed feature set for each project/release

## Slide 10: Conclusions
In this contribution, we share our thoughts on requirements and potential technologies for Next Gen WLAN
  QoS improvement
    Low latency and high reliability, which may require multi-facet solutions
  Per link throughput improvement
  Better integration of various 802.11 amendments
  Next Gen project management: a focused PAR with an agreed fixed set of features and an achievable timeline

## Slide 11
References
[1] 11-22/0030, Look ahead to next generation
[2] 11-22/0032, Next Gen After 11be
[3] 11-22/0046, Next Generation After 802.11be
[4] 11-22/0059, Beyond ‘be’
[5] 11-22/458, Looking ahead to next generation: follow up
[6] Towards 6G: Evolution of Key Performance Indicators and Technology Trends, 2nd 6G Wireless Summit, March 2020