## Slide 1: Next Gen After 11be: Main Directions Proposal
Date: 2022-05-10
Authors:

## Slide 2: Abstract
Main Directions Proposal for the Next Generation PHY/MAC Task Group

## Slide 3: High Level Approach and Potential Next Gen Targets
We prefer a focused and unified approach to improve usage of the newly received 6GHz spectrum along with 5GHz and 2.4GHz spectrum
In our view spectrum below 7GHz provides the best way to achieve reliable communication with high data rate, especially in NLOS conditions common in indoor/outdoor environments
Higher spectral efficiency/throughput
  Approach 1Gbps throughput over target area
    House, apartment buildings, office, venues, ..
Significantly more efficient channel access
  Results in better usage of wider bandwidths
Higher reliability
Better coverage
Lower latency

## Slide 4: Main Use Cases Envisioned
AR/VR
Video Distribution
Fast data transfers
Gaming
Automation
Automotive
Robotics
Medical
  Surgical Applications
Backhaul
Social Media

## Slide 5: Features From 11be That May be Reconsidered for Next Gen
Multi-AP
  Frequency/Time coordination
  Coordinated SR
  BF and nulling
  JT
Secondary channel access protocol
  Important for wider BWs
TB Punctured PPDU
A-PPDU (aggregate OFDMA PPDU, 11be/next gen aggregation)
Lower CSI feedback
BA Modification
Improved link adaptation
  Fast feedback
  Added MCS for denser grid
  Multi-layer Transmission
Note: HARQ seems too complex for gains seen (improved link adaptation may be a better choice)

## Slide 6: New Feature: BW Expansion in 5GHz Band
Expand to 240MHz BW in UNII2
5490
MHz
5895
MHz
5735
MHz

## Slide 7: New Feature: BW Expansion in 6GHz Band
802.11be Channelization
  320 MHz channelization is defined
    Partially overlapping 320 channels to maximize utility
Expand to 480MHz channels – e.g. 4 channels, two for 320-1 set and two for 320-2 set
Expand to 640MHz channels
  Two non-overlapping 560MHz channels
  Two 640MHz channels with 160MHz overlap

## Slide 8: New Features: Bandwidth Expansion Summary of Rates
Wider bandwidths (along with STR and MU-MIMO option)
  240 MHz in 5GHz band
  480 MHz in 6GHz band
  640 MHz in 6GHz band
 | 5GHz (Gbps) | 6GHz (Gbps) |  |  | Total SU-MIMO (MLO STR) 5GH+6GHz (Gbps) |  |  | Total MU-MIMO (3 users, x3) (MLO STR) 5GH+6GHz (Gbps) |  |  | 
Nss (per user) | 240MHz | 320MHz | 480MHz | 640MHz | 240MHz+320MHz | 240MHz+480MHz | 240MHz+640MHz | Total Nss/ Total # AP antennas | 240MHz+ 320MHz | 240MHz+480MHz | 240MHz+ 640MHz
2 | 4.4 | 5.8 | 8.7 | 11.6 | 10.2 | 13.1 | 16 | 6/8 | 30.6 | 39.3 | 48
3 | 6.5 | 8.7 | 13.1 | 17.4 | 15.2 | 19.6 | 23.9 | 9/12 | 45.6 | 58.8 | 71.7
4 | 8.8 | 11.6 | 17.4 | 23.2 | 20.4 | 26.2 | 32 | 12/16 | 61.2 | 78.6 | 96

## Slide 9: Secondary Channel Utilization
Very important in order to utilize wider bandwidths
Currently Wi-Fi greatly suffers because of artificial channel access rules applied for 20MHz channels 20+ years ago
  Wider BW transmission can be utilized only if primary channels are free
  Incredible waste of efficiency
  Should have been already addressed during 11ac standard development
Allow transmissions on secondary channels when primary channels are occupied
Crucial for 160MHz and larger bandwidths, even for 80MHz
https://mentor.ieee.org/802.11/dcn/20/11-20-0363-03-00be-proposals-on-unused-bandwidth-utilizations.pptx
  Already specified by the ETSI harmonized standard for 5 GHz (EN 301 893)
  Expected to be copied into the ETSI rules for 6GHz
  Already supported by LAA and NR-U

## Slide 10: Benefits Matrix of Potential Wi-Fi 8 Features
 | Gain | Peak Throughput | System Throughput | Latency | Range/ Higher Rate at Range | Higher Reliability
Multi-AP | multiplicative | YES (for JT) | YES | YES | YES | YES
Secondary channel access | multiplicative |  | YES | YES |  | YES
Wider bandwidths | multiplicative | YES | YES | YES | YES | 
TB Punctured PPDU | efficiency |  | YES | YES |  | 
A-PPDU | efficiency |  | YES | YES |  | 
Multi-layer transmission | additive |  | YES | YES |  | YES
Lower CSI feedback | efficiency |  | YES | YES |  | 
BA modification | efficiency coexistence |  | YES |  |  | YES
Enhanced long range | improved performance |  |  |  | YES | YES

## Slide 11: Next Gen: Possible Feature Set for Consideration - Summary
Core:
  Meaningful subset of Multi-AP features
  Secondary channel access
  Wider bandwidth
Subset of the following features:
  TB Punctured PPDU
  A-PPDU (aggregate OFDMA PPDU, 11be/next gen aggregation)
  Lower CSI feedback
  BA Modification
  Improved link adaptation
    Fast feedback
    Added MCS for denser grid
    Multi-layer Transmission
Other:
  Enhanced long range
  TBD (SG/TG will for sure come up with quite a few other compelling ideas)