## Slide 1: Cloud VR Use Case and Requirements
Date: 2022-07-08
Authors:
Name | Affiliation | Address | Phone | Email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Wei Lin |  |  |  | 
Mengyao Ma |  |  |  | 
Ming Gan |  |  |  | 
David Xun Yang |  |  |  | 
Edward Au |  |  |  | 
Stephen McCann |  |  |  | 

## Slide 2: Cloud VR
Cloud VR is a new cloud computing technology for VR services. With fast and stable transport networks, VR content is stored and rendered in the cloud, and video and audio outputs are coded, compressed, and transmitted to user terminals [1].
Cloud VR B2C Application Scenario | Cloud VR B2B Application Scenario
Cloud VR IMAX | Cloud VR education
Cloud VR live broadcast | Cloud VR eSports arena
Cloud VR 360° video | Cloud VR marketing
Cloud VR gaming | Cloud VR healthcare
Cloud VR music | Cloud VR tourism
Cloud VR fitness | Cloud VR real estate
Cloud VR karaoke | Cloud VR engineering
Cloud social VR | 
Cloud VR shopping | 
Cloud VR service scenario overview

## Slide 3: Network Requirements of Cloud VR
Three characteristics and advantages of VR are immersion, interaction, and imagination (3I).
  Immersion: 3D images are generated by a computer to create a virtual environment that feels like the physical world.
  Interaction: People can use sensor devices to interact with each other in the virtual environments generated and feel like they are in the real world.
  Imagination: The virtual environment inspires the imagination of users.
Accordingly, the experience evaluation factors of VR include sense of reality, interaction, and pleasure.
[1]
Sense of reality
Sense of interaction
Sense of pleasure
Experience factor
Resolution
Frame rate
FOV
Color depth
Coding & compression
Initial buffer time
Motion sensory conflict
Operation latency
Stalling (time and duration percentage)
Artifacts (times and duration/area percentage)
Effective frame rate in gaming
Bandwidth
Delay
Packet loss
Service indicator
Network indicator

## Slide 4: Cloud VR Network Development Strategy
Before we look into details of the network requirements of cloud VR, let’s divide the cloud VR development into three phases:
  Fair-experience phase: Home WLAN networks are added, and 4K-ready bearer network expansion and upgrade are performed.
  Comfortable-experience phase: Home WLAN and bearer networks are upgraded to guarantee bandwidth and latency.
  Ideal-experience phase: Networks are evolving towards higher bandwidth and lower latency
Next we will discuss the cloud VR network requirement with regard to the three phases.

## Slide 5: Deterministic Low Latency Required by Cloud VR
For traditional 4K services, latency only slightly affects the channel switching time and loading duration. Therefore, the latency requirements for traditional 4K services are not demanding.
However, the latency must be deterministic for strong-interaction VR services, because images are remotely rendered in the cloud. Otherwise, the screen refresh quality and user interaction are compromised.
The following table provides recommended network latency levels for home WLAN, fixed access network, and metro network latency, according to the theoretical models and actual test results.
[1]
Phase | E2E Network RTT | Home WLAN | Fixed Access Network | Metro Network
Fair-experience Phase | ≤ 20 ms | ≤ 10 ms | ≤ 2 ms | ≤ 8 ms
Comfortable-experience Phase | ≤ 15 ms | ≤ 7 ms | ≤ 2 ms | ≤ 6 ms
Ideal-experience Phase | ≤ 8 ms | ≤ 5 ms | ≤ 2 ms | ≤ 1 ms

## Slide 6: Deterministic Low Latency Required by Cloud VR
Recommended E2E latency planning for strong-interaction VR services:
[1]
 | Cloud processing | Network Transmission | Terminal processing | 
Procedure | Content/GPU engine cloud Logic computing Content rendering Coding, and data transmission | Bearer network Home-Wi-Fi | Decoding & synchronization | Asynchronous time wrapping, anti-distortion and light-up of the screen
Delay planning (Fair/comfortable/ideal-experience phase) | ≤ 30 ms ≤ 25 ms ≤ 16 ms | ≤ 20 ms ≤ 15 ms ≤ 8ms | ≤ 20 ms ≤ 10 ms ≤ 6ms | ≤ 20 ms
Delay requirements (Fair/comfortable/ideal-experience phase) | Cloud rendering and streaming delay: ≤ 70 ms ≤50 ms ≤ 30 ms |  |  | MTP: ≤ 20 ms

## Slide 7: Bandwidth Requirements of Cloud VR
The immersive terminals of Cloud VR have a greater FOV than a traditional TV. To achieve the same definition as 4K video, the resolution, frame rate, and bitrate of Cloud VR must be higher than those of the 4K video services, posing higher bandwidth requirements on networks.
According to the actual tests and theoretical analysis, Cloud VR has the following bandwidth requirements:
[1]
Network KPI | 4K Video | Fair-experience Phase of VR (4K Panorama) | Comfortable-experience Phase of VR (8K Panorama) | Ideal-experience Phase of VR (12K/24K Panorama)
Bandwidth per service | ≥50 Mbit/s | ≥80 Mbit/s | ≥260 Mbit/s | ≥1 Gbit/s

## Slide 8: Bandwidth Requirements of Cloud VR
The estimated bandwidths required by VR video services in the three phases of Cloud VR development are as follows:
Phase |  | Fair-experience Phase | Comfortable-experience Phase | Ideal-experience Phase
Typical full-view resolution |  | 4K (3840*1920) | 8K (7680*3840) | 12K (11520*5760)/24K(23040*11520)
Typical terminal resolution |  | 2K | 4K | 8K
FOV |  | 90° to 110° | 120° | 120° to 140°
Color depth (bits) |  | 8 | 8 | 10~12
Coding standard |  | H.264/265 | H.265 | H.265/266
Frame rate |  | 30 | 30 | 60~120
Compression ratio |  | 133 | 230 | 410(12K), 1050(24K)
VR video service | Typical bitrate | 40 Mbit/s | Full-view: 90 Mbit/s FOV: 50 Mbit/s | Full-view: 290 Mbit/s (12K) 1090 Mbit/s(24K) FOV: 155 Mbit/s (12K) 580 Mbit/s(24K)
 | Typical bandwidth requirement | 60 Mbit/s | Full-view: 140 Mbit/s FOV: 75 Mbit/s | Full-view: 440 Mbit/s (12K) 1.6 Gbit/s(24K) FOV: 230 Mbit/s (12K) 870 Mbit/s(24K)
[1]

## Slide 9: Bandwidth Requirements of Cloud VR
The estimated per-user bandwidths required by strong-interaction services in the three phases of Cloud VR development are as follows:
Phase |  | Fair-experience Phase | Comfortable-experience Phase | Ideal-experience Phase
Typical content resolution |  | 2K (equivalent full-view resolution: 4K) | 4K (equivalent full-view resolution: 8K) | 8K/16K (equivalent full-view resolution: 12K/24K)
Typical terminal resolution |  | 2K | 4K | 8K/16K
FOV |  | 90° to 110° | 120° | 120° to 140°
Color depth (bits) |  | 8 | 8 | 10~12
Coding standard |  | H.264/265 | H.265 | H.265/266
Compression ratio (I-frame/P-frame) |  | 25/75 | 38/165 | 50/255(8K), 83/585 (16K)
Strong-interaction VR service | Typical bitrate | 40 Mbit/s | 90 Mbit/s | Full-view: 290 Mbit/s (12K) 1090 Mbit/s(24K) FOV: 155 Mbit/s (12K) 580 Mbit/s(24K)
 | Typical bandwidth requirement | 80 Mbit/s | 260 Mbit/s | 360 Mbit/s (8K) 1.5 Gbit/s (16K)
[1]

## Slide 10: Packet Loss Requirements of Cloud VR
The packet loss rate requirements of video on demand (VoD) services can be calculated as follows under given RTT and bandwidth:
For strong interaction and live video services, the recommended packet loss requirements are as follows:
[1]
Phase | Fair-experience Phase | Comfortable-experience Phase | Ideal-experience Phase
RTT | 20ms | 20ms | 20ms
Bandwidth | 60 Mbit/s | 140 Mbit/s | 440 Mbit/s
Packet loss rate | ≤ 9e-5 | ≤ 1.7e-5 | ≤ 1.7e-6
Phase | Fair-experience Phase | Comfortable-experience Phase | Ideal-experience Phase
Packet loss rate | ≤ 1e-5 | ≤ 1e-5 | ≤ 1e-6

## Slide 11: Network KPI Requirements Summary
[1]
Phase |  | Fair-experience Phase | Comfortable-experience Phase | Ideal-experience Phase
Video full-view resolution |  | 4K to 8K | 8K to 12K | 12K to 24K
Strong-interaction content resolution |  | 2K to 4K | 4K to 8K | 8K to 16K
FOV |  | 90° to 110° | 120° | 120° to 140°
Color depth (bits) |  | 8 | 8 | 10~12
Coding standard |  | H.264/265 | H.265 | H.265/266
Frame rate (FPS) |  | 30 (video services) 50-90 (strong interaction services) | 30 (video services) 90 (strong interaction services) | 60-120 (video services) 120-200 (strong interaction services)
VR video service | bitrate | ≥40 Mbit/s (4K) | Full-view: ≥90 Mbit/s FOV: ≥50 Mbit/s | Full-view: ≥290 Mbit/s (12K) ≥1090 Mbit/s(24K) FOV: ≥155 Mbit/s (12K) ≥580 Mbit/s(24K)
 | Bandwidth requirement | 60 Mbit/s (4K) | Full-view: ≥140 Mbit/s FOV: ≥75 Mbit/s | Full-view: ≥440 Mbit/s (12K) ≥1.6 Gbit/s(24K) FOV: ≥230 Mbit/s (12K) ≥870 Mbit/s(24K)
 | Recommended RTT level | ≤20ms | ≤20ms | ≤20ms
 | Packet loss requirement | ≤ 9e-5 | ≤ 1.7e-5 | ≤ 1.7e-6
Strong-interaction VR service | bitrate | ≥40 Mbit/s | ≥90 Mbit/s | ≥360 Mbit/s (8K) ≥440 Mbit/s(16K)
 | Bandwidth requirement | 80 Mbit/s | ≥260 Mbit/s | ≥1 Gbit/s (8K) ≥1.5 Gbit/s(16K)
 | Recommended RTT level | ≤20ms | ≤15ms | ≤8ms
 | Packet loss requirement | ≤ 1e-5 | ≤ 1e-5 | ≤ 1e-6

## Slide 12: Some enablers for Cloud VR Requirements
Retransmission heavily prolongs packet transmission latency. If the latency exceeds the device tolerance or the number of retransmission attempts exceeds the threshold, packet loss occurs.
When the actual channel condition is worse than the chosen code rates, the receiver can easily fail to decode the channel codeword, leading to a failure in source decoder and significant reduction in reconstructed video/image quality. Retransmission occupies the airtime, and thus also reduces the throughput/bandwidth of the cloud VR services.
Some enablers are needed to reduce the latency.

## Slide 13: QoS enhancement
Enable different QoS for different frame types (I/P frame) or different modalities (video, audio, emotion data, haptic data, sensor data etc.).
There are many works in 3GPP regarding how to standardize XR support since 2016 [2].
  Service and System Aspect (SA) working group (WG) on “Services” (SA WG1 or SA1) specified 5G service requirements for high-rate and low-latency XR applications [3].
  SA4 (“Multimedia Codecs, Systems and Services”) documented relevant traffic characteristics in [4] and provided a survey of XR applications in [5].
  SA2 (“System Architecture and Services”) standardized new 5G quality of service identifiers (5QI) to support interactive services including XR [6].
  RAN1 performed a R17 study on evaluating NR performance for the XR [7].
  The normative work now continues in both SA and RAN for Release 18 (first 5G-Advanced release, tentatively, until 2023) [11,12].
There are also related papers discussing how to improve XR/Video over WLAN [9, 10]  “XR/Video awareness WLAN”
Higher QoS can enable lower latency for more important (e.g., base layer) services.

## Slide 14: Unequal error protection (UEP)
In [13], multi-layer transmission under improved link adaptation is mentioned as a feature that can be considered for next generation.
Multi-layer transmission is one kind of unequal error protection at PHY layer that can provide different robustness to different services.
  The base layer is protected better with lower rate/MCS whilst the enhancement layer is protected with higher rate/MCS.
  May further do joint source and channel coding (JSCC) at PHY.
UEP can achieve a good tradeoff between data rate and robustness. It can further reduce transmission latency.

## Slide 15: Summary
Cloud VR use cases and its requirements are introduced for three different phases.
  Latency
  Bandwidth
  Packet loss
Some enablers for the cloud VR are briefly discussed.
  QoS enhancement
  Unequal error protection
The details need to be further discussed within the Study group period.

## Slide 16: Reference
[1] Cloud VR network solution white paper, iLab, Huawei, https://www.huawei.com/minisite/pdf/ilab/cloud_vr_network_solution_white_paper_en.pdf
[2] Extended Reality (XR) over 5G and 5G-Advanced NewRadio: Standardization, Applications, and Trends, Vitaly Petrov et. al.
[3] 3GPP, TS 22.261 “Service requirements for the 5G system,” v.18.5.0, Dec. 2021.
[4] 3GPP, TR 26.925 “Typical traffic characteristics of media services on
3GPP networks,” v.17.0.0, Sept. 2021.
[5] 3GPP, TR 26.928 “Extended Reality (XR) in 5G,” v.16.1.0, Dec. 2020.
[6] 3GPP, TS 23.501 “System architecture for the 5G System (5GS)”,
v.17.3.0, Dec. 2021.
[7] 3GPP, TR 38.838 “Study on XR (Extended Reality) evaluations for NR”, v.17.0.0, Jan. 2022.
[8] 11-22-0638-01-00be-consideration-on-the-tsn-capabilities-and-xr-applications-in-wi-fi

## Slide 17: Reference (cont’d)
[9] Toward an improvement of H.264 video transmission over IEEE 802.11e through a cross layer architecture
[10] Video over IEEE802.11 Wireless LAN: A Brief Survey
[11] SP-211610 New SID on Study on architecture enhancement for XR and media services
[12] RP-213587 XR Enhancements for NR
[13] 11-22/0734r0
[14] 11-22/0030r1