## Slide 1: Overview of 802.15.4ab
Date: 2022-07-12
Authors:
July 2022
Notes: September 2012

## Slide 2: Abstract
An overview of amendment 802.15.4ab:
Next Generation UWB
With a focus on the narrow band/UWB hybrid proposals and coexistence with other services
July 2022
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 2

## Slide 3
Task Group 15.4ab Next Generation UWB Amendment
to IEEE Std 802.15.4
Objective: enhancements to 802.15.4 Ultra Wideband (UWB) physical layers (PHYs) medium access control (MAC) and associated ranging techniques while retaining backward compatibility with enhanced ranging capable devices (ERDEVs).

## Slide 4: A Brief history of time…ok just 802.15.4 UWB
2006: IEEE 802.15.4 first published in 2003 and first revision in 2006
2007: IEEE 802.15.4a introduced UWB PHY and related MAC enhancements
  One impulse radio PHY, currently known as High Repetition Pulse (HRP)
  Adopted in a variety of applications
  Channel plans for 3.1 to 5 GHz and 6 to 10.3 GHz
  Moderately widely used in specialty applications requiring high precision ranging and real time location tracking including industrial, commercial and military applicaitons
2012: IEEE 802.15.4f introduced a new low pulse repetition (LRP) PHY
  Focused on RFID applications
  Channel plan for 6 to 8.5 GHz
  Widely used for tracking and location in manufacturing and other industries

## Slide 5: A Brief history of time…ok just 802.15.4 UWB
2020: IEEE 802.15.4z Enhanced UWB
  Enhanced both HRP and LRP PHYs
  HRP channel plan same as 802.15.4a
  LRP channel plan extended up to 10 GHz
  Widely deployed (billions) in consumer devices (smart phones), vehicle entry systems, location tracking and navigation applications of all kinds, and growing rapidly
  Included features to assure coexistence with legacy UWB
2021: Task Group 15.4ab created to address the next generation of UWB enhancements
  Building upon 15.4a, 15.4f, 15.4z
  Feedback from multiple industry groups using the standard
  Based on real world experience
  Further enhancing coexistence (with everything) is a project goal (priority)

## Slide 6: 5.2.b Scope of the project (As approved):
This amendment enhances the Ultra Wideband (UWB) physical layers (PHYs) medium access control (MAC), and associated ranging techniques while retaining backward compatibility with enhanced ranging capable devices (ERDEVs). Areas of enhancement include:
  additional coding, preamble and modulation schemes to additional coding, preamble and modulation schemes to support improved link budget and/or reduced air-time relative to IEEE Std 802.15.4 UWB;
  additional channels and operating frequencies;
  interference mitigation techniques to support greater device density and higher traffic use cases relative to the IEEE Std 802.15.4 UWB;
  improvements to accuracy, precision and reliability and interoperability for high-integrity ranging; schemes to reduce complexity and power consumption;
  definitions for tightly coupled hybrid operation with narrowband signaling to assist UWB;
  enhanced native discovery and connection setup mechanisms;
  sensing capabilities to support presence detection and environment mapping;
  and mechanisms supporting low-power low-latency streaming as well as high data-rate streaming allowing at least 50 Mb/s of throughput.
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols are in scope, as are infrastructure synchronization mechanisms. This amendment includes safeguards so that the high throughput data use cases do not cause significant disruption to low duty-cycle ranging use cases.
https://development.standards.ieee.org/myproject-web/app#viewpar/9081

## Slide 7: What is it
Amendment 4ab is a work in progress
Exiting 802.15.4 PHYs cover all sorts of bands
  UWB in 3.1 to 5, 6 to 10.6 (published in 2007)
  Narrow band PHYs (many) in sub 1GHz, 2.4 GHz and many other bands
  Already coexist in several bands with 802.11
What’s been proposed in a nutshell
  Coupling NB with UWB cooperatively
  Improved coexistence mechanisms
  New channel plans for existing PHYs to support the above
  Some enhancements to existing PHYs to improve coexistence

## Slide 8: 802.15.4 MAC
Simple and flexible MAC architecture
Optimized for lower duty cycle and activity factors
  Optimized to provide a lot of “gaps” (time domain)
Includes CSMA
  Multiple CSMA options
  Multiple CCA methods including Energy above Threshold (ED)
  Available for all PHYs
  NB PHYs under consideration typically will use CSMA
Considering CSMA enhancements under consideration specifically to improve coexistence with other services

## Slide 9: Channelization
Several options under discussion - This is a work in progress
Low data volumes and very low activity and duty factors
U-NII bands (upper 5 GHz) under consideration
  Upper 5 GHz U-NII attractive due to ability to share signal path with UWB at 6 GHz
  Generally better behavior than 2.4 GHz
Good coexistence with 802.11 is a primary goal
  The point is better reliability (less interference)

## Slide 10: List of references: NB technical contributions