## Slide 1: Thoughts on High Reliability Communications (for Next Gen WiFi)
Date: 2022-08-29
Authors:
Name | Affiliation | Address | Phone | Email
Aiguo Yan | Zeku | 2479 E Bayshore Rd, Palo Alto, CA 94303 |  | aiguo.yan@zeku.com
Yi-Hsiu Wang | Zeku |  |  | 
Xiaogang Chen | Zeku |  |  | 
Doc.: IEEE 802.11-22/1413r1
August 2022

## Slide 2: Agenda
Goal of This Presentation
Key Points from past WNG Presentation
Area 1 for Improvement (TXBF with SVD)
Area 2 for Improvement (TXBF Feedback Compression)
Area 3 for Improvement (TXBF with GMD)
Summary
Straw-Polls
August 2022
Doc.: IEEE 802.11-22/1413r1

## Slide 3: Goal of This Presentation
List some potential areas for improvement
Seek collective wisdom of 802.11 WLAN community on how to proceed.
Welcome questions, comments, suggestions, and information of historical efforts on these areas especially.
August 2022
Doc.: IEEE 802.11-22/1413r1
Notes: BW, Modulation Order, Power, Coding, ……….

## Slide 4: Key points from previous WNG meetings
Throughput/DataRate, and Latency are two KPIs emphasized by many presenters. [WNG01]
Another often emphasized point is Reliability, along with similar KPIs such as QoS, Robustness, Coverage and Efficiency.
One presentation [WNG02] specifically emphasized “practical” throughput improvements instead of theoretic throughput improvements on paper, in general popular usage scenarios instead of some rare usage scenarios.
UHR-SG is formed with emphasized on Reliability. One of requirements is also to “increase throughput including at different SNR levels” . [WNG03]
More resources (such as Higher TX power, wider channel BW, more antennas, more available spectrum … ) can always make a wireless system more reliable.
In addition to high cost with these approaches, resources may be unavailable and there are constraints to these resources (regulatory issues and physical size of a device)
Question: What could WiFi Community do to optimize existing technologies for improving reliability?
August 2022
Doc.: IEEE 802.11-22/1413r1
Notes: BW, Modulation Order, Coding, ……….

## Slide 5: Area 1: Existing Concerns with MIMO/TXBF
11ax-P579: It is recommended that the spatial mapping matrix applied to HE-STF and beyond be chosen such that it preserves the smoothness of the physical channel, achieved by limiting the variation of each element’s real and imaginary values in the spatial mapping matrix across successive tones within one RU
11beD1.5-P652: It is recommended that the spatial mapping matrix applied to EHT-STF and beyond is chosen such that it preserves the smoothness of the physical channel, achieved by limiting the variation of each element's real and imaginary values in the spatial mapping matrix across successive tones within one RU.
Many papers talking about preserving the smoothness [TXBF01 –05]
Call for actions: Could WiFi community define ways for AP/STA work together to better preserves and improve the smoothness of the BFed physical channel?
August 2022
Doc.: IEEE 802.11-22/1413r1
Notes: Well known issue since early days of 11n.
Not just preserve, but also improve?
In 2006, Authors of [TXBF01] presented concept of SSVD in WNG.
“11-06-0979-00-0wng-mimo-ofdm-beamforming.ppt”

## Slide 6: Area 2: TXBF feedback Overhead
With more 4K subcarriers (possible more in NextGen) and 8 TX antennas (possible more in NextGen), and potential multi-AP schemes in NextGen, amount of data to be fed-back is enormous in 802.11.
Many contributions emphasized importance of overhead reduction and proposed ways to reduce these overheads. But these ideas didn’t yet get into standards. [BFOR01]
Recently, CSI Feedback Overhead Reduction was proposed as the top use cases in July AIML TIG meeting. [BFOR02]
August 2022
Doc.: IEEE 802.11-22/1413r1

## Slide 7: A Subset of Existing Proposals on Overhead Reduction
August 2022
Doc.: IEEE 802.11-22/1413r1
 | Scheme | Pros | Cons
1 | ϕ only feedback | exists in 802.11ah | single data stream only
2 | time domain channel | exists in 802.11ad/ay | may need additional signaling to identify tap positions and the extra matrix
3 | Differential Givens Rotation | Simple improvement from 802.11ax, variant in 11ay | Additional processing, Error Propagation
4 | Variable Angle Quantization | simple improvement from 802.11ax | additional processing
5 | Multi-component Feedback | Well understood, reduced feedback overhead | May need additional design
6 | Codebook based Feedback | Well understood, reduced feedback overhead | May need additional design
7 | Two way channel training | Do not need calibration, reduced feedback overhead | May need additional design
8 | Implicit Feedback | Simple improvement from 802.11n | Needs calibration
The Table is from “11-19-0391-00-0eht-feedback-overhead-reduction-in-802-11be.pptx” (Komi Oteri and et al.)
Notes: There are more proposals in IEEE802.11 document server.

## Slide 8: Area 3: GMD based TXBF
SVD based TXBF was first introduced in 11n.
There are no much changes since then.
GMD (Geometric Mean Decomposition) based TXBF has been a hot topic in research community. [TXBF05]
Question: could the WiFi community conduct more research in this area and standardize the GMD based TXBF scheme, providing gain is significant and complexity increase is acceptable?
August 2022
Doc.: IEEE 802.11-22/1413r1
Notes: TX power allocation.

## Slide 9: Summary
Performance (such as Throughput, Latency, Reliability and etc.) of 802.11 WLAN can be improved from multiple directions.
802.11 WLAN is already using very high BW, very high modulation order, very advanced coding scheme.
Could we use both more advanced algorithms and additional functionalities supported by standard to further unlock the potential of MIMO technologies?
August 2022
Doc.: IEEE 802.11-22/1413r1

## Slide 10: SP #1 and #2
Are you willing to support enhancement of standard on SVD based TXBF if SNR gain is at least 1.0 dB?
Are you willing to support enhancement of standard on SVD based TXBF if SNR gain is around 2.5 dB?
Note:
Baseline: SVD based TXBF Performance without channel smoothing.
These SPs are for Information Collection only.
August 2022
Doc.: IEEE 802.11-22/1413r1
Notes: 1st step: without impairments (except AWGN and Channel Est)  Gain should be 2.5dB
Estimated degradation with all impairments and estimation: 0.5 dB since both existing and new simulations need these impairment mitigation.
2nd step: add all impairments.

## Slide 11: SP #3 and #4
Are you willing to support enhancement of standard for SVD TXBF feedback overhead reduction if the amount of data to be feedbacked is reduced to ½-th, with potential performance degradation <=0.25dB?
Are you willing to support enhancement of standard for SVD TXBF feedback overhead reduction if the amount of data to be feedbacked is reduced to 1/4-th, with potential performance degradation <=0.25dB?
Note:
Baseline: 11be feedback scheme
These SPs are for Information Collection only.
August 2022
Doc.: IEEE 802.11-22/1413r1

## Slide 12: SP #5 and #6
Are you willing to support enhancement of standard for GMD based TXBF if SNR gain is at least 1.0 dB?
Are you willing to support enhancement of standard for GMD based TXBF if SNR gain is around 2.5 dB?
Note:
Baseline: SVD based TXBF Performance.
These SPs are for Information Collection only.
August 2022
Doc.: IEEE 802.11-22/1413r1

## Slide 13: Selected References
WNG Presentations (WNG)
[WNG01]: All WNG presentations until Meeting of July 2022. (inclusive)
[WNG02]: 11-22-0418-00-0wng-considerations-of-next-generation-beyond-11be.pptx (Jianhan Liu and et al.).
[WNG03]: 11-22-0708-03-0wng-beyond-be-next-step.pptx (Rolf De Vegt and et al.)
Overhead Reduction Presentations (BFOR)
[BFOR01]: Key reference: 11-19-0391-00-0eht-feedback-overhead-reduction-in-802-11be.pptx (Kome Oteri and et al.)
[BFOR02]: 11-22-0950-02-aiml-discussion-on-interaction-between-ai-ml-wireless-lan.pptx (Zinan Lin and et al.)
IEEE Journal/Conference Papers on both Channels estimation smoothing and GMD [TXBF]
[TXBF01]: C. Shen and M. P. Fitz, "MIMO-OFDM Beamforming for Improved Channel Estimation," in IEEE Journal on Selected Areas in Communications, vol. 26, no. 6, pp. 948-959, August 2008, doi: 10.1109/JSAC.2008.080811.
[TXBF02]: W. Hu, F. Li and Y. Jiang, "Phase Rotations of SVD-Based Precoders in MIMO-OFDM for Improved Channel Estimation," in IEEE Wireless Communications Letters, vol. 10, no. 8, pp. 1805-1809, Aug. 2021, doi: 10.1109/LWC.2021.3081583.
[TXBF03]: E. Jeon, M. Ahn, S. Kim, W. B. Lee and J. Kim, "Joint Beamformer and Beamformee Design for Channel Smoothing in WLAN Systems," 2020 IEEE 92nd Vehicular Technology Conference (VTC2020-Fall), 2020, pp. 1-6, doi: 10.1109/VTC2020-Fall49728.2020.9348441.
[TXBF04] F. Jiang, Q. Li and X. Chen, "Channel Smoothing for 802.11ax Beamformed MIMO-OFDM," in IEEE Communications Letters, vol. 25, no. 10, pp. 3413-3417, Oct. 2021, doi: 10.1109/LCOMM.2021.3099167.
[TXBF05]: Yi Jiang, J. Li and W. W. Hager, "Joint transceiver design for MIMO communications using geometric mean decomposition," in IEEE Transactions on Signal Processing, vol. 53, no. 10, pp. 3791-3803, Oct. 2005, doi: 10.1109/TSP.2005.855398.
August 2022
Doc.: IEEE 802.11-22/1413r1
Notes: Wolf