## Slide 1: Roaming handoff time reduction to improve user experience
Date: 2022-xx-xx
Authors:

## Slide 2: Abstract
Introduction
Observation
Some suggestions
Conclusion

## Slide 3: Introduction
With the rise of mobile working, more and more latency-sensitive applications, such asvideo and voice conferencing, are widely used.
Although IEEE 802.11k/v/r have greatly reduce the BSS detection and authentication time during roaming; IEEE 802.11e QoS reduces the transmission latency of audio and video packets. However, up to now, the actual Wi-Fi roaming handoff process still makes users feel video and call interruptions.
Notes: Although these interruptions of application layer are closely related to cache, codec, traffic prediction algorithm; on the other hand, if Wi-Fi can further reduce the service interruption time of roaming handoff or provide a relatively reliable prediction of interruption time, it is believed that the user-level experience will be greatly improved.

## Slide 4: Introduction
The Wi-Fi Alliance provides “Voice-Enterprise” certification[2], aimed at voice over Wi-Fi application. The Latency threshold is below 50 ms.
The 《 Cloud AR/VR Whitepaper》[3] published by CSMA says:
The latency requirement for the overall end-to-end in VR is commonly targeted at 20 ms.
In AR the requirement is even stricter. Some sources identify the limit for a perfect AR experience at 5 ms.

## Slide 5: Observations
L2 layer roaming test
The test is performed in the roaming handoff system in the shield box. The actual service interruption time during roaming is tested by sending data packets at an interval of 10ms.
Roaming handoff time test environment
Notes: The roaming switch time was tested through the environment shown on the right.
The test is performed in the roaming handoff system in the shield box. The actual service interruption time during roaming is tested by sending data packets at an interval of 10ms.

## Slide 6: Observations
Stage | Time Phasing | Stage description | Average time consumption in each stage Unit: ms | Time consuming in stages Unit: ms
Pre-roaming | T0-T1 | STAs meet roaming threshold or receive bss transition management(BTM)request, and prepare to send probe request. | 3.5 | 47
 | T1-T2 | STAs get into PS status, change to different channels and send probe request | 25 | 
 | T2-T3 | STAs receive probe response or not, back to working channel , quit PS status and response to BTM | 5 | 
 | T3-T4 | STAs decide to roam, refresh state machine,prepare to get into PS mode | 1 | 
 | T4-T5 | In working channel, STAs get into PS mode In new channel, STAs send Auth request to a new AP | 12.5 | 
Roaming | T5-T6 | The new AP response to theAuth | 1 | 32.5(10.5)
 | T6-T7 | STAs send Reassoc Req | 5.5 | 
 | T7-T8 | AP reponses to the Reasso Rsp | 4 | 
 | T8-T9 | 4 way handshake of WPA2/PSK | 22 0 if 802.11r | 
Post-roaming | T9-T10 | STAs quit PS mode | 5 | 23
 | T10-T11 | STAs start to send /answer packets | 15 | 
 | T11-T12 | STAs complete to send the packets that buffer before roaming | 3 | 
The right table shows the average roaming data of some mobile terminals.The roaming process could be divided into three stages: pre-roaming, roaming and post-roaming.
In the test, we observed that packets loss or latency occurred in either stage during roaming handoff.
Roaming is triggered by BTM(11v)
Generally, the roaming time is 32.5ms, from Auth to 4WAY handshake
For 802.11r support terminals, it can be reduced to 10.5ms.
However, if these delay added:
1.packets that are cached in advance due to the cross-channel probe of the terminals before roaming. (T0 to T4)
2. The waiting time between the terminals entering power saving and sending Auth.(T4~T5)
3. After completing the reassociation and stating to send packets.(T9 to T12)
In the worst case, even if 802.11r support device, it would cost average 80.5 ms (47 +10.5 +23）.
Notes: Obviously, it’s not enough for most vowifi application, let alone AR/VR

## Slide 7: Some suggestions
The station empties the cache more aggressively before roaming.
The state machine transition of the terminals(laptop, wireless card, smartphones) and APs in the handoff process is time-consuming .
Links are quickly recovered after roaming, and the wireless rate adjustment and aggregation process could be accelerated.

## Slide 8: Conclusion
Low latency is one important KPI for future wireless networks, according to 4K/AR/VR applications.
Current handoff time of roaming between two APs does not meet the application requirements, the latency of roaming needs to be further reduced.

## Slide 9: References
802.11-18/1231r4, “EHT Draft Proposed PAR”
Wi-Fi CERTIFIED Voice-Enterprise: https://www.wi-fi.org/discover-wi-fi/wi-fi-certified-voice-enterprise
Cloud AR/VR Whitepaper: https://www.gsma.com/futurenetworks/wiki/cloud-ar-vr-whitepaper/#_ftn9