## Slide 1: Faster S1G+ Follow up
Date: 2022-12-30
Authors:
Name | Affiliation | Address | Phone | email
David Halasz | Morse Micro |  |  | dave.halasz@morsemicro.com

## Slide 2: Abstract
Follow up submission to 11-22/1831, which is about updating Sub 1 GHz with functionality already in the IEEE 802.11 specification.
Three functionalities identified were,
  1024 QAM
  Uplink Multi User MIMO
  Preamble Puncturing
This submission is a companion to 11-23/0039 S1G 1024QAM, which identifies changes to enable 1024 QAM for Sub 1 GHz

## Slide 3: Increased throughput for 802.11ah
Usage of 1024 QAM
  - rate ¾
  - rate ⅚
    - same puncturing patterns as for other rates
  - Interleaver parameters remain defined by S1G/.11ah & VHT/.11ac
Parameter | 1MHz | 2MHz | 4MHz | 8MHz
Ncol | 8 | 13 | 18 | 26
Nrow | 3*10 | 4*10 | 6*10 | 9*10
Nrot | 2 | 11 | 29 | 58
MCS mapping
  - Constellation mapping referenced to HE/.11ax
  - SIG field has 4 bit MCS
    - MCS11 → rate ¾ 1024-QAM
    - MCS12 → rate ⅚ 1024-QAM

## Slide 4: Increased throughput for 802.11ah
Theoretical rates achieved
MCS | Spatial Streams | Modulation Type | Coding rate | Data Rate (Mbps) |  |  |  |  |  |  | 
 |  |  |  | 1 MHz Bandwidth |  | 2MHz Bandwidth |  | 4MHz Bandwidth |  | 8Mhz Bandwidth | 
 |  |  |  | 8 𝝁sec GI | 4 𝝁sec GI | 8 𝝁sec GI | 4 𝝁sec GI | 8 𝝁sec GI | 4 𝝁sec GI | 8 𝝁sec GI | 4 𝝁sec GI
MCS11 | 1 | 1024-QAM | 3/4 | 4.5 Mbps | 5.0Mbps | 9.75 Mbps | 10.833Mbps | 20.25 | 22.5 | 43.875 | 48.75
MCS12 | 1 | 1024-QAM | 5/6 | 5 Mbps | 5.55Mbps | Not valid | Not valid | 22.5 | 25 | 48.75 | 54.1667
TX EVM requirement
  < -35 dB

## Slide 5: Increased throughput for 802.11ah
S1G Extended Capabilities element
  Used to signal MCS11 & MCS 12 capability
  Used in addition to S1G Capabilities element
    Does not replace S1G Capabilities element
Rate selection updates per availability of MCS 11 & 12
PICS updated to indicate S1G Extended Capabilities element is mandatory if support MCS 11 or MCS 12

## Slide 6: References