## Slide 1: Considerations for AP coordination in UHR: Coordinated Medium Access
Date: 2023-01-30
Authors:

## Slide 2: Problem Statement
Problem: today, in most deployments, APs don’t hear each others preamble which leads to overlapping transmissions within different BSSs resulting in higher latency due to collisions, retransmissions, hidden node issues, etc.
  In addition, single BSS transmissions efficiency may drop significantly with OBSS transmissions occupying the medium
Objective: improve the reliability of the network in terms of latency and throughput by increasing the chances for APs to listen to each others' transmissions and have a better coordination among them

## Slide 3: Design Principles
Coordinating APs need to end transmissions at predetermined time to be able to listen to each others' transmissions
Some hooks (e.g., Restricted TWT) have been introduced in EHT where STAs end the TXOP before the start time of a service period
  Restricted TWT is per single BSS
  UHR design can be built on top of the existing hooks
The coordination scheme between APs will facilitate the transmissions between the Coordinating APs at the start of the service periods
  This will help to reduce the unsynchronized transmission that may result from hidden nodes

## Slide 4: Coordinated Medium Access
Coordinated Medium Access allows several APs to coordinate their medium access to provide enhanced latency sensitive traffic delivery
Two levels of coordination:
  Level 1: Only APs end the TXOP before the other APs Coordinated SP
    APs can setup Trigger-enabled R-TWT SPs and use MU EDCA to reduce contention from STAs
  Level 2: STAs within each BSS end the TXOP with respect to the start of Coordinated SPs of other coordinating APs
    Associated AP will announce the Coordinated SP of other coordinating APs
    Coordinated SP can be announced through an R-TWT SP
      R-TWT supporting STAs will also end the TXOP before the R-TWT SP announced by the associated AP

## Slide 5: R-TWT TXOP rules per BSS, Coordinated Medium Access is for multi-BSS
11be R-TWT
Coordinated Medium Access
R-TWT SP
BSS-1
TXOP
R-TWT SP
BSS-2
TXOP
t
t
BSS-3
TXOP
t
Within the BSS, R-TWT supporting STA shall end TXOP before start of R-TWT SP announced by the associated AP
BSS-3 extend over the start of the R-TWT SP of BSS-1 and BSS2. Hence delay the transmissions.
Coordinated SP
BSS-1
TXOP
BSS-2
TXOP
t
t
BSS-3
TXOP
t
Level 1: APs end TXOP before Coordinated SP of its BSS and coordinating APs SP
Level 2: in addition, STAs that support Coordinated Medium Access end TXOP before the coordinated SP of other BSS

## Slide 6: Initial Gain Analysis
Parameters | values
Bandwidth | 80MHz @ 5 GHz, 2 SS
max TXOP | 4 ms
MCS | Fixed MCS 5
AP TXPw | 21 dBm
Low latency traffic | DL VR (Data rate: 60 Mbps, Frame Generation rate: 60 fps)

## Slide 7: Initial Gain Analysis (Cont’d)

## Slide 8: For Level 2: TSF may be different at different APs, two candidate solutions
  Option 1: APs synchronize their TSF
  Option 2: each AP corrects the start time of SPs announced by other APs before announcing other APs Coordinated SP information to its associated STAs (e.g., in its transmitted Beacon frames)
    requires extensions for TWT field to support different offsets between APs when Coordinated SP is communicated through R-TWT
AP1
AP2
Beacon of AP1
t
SP 1
t1 (w.r.t AP1)
t1 (w.r.t AP2)
SP 1
Correct start time
SP 1
t
If AP2 announces Coordinated SP1 without correcting the Target Wake Time, then AP2 will announce a start time that is different from the correct start time of SP1
Coordinated SP information

## Slide 9: Conclusion
We introduced the Coordinated Medium Access framework that can be considered for UHR
Two levels of coordination has been proposed in the Coordinated Medium Access framework
Coordinated Medium Access will facilitate the transmissions between the Coordinating APs at the start of the service periods and hence increase the reliability of the network

## Slide 10: Follow up On Coordinated Medium access

## Slide 11: Additional Aspects on Coordinated Medium Access
Coordinated Medium Access allows several APs to coordinate their medium access to provide enhanced latency sensitive traffic delivery
Within Level 1 or Level 2 (see slides 4 and 5), APs are expected to end the TXOP at coordinated TSF timestamps (e.g., start of coordinated SPs)
Coordinating APs need to ensure efficient medium access after ending the TXOP (e.g., within the Coordinated SPs)
One aspect of such efficient medium access would, for example enable coordination of the EDCA parameters used by each coordinated AP
  Aiming at reducing collisions between APs after the coordinated TSF timestamps (e.g., within the Coordinated SPs) where several APs may use prioritized EDCA parameters without coordination
  Provide a subset of AP(s) a prioritized access over other AP(s) during the Coordinated SPs

## Slide 12: Additional Aspects on Coordinated Medium Access (Cont’d)
Coordinated EDCA allow the APs to coordinate the channel access parameters among the coordinated APs
The coordinated APs will use the Coordinated EDCA parameters at the coordinated TSF timestamps (e.g., during the coordinated SPs)
At the coordinated TSF timestamps, the coordinated APs will contend for channel access using the Coordinated EDCA Parameter Set
Coordinated APs may fall back to other EDCA parameters outside the coordinated SPs which can be either coordinated or selected independently at each coordinated AP
The Coordinated EDCA Parameter Set may be carried in transmitted management frames