## Slide 1: Dynamic QoS feedback for UHR
Date: 2023-05-03
Authors:

## Slide 2: Problem Statement
Problem: today, clients report the buffer status, but the client has no means to communicate to the AP in real-time the expiry time by which it needs to deliver the queued low latency packets so that the client can meet the latency requirements of real-time applications (e.g., Gaming, …) in terms of delay bound and MSDU delivery ratio (e.g., 99.9%)
Proposal: improve the reliability of the network in terms of latency by allowing the UHR clients to report the packet enqueue/expiry time or delay bound of the low latency packets to facilitate the delivery of those packets before it gets expired while waiting in the queue
Is the STA meeting its latency requirements?
Need to tell the AP that I need (more) triggering before my packets expire

## Slide 3: Dynamic QoS feedback for UHR
11be allows a STA to setup an SCS agreement with an MSDU delivery ratio up to 99.9999%
Due to varying traffic and network conditions, during operation a STA may start failing the target MSDU delivery ratio
This requires the AP to react and recover the target MSDU delivery ratio in an efficient manner
The current BSR does not include timing component that can assist scheduling of latency sensitive traffic to meet the delay bound or help prioritize the low latency STAs
Different clients may report similar queue size in the BSR; however, some clients may have more urgent traffic pending delivery before getting expired while waiting in the queue
  This could be due to non-deterministic traffic arrival or non-deterministic channel access delays due to OBSS occupying the medium

## Slide 4: Design Principles
Per TID report carried in MAC frame header (e.g., A-control)
Include low latency queue size
Include Timing Component to report most urgent packets (e.g., Head-of-line (HOL) packets) per TID
  HOL packet delay bound (exact amount of time after which the packet gets dropped, e.g., 10 msecs)
    In some cases, the delay bound may not be known
    if known, the reported delay bound will change based on (re)-transmission time
  HOL packet enqueue time or expiry time in terms of TSF time
    Enqueue time helps the AP to prioritize scheduling without necessarily a delay bound
    Enqueue/expiry time does not need to be changed frequently as in case of delay bound
AP
STA
QoS DATA/NULL
BA
Trigger
Low latency data
Request for UL resources
Low latency Traffic arrives
Dynamic QoS Feedback
Max tolerable delay
Could be TB-PPDU or non-TB PPDU
QoS Data frame may carry low latency data as well as Dynamic QoS Feedback for same/other TIDs

## Slide 5: Design Principles (Cont’d)
The dynamic QoS feedback can be either:
  Solicited:
    AP sends a Trigger frame to solicit the dynamic QoS feedback from the client
      The Trigger frame may carry a special indication for the Dynamic QoS feedback vs. regular BSR
    Client responds with a QoS Null frame that carry the dynamic QoS feedback in the MAC frame header (A-control)
  Unsolicited:
    Client reports the dynamic QoS feedback in the MAC header of QoS Data and QoS Null frames

## Slide 6: Conclusion
We introduced the Dynamic QoS feedback that can be considered for UHR
The Dynamic QoS feedback allows the STA to report the time by which it expects the AP to send the Trigger frame so that the STA can meet its latency requirements
This information will be considered by the AP when scheduling the clients to enhance the reliability in the network

## Slide 7: Appendix