## Slide 1: OTA MAC Rotation
Date: 2023-10-19
Authors:

## Slide 2: Summary
Background
  Unencrypted predictable frame fields can enable client tracking by identifying a set of frames for which a single client is transmitter or intended receiver. This can allow tracking presence or location of the person using that client, compromising privacy.
Proposal
  Goal: prevent tracking associated clients across epoch boundaries, within each epoch is acceptable.
OTA Randomization:
  Prevents client frame tracking across epoch boundaries
    “Re-randomize” MAC address at every epoch
  Does not prevent client frame tracking within an epoch

## Slide 3: Approach
At association AP STA and non-AP STA shall negotiate if they both support OTA rotation;
AP STA and non-AP STA shall use HKDF to construct the new OTA MAC prior to epoch
HKDF-Extract requires a salt, and IKM (Input Keying Material) value to derive the PRK (pseudo random key)
    For the salt value we can use an FTM value
    the PMK derived from the 4WHS shall be used as the IKM
      Because FTM (Fine Time Measurement) and PMK are known to both AP and non-AP STA – the new IRM can be validated by the AP
      There is no need to send the new IRM over the air, STA can just start using it
PRK = HMAC-Hash (FTM, PMK)
    Hash algorithm would be aligned with the Hash algorithm used with the AKM during association (SHA256, 384,512)

## Slide 4: Approach
HKDF-Expand (PRK, info, L) -> OKM
    Pseudo Random Key – calculated from HKDF-Extract function (PRK)
    Info – context, in this case “New OTA MAC”
    L – length of output keying material in octets (<= 255*HashLen)
  IRM_List = HMAC-Hash(PRK, "New OTA MAC”, L)
    Hash would be aligned with the Hash algorithm used with the AKM during association (SHA256, 384,512)
    L = Num_Macs * 6(bytes)
      Num_Macs must be an integer between 1 and 42
    Mac1 = IRM_List [first 6 bytes:] | Mac2 = IRM_List [second 6 bytes:] etc; second bit force to 26 A | E to align with IEEE

## Slide 5: Client Initiated Rotation
Before the defined epoch, allow the client to rotate the OTA mac
Announce time – Tell AP-STA when we will start to use new OTA IRM – sent in a protected frame
e.g. in 1 minute we will use new OTA IRM
Once announce time has elapsed, countdown to Sunset time starts.
Sunset time – After old mac shall not respond and AP shall not forward packets for old IRM
Fully Untrusted - DTIM * 5
Semi Untrusted – DTIM * 5
Trusted – DTIM * 5

## Slide 6: Straw Poll
Would you agree that HKDF could solve the OTA mac rotation issue?
Would you agree that computing multiple future OTA at one time would be beneficial?