## Slide 1: Enhanced replay detection for header protection
Authors:
Name | Affiliations | Address | Phone | email
Abhishek Patil | Qualcomm |  |  | appatil@qti.qualcomm.com
Duncan Ho |  |  |  | 
Alfred Asterjadhi |  |  |  | 
George Cherian |  |  |  | 
Gaurang Naik |  |  |  | 
Date: 2023-11-03

## Slide 2: Background
Enhancing security in 802.11 is one of the goals of UHR
  To that effect, UHR will provide mechanisms to protect certain Control frames and fields within the MAC header.
Previous proposals (e.g., 23/1888) discuss protection the MAC header via integrity check
  A MIC is generated based on the fields in the MAC header.
    Since the contents of the header fields can change when an MPDU is retried, a fresh MIC is generated for the header fields each time an MPDU is retried
      The payload of the MPDU is not re-encrypted
  Control frames are also protected via a MIC
In this contribution we look at attack scenarios that warrant the need for adding a time component to the security algorithm.
  Specifically, we propose to have the PN for header (and Control frame) protection be based on portion of the TSF

## Slide 3: Issue
A frame is considered as replayed if the received packet number (PN) is <= the last received PN
  In other words, the PN needs to be monotonically increasing.
  The PN is included within the frame so that the receiver knows the PN that was used for protecting the frame.
    Helps keep both sides in-sync in case of lost packets
There can be attack scenarios where a rogue device is able to jam the reception of MPDUs and later replay them
  In this contribution, we call such an attack as a jam, record and replay attack (JRR)
  The replayed MPDUs can either be
    unmodified or
    the MAC header and data payload of different MPDUs are swapped
      This goes unnoticed since the security checks for header and payload will pass
  Since the recipient did not receive the original MPDUs, it does not have a record of a PN to compared with.
    As a result, the JRR attack is successful (i.e., the attacker manages to fool the replay detection logic).
  The JRR attack is especially possible when there is sparse or bursty traffic
With the JRR attack, the recipient can get into an undesirable state or perform unwanted actions depending on the contents of the MAC header fields. For example:
  When the original frame indicates changes to some operational parameters, the receiver would apply them later.
    This would cause the transmitter and receiver to be in different states.
    For example, MPDU(s) carrying PM=1 is jammed (and delivered late) causing the AP to perform a DL of MPDUs meant for the recipient while the recipient is in doze state.
  When data and header of a series of MPDUs is swapped, the payload for some MPDUs will be dropped since the monotonically increasing property of PN will not hold true.
    For example, attacker records MPDU1 (SN=1, PN=1) and MPDU2 (SN=2, PN=2) and switches the header of an MPDU1 with header of MPDU2 causing the receiver to receive MPDU1 with SN=1, PN=2 and MPDU2 with SN=2, PN=1. This will cause MPDU2 to be dropped during PN based replay check.

## Slide 4: Solution and challenges
Solution summary:
  The remedy for such a jam, record and replay attack is to have a time component in the PN so that the receiver can discard a ‘stale’ frame.
    Using TSF as PN is an option
Although the approach will preserve the requirement that a PN is monotonically increasing, there are challenges to this approach as described below
Challenge:
  At the receiving device, the time based PN needs to match with the local time
  However, a client device is allowed to have extend periods of doze state to conserve battery.
    For example, a client that has indicated a listen interval (LI) of 10 is allowed to skip up to 10 beacons.
      TBTT occurs every 100 ms  a client with LI of 10 will skip beacons for up to 1 second (10 BIs).
  Since the clocks run independently on each device, they will drift overtime. The standard requires an accuracy of +/-100ppm
    Therefore, in the worst-case drift between an AP and a client can be ± 200 ppm (see 11.1.3.9)
  As an example, a client with an LI of 10 can have its local TSF off by 200 µs with respect to its AP after skipping 10 beacons (1sec).
    In such case, if the client has a slower clock, it will be 200 µs behind the AP’s TSF and a UL frame from the client will have a PN that will be 200 µs in the past.
    This will cause the AP to discard a genuine frame since the TSF appears to be stale

## Slide 5: Addressing drift
Solution:
  Reduce the granularity of time by ignoring lower bits of TSF to mask the clock drift
    The number of LSBs ‘x’ to ignore is TBD.
    In this contribution, we provided some examples with x=8.
    The x value could be standardized or can be negotiated between the two devices based on their capability
      i.e., LI and expected drift.
  For example, by not including the lower 8 bits, the timing granularity reduces to 256 µs which would be sufficient to address majority of the clock drift scenarios.
However, the reduced time granularity means multiple packets sent within a 256 µs window would be stamped with the same TSF.
  This will cause the receiver to drop packets
To address this, append a counter to the partial TSF
  Counter increments each time a packet is transmitted with the same TSF value and resets to 0 when LSB of the partial TSF rolls over
  The overall PN is a concatenation of partial TSF + an x bit counter
  Assuming PN size remains unchanged (48 bits) and the lower 1 octet represent a counter:
    PN[0:7] = 8bit counter
    PN[8:47] = TSF[8:47]
  TSF[48:63] is not signaled

## Slide 6: Multiple tx with the same (partial) TSF
At the receiving device, the replay check is performed as follows:
  compare the (partial) TSF with current local time and
    If the received value is lower than the current local (partial) TSF, drop the packet*.
    Else, if the received TSF is the same as the TSF received in the most recent packet, compare the received counter value:
      If the received counter value is equal or less than previously received counter, drop the packet
      Else, process the packet further
    Else process the packet further
  Record the received (partial) TSF and the counter values as the last know values (respectively) for a packet that passed replay check and subsequent checks (e.g., MIC validation)
    These are used for comparison with the immediately next received packet
* there is a corner case when the (x+1)th bit of the TSF has recently flipped.
  For example (assuming x=8), receiver’s 9 bits of TSFR[0:8] = 100000001; while transmitter is TSFT[0:8] = 011111101)  off by 4 us
  In such case, since the PN value used for header protection is carried within the frame, the recipient will know that the transmitter clock is slightly behind and will still accept the frame.
    There can be some tolerance built into the system.

## Slide 7: MLO consideration
In MLO, each affiliated AP is allowed to have an independent clock
  As a result, TSF on each link can be a different value
    Consequently, a TSF based PN would be link specific
  This would be OK since the contents of the MAC header and Control frames are specific to a link.
  This can be addressed by adding link ID as part of the PN.
    Assuming upper byte is reserved for link ID

## Slide 8: PN rollover
Today, when the PN wraps around (i.e., all the values are exhausted), both devices perform a rekeying operation to generate a new security key.
If lower 8 bits of the PN is used for signaling a counter and the upper 8 bits are used for signaling link ID, then the PN[8:39] will carry the partial TSF.
  PN[0] = counter
  PN[8:39] = TSF[8:39]
  PN[5] = link ID
For TSF[8:39] the wraparound would occur after 2^40 µs = 12 days
  Therefore, TSF/PN wraparound will not be the reason for rekeying (i.e., TSF space is sufficiently long)
2^48 | 2.81475E+14 |  | 2^40 | 1.09951E+12
sec | 281474976.7 |  | sec | 1099511.63
hrs | 78187.49 |  | hrs | 305.42
days | 3257.81 |  | days | 12.73

## Slide 9: Applicability to Control frame protection
TSF based PN can also be used for Control frame protection
  This will simplify the PN space maintenance.
    i.e., we don’t need to manage a third PN spaces (one for header protection, another for Control frame protection in addition to the PN for Data payload encryption).
In addition, the PN space will not get exhausted for several days (12 or more) when TSF based PN is used.
  This is regardless of TSF-based PN being used for Control frame and header protection.
  New PN is needed for each (re)transmission of an MPDU and for each protected Control frame.
    Without TSF-based PN, we run the risk of frequently encountering PN rollover (and hence frequently requiring re-keying).

## Slide 10: Summary
In summary, this contribution proposes to use portion of the TSF as PN to prevent jam, record, replay attacks.
  The proposal accounts for clock drift and MLO
The proposal maintains the monotonically increasing properties of PN
  A counter accounts for more than one transmission for the same TSF value.
The scheme will also work for Control frame protection and will eliminate the need for maintain multiple PNs
  Simplifies the operations at tx and rx side since TSF is an on-going clock (i.e., doesn’t require additional storage).
  Even in a high thruput scenario, it does not run the risk for PN rollover for many days.