## Slide 1: MAC Header Protection
Date: 2023-11-09
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Daniel F Bravo |  |  |  | 
Ido Ouzieli |  |  |  | 
Johannes Berg |  |  |  | 
Ilan Peer |  |  |  | 
Danny Alexander |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Protection of MAC header has been discussed [1]
We provide our thoughts in this presentation

## Slide 3: Need for MAC Header Protection
Several fields in the MAC header today are masked out and not protected by the frame body protection
  Due to possibility of value change during retransmission and the need to reuse a PN
However, those masked out fields do introduce security concern
  PM bit as discussed in [2]
  SN field due to BA protocol attack to complete the protection of BA protocol attack
  HT control due to various information that maybe piggybacked
Hence, it is indeed useful to protect MAC header

## Slide 4: Protect MAC header of which frame
The problem we have in hand (ex, PM, SN, HT Control) are in the MAC header of data and management.
Further, those problems (PM, BA protocol, HT Control) are specific to individually addressed data and management frame.
  Introduce MAC header protection for group addressed data and management frame likely have backward compatibility issues or blow out the group addressed transmission over the air
It then makes sense for 11bn to focus the design of MAC Header protection on individually addressed data and management frame

## Slide 5: Attack model
The basic attack model is forgery attack, where an attacker can achieve the attack by simply forging one frame rather than other more involved attack methods
  Preventing this basic attack model only needs integrity check
For other attack models,
  privacy attack may require encryption and introduce higher implementation complexity
  jam/record/replay attack is more involved and also requires more complicated mechanism to resolve
Suggest to focus on basic forgery attack model and use GMAC-256
  GCMP-256 is supported by every 11be device
  The best we have and no need for negotiation or rules

## Slide 6: Consideration with existing Framebody protection
To accommodate the possibility of MAC header change during retransmission, MAC header protection and Frame body protection needs to be MIC separately
  Imply separate key different from frame body protection
  Imply separate PN field different from frame body protection
  Imply separate MIC computation different from frame body protection
Propose to have additional Key ID, PN and MIC fields to protect MAC header of individually addressed data frame and management frame

## Slide 7: Consideration of key
Since the scope is on individually addressed frame, it is natural to have the key as part of the PTKSA between MLDs
However, given that the MIC check is likely lower layer, we may want to have per link PN and replay counter to avoid coordination of PN across links
Further to avoid nonce reuse, we will need the nonce construction to be based on STA MAC address identified in A2

## Slide 8: Consideration on Acknowledgement Response
Today acknowledgement is sent to individually addressed data/management frame after FCS check
With MAC header protection, better to do MIC check before sending acknowledgement
  If Acknowledgement is sent without MIC check of MAC header, then a valid acknowledgement is sent even the frame is eventually dropped due to MIC check failure
  More mechanisms maybe required to tolerated MIC check after sending acknowledgement
Suggest to at least allow receiver to do MIC check before sending acknowledgement

## Slide 9: Fields to be Protected
Fields like PM, SN, HT Control should naturally be protected
Fields like Duration need separate discussion
  Recall Duration from any 3rd party CTS is not protected, and is difficult to be protect if feasible at all
A natural argument is to basically protect everything of MAC header fields instead of regretting later
If the argument is to simply protect everything, then suggest to protect also security header of frame body, so we protect everything in the “header”

## Slide 10: Conclusion
We think MAC header protection is an important feature for 11bn
  Focus on individually addressed data and management frame
  Use GMAC-256 to prevent basic forgery attack
  Have separate key, PN field, MIC calculation different from frame body protection
  Have pairwise key between MLD but per link PN and replay counter with nonce construction based on STA MAC address
  Allow sending response after checking FCS and MIC of MAC header protection
  Simply protect everything including security header of framebody

## Slide 11: SP #1
Do you support to define MAC header protection for individually addressed data and management in 11bn?

## Slide 12: SP #2
Do you support to use GMAC-256 to protect MAC header of individually addressed data frame and management frame?

## Slide 13: SP #3
Do you support to have additional Key ID, PN and MIC fields to protect MAC header of individually addressed data frame and management frame?

## Slide 14: SP #4
Do you support to have a pairwise key between an AP MLD and a non-AP MLD with per link PN and replay counter to protect MAC header of individually addressed data and management frame?

## Slide 15: SP #5
Do you support that nonce construction for the MAC header protection will use STA MAC address identified by A2?

## Slide 16: Reference
[1] 11-23-1888 MAC Header Protection follow up
[2] Framing Frames: Bypassing Wi-Fi Encryption by Manipulating Transmit Queues