## Slide 1: Secure Control frames-Follow Up
Date: 2024-01-11
Authors:
March 2024
Notes: September 2012

## Slide 2: Introduction
UHR will rely on control information for lots of purposes
  Acknowledgment, NAV setting, sounding, triggering, etc.
While frames carrying this information are not be protected
  BAR, BA, Trigger, etc.
A malicious player can attack a link by targeting frames containing control information leading to
  Data stream disruption, denial of service, power drainage, resource wastage, etc.
Data stream disruption is especially problematic for UHR
  Since it directly affects the reliability of the communication link
Which is an important issue that need to be addressed,
  And if the other abovementioned issues are solved on the way, then much better
March 2024

## Slide 3: Proposal
Provide means to protect:
  At least certain control frames
And since control info., in general, needs to be generated quickly:
  Provide message integrity check (MIC),
    Perhaps not worrying about encryption (more complex)
In the following we discuss mechanisms to protect at least:
  Trigger, Multi-TID BAR, and Multi-STA BlockAck (M-BA) frames
    Possibly expand to C-BA, and BAR frames as well
Since an attacker can exploit the vulnerability of these frames
  To disrupt/corrupt the data paths between two STAs
Aiming at solving the issue at both the AP and the STA side
March 2024

## Slide 4: Example of Attacks
MU BAR Trigger frames solicits TB PPDUs from one or more STAs
  PPDUs are generated from the intended recipients of the Trigger frame
    Each TB PPDU contains a C-BlockAck or M-BA frame
      All buffered QoS Data up to SSN of the BAR are reordered and passed to the next MAC process
      BA scoreboards are shifted to align with the value of the SSN of the BAR
  Now if this frame is sent by an attacker, then there will be a misalignment of
    QoS Data delivery status and BA scoreboards between the originator and recipient
  Same issue exists with Multi-TID BAR and C-BAR frames
M-BA frame is sent to acknowledge received QoS Data frames
  BlockAck Bitmap indicates receive status of the received QoS Data frames
    Originator uses this information to update the BA scoreboard
  Now if this frame is sent by an attacker, then again there will be a misalignment
    But also, false indications of receive status of Data frames at the recipient
Hence, misalignment, wrong classifications, packets discarded, etc.
C-BA 1
MU BAR
backoff
C-BA 2
Data 1
Basic Trigger
Data 2
M-BA
March 2024

## Slide 5: Proposal: Control MIC
Define a Control MIC Field (CMF)
  Inherit structure from Management MIC IE (MME) (used for beacon protection)?
    But will benefit from overhead reduction since CMF will be carried in control frames
    E.g., one bit for Key ID, partial PN in the frame and base PN is not; reduced MIC, etc.
      We can think more about it (lots of existing methods, see protected WUR frames, PV1 frames, etc.)
Add CMF field to at least the following control frames
  Trigger, M-BA, (covering DL and UL MU sequences),
  BAR, C-BA and Multi-TID BAR (covering DL and UL SU sequences)
In such a way that it is backwards compatible (whenever necessary)
  E.g., a group addressed control frame can address both UHR and non-UHR STAs
Decide if extra padding is needed when the control frame is protected
  Since MIC check may need some extra processing time
  Noting that we already have several tools in place to provide this flexibility
    However, separate padding indication may be needed
 | Key ID | IPN/BIPN | MIC
Octets: | X | Y | Z
March 2024

## Slide 6: Secure Trigger frame
Add CMF to provide Trigger frame protection
  MIC is calculated over the preceding fields (whichever needs protection)
    Including the Common Info and User Info List fields
  Applicable to supporting UHR STAs (& unassoc. UHR STAs that know the key)
    Other STAs (e.g., HE/EHT) simply ignore CMF, but keep processing the Trigger frame
MIC is carried in the CMF and follows the “useful” User Info List
  GMAC for MIC calculation & temporal key (TK) to compute MIC
  Separate PN for Trigger frame replay protection
UHR STAs discard a received Trigger frame in case of a MIC mismatch
  Hence, no need to generate TB PPDUs, saving power, keep data path intact, etc.
A side benefit is that the receiving UHR STA need not wait for FCS check
 | Frame Control | Duration | RA | TA | Common Info | User Info List | CMF | Padding | FCS
Octets: | 2 | 2 | 6 | 6 | 8 or more | variable | variable | variable | 4
 | Key ID | PN | MIC
Octets: | X | Y | Z
March 2024

## Slide 7: Where to carry the CMF in Trigger frame
Option 1: In User Info fields
  Identified with an unassigned value of the AID12 field (e.g., 2023)
    Each User Info field is 5 bytes and how many depends on the length of the CMF field
Option 2: In Padding field, (immediately) after the first two octets
  First two octets are a sequence of one’s that STAs use to start ignoring padding
  Next X+Y+Z octets of Padding field would be the CMF, and rest will be padding
    A bit for CMF presence (e.g., use Protected bit in Frame Control field?) and possibly
    A CMF length field (while avoiding the all one's combination to not confuse with padding)
 | AID12 (2023) | Reserved | Reserved
Bits: | 12 | 4 | 24
 | Key ID | IPN | MIC
Octets: | X | Y | Z
 | AID12 (2023) | Reserved | Reserved
Bits: | 12 | 4 | 24
 | AID12 (2023) | Reserved | Reserved
Bits: | 12 | 4 | 24
Option 1
…
March 2024

## Slide 8: Secure M-BA frame
Add CMF to provide M-BA frame protection
  MIC is calculated over the preceding fields of the frame (whichever needs protection)
    Including the BA Control and the preceding Per AID TID Info fields
  Applicable to supporting UHR STAs
    Other STAs (e.g., HE/EHT) simply ignore CMF, but keep processing the M-BA frame
MIC is carried in the CMF and follows “useful” Per AID TID Info List
  GMAC for MIC calculation & temporal key (TK) to compute MIC
  Separate PN for M-BA frame replay protection
Padding: Achieved with STA Info fields addressed to other STAs or to nobody
UHR STAs discard a received M-BA frame in case of a MIC mismatch
  Hence, no update of BA scoreboards or modification of data path
Octets: | 2 | 2 | 6 | 6 | 2 | variable | 4
 | Frame Control | Duration/ ID | RA | TA | BA Control | BA Information | FCS
Per AID TID Info 1
…
Per AID TID Info n
Repeated for each
<AID, TID> tuple
CMF
Padding
March 2024

## Slide 9: Where to carry the CMF in M-BA frame
Also applicable to Multi-STA BlockAck frame, wherein
  CMF field is in a Per AID TID Info field that is identified by an AID11 field that is unassigned (say e.g., 2023)
    The FN subfield of the BA SSC indicates the CMF field length
Note: We can add CMF to C-BlockAck frames as well
Octets: | 2 | 2 | 6 | 6 | 2 | variable | 4
 | Frame Control | Duration/ ID | RA | TA | BA Control | BA Information | FCS
Per AID TID Info 1
…
Per AID TID Info n
Repeated for each
<AID, TID> tuple
2 | 0 or 2 | 16, 32
AID TID Info | Block Ack Starting Sequence Control | CMF
Bits: | 11 | 1 | 4
 | AID11 | Ack Type | TID
March 2024

## Slide 10: Secure Multi-TID BlockAckReq frame
By now, notice the pattern
  CMF follows the last useful BAR Information
  The first bit of the Per TID Info field is set to 1 to indicate CMF
    Possibly they can also indicate the length (e.g., use 2 bits and nonzero)
  Padding can be achieved with useless BAR Information fields
Note: We can add CMF to C-BlockAckReq frames as well
CMF
Padding
March 2024

## Slide 11: Temporal Keys
Traditionally we use
  Integrity group temporal key for protecting group addressed frames
    This key is only used by the AP (note: Beacon has its own key, namely BIGTK)
  Pairwise temporal keys for protecting individually addressed frames
    This key is used by the AP and by non-AP STAs, and
    There are at least as many as there are associated STAs
So, it is natural to consider control group/pairwise temporal keys as well
  However, the more keys are used the more time is needed for key lookup (especially for AP)
    Could be problematic when generating control frames (on-the-fly)
    Hence, it may be worth evaluating the use of padding to give time for key retrieval
Since this is this is preferred choice from security perspective, then
  Control integrity group temporal key only used by AP for group control frames
  Control pairwise temporal keys used by STAs for individual control frames
February 2024

## Slide 12: Conclusions
We discussed security issues with certain control frames and discussed mechanisms for securing them
The idea is that securing control information
  Will solve security issues with (at least some) control frames, and
  Ensure reliable exchanges between UHR STAs
And as side benefits of securing Triggers, it can reduce
  STA’s draining their power (useless response PPDUs),
  Waste resources (useless TXOPs),
  False wake transitions (eMLSR, HE dynamic SMPS, etc.)
March 2024

## Slide 13: Straw Poll
Do you agree to define protection in IEEE802.11bn for the following frames
  Trigger, BlockAck, and Block Ack Request frames
    Which variants of BlockAck and BlockAckReq frames are to be protected is TBD
March 2024