## Slide 1: mmWave Operation without mmWave Beacon
Date: 2023-11-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: MLD with mmWave Link
In a MLD with mmWave link and 2.4/5/6GHz link (non-mmWave link) the different links have different coverage.
In order for a non-AP MLD with mmWave link and non-mmWave link to decide whether it can reach an AP MLD through mmWave link, different methods can be considered
  one way is to define the light Beacon in mmWave link.
    The light Beacon is not used for association, BSS management.
    The light Beacon is used for reachability decision, mmWave AP’s channel selection, smooth roaming etc.
  Another way is no mmWave Beacon is defined
In this presentation, the MLD operation without mmWave Beacon is proposed

## Slide 3: Reachability Decision through Non-mmWave Link
An AP MLD with mmWave link and at least one non-mmWave link announces the threshold about whether a non-AP MLD can reach the AP MLD through the non-mmWave link.
  The threshold could be the path loss in the non-mmWave link, the RSSI in the non-mmWave link (of the received Beacon) or the other threshold.
If a non-AP MLD receives the Beacon or the other frames from an AP MLD in a non-mmWave link whose threshold is more than the threshold announced in the Beacon of the non-mmWave link, the non-AP MLD can do the association with AP MLD with the assumption that the non-AP MLD can reach the AP MLD through the mmWave link.

## Slide 4: Beamforming Before Association
Before the association, a non-AP MLD with mmWave link + non-mmWave link and the AP MLD with mmWave link + non-mmWave link can do the beamforming of mmWave link for deciding whether the non-AP MLD can reach the AP MLD through the mmWave link.
The frames related to the beamforming in mmWave link are class 1 frames.

## Slide 5: No Beacon on mmWave Link
An AP MLD with mmWave link and non-mmWave link will not transmit its Beacon on its mmWave link.
Some amendment to 802.11be MLD operation is required, e.g.
  The channel switch procedure.

## Slide 6: TSF Related Operation
A non-AP MLD can’t do the TSF synchronization with the AP MLD on mmWave link since the Beacon frames are not transmitted on mmWave link.
One method for TSF related operation is that the TSF time and number of TBTT are defined based on another active link (reference link) of the AP MLD.
  The operation per the TBTT, e.g. BSS color change of mmWave link will use the TBTT of the reference link.
Another method is that the TSF time and TBTT of the mmWave link are defined without the Beacon transmission
  TBTT is virtual since no Beacon is scheduled for the transmission at the TBTT on mmWave link.
  The operation per the TBTT, e.g. BSS color change of mmWave link will use the virtual TBTT.