## Slide 1: Power Save for UHR
Date: 2024-01-12
Authors:

## Slide 2: Introduction
According to 11bn PAR [1] , power saving of AP as well as non-AP STA is one of key features.
In this contribution, we propose methods for reducing power consumption of STA or AP in Triggered TXOP Sharing procedure

## Slide 3: Recap: Triggered TXOP Sharing in EHT
An AP can allocate a time portion of an obtained TXOP to one associated non-AP EHT STA for transmitting one or more non-TB PPDUs.
Allocation Duration
CTS
MU-RTS TXS TF
BA
AP
STA1
Non-TB PPDU
Allocation Duration
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
TXS Mode 1
TXS Mode 2
Non-TB PPDU
BA

## Slide 4: Recap: Triggered TXOP Sharing in EHT
During TXS allocated time, non-AP STAs that don’t participate in the procedure are still in awake state although they want to save more power and they don’t intend to communicate with AP
In TXS mode 2, the non-AP STA allocated by the AP may return the remaining time of the allocated time if the STA finished the transmission earlier
Allocation Duration
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
BA
Non-TB PPDU
QoS Null
ACK
NAV
TXOP
DL frame
BA
DL frame
BA

## Slide 5: Recap: Dynamic PS mode [2]
STA is in Listen State unless solicited to transition to Awake state
  Listen State: STA is only capable of RX PPDUs of certain configuration
    E.g., non-HT (dup) PPDUs, and mandatory data rates
  Awake State: STA is capable of RX PPDUs with highest BW/NSS
    E.g., as advertised in most recent Caps/OMN/OM Control (for both AM and PS modes)
<20MHz,1SS>
Non-HT (dup) PPDU
<80MHz,1SS>
<160MHz, 2SS>
Beacon
…
Beacon
ICF
ICR
Data
BA
ICF
ICR
Data
BA
Frame Exchange/TXOP
Frame Exchange/TXOP

## Slide 6: TXS Power Save (PS) Operation – TPS Mode 1
When a STA receive an MU-RTS TXS Trigger frame, if the STA is not scheduled and supports the TXS PS Mode 1, the STA enters the doze state
During the TXS allocated time, the AP does not transmit a frame to the STA and the AP can transmit a frame to another STA
Allocation Time
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
BA
Non-TB PPDU
QoS Null
ACK
Doze state
DL frame
BA
DL frame
BA

## Slide 7: TXS Power Save (PS) Operation – TPS Mode 1
The STA can enable or disable the TXS PS Mode 1 before the TXS procedure
STA may enter the doze state only in case of enabling the TXS PS Mode 1
  Ex1) if the STA has lower battery power, the STA can enable the TXS PS Mode 1
  Ex2) if the STA has higher battery power or wants to receive DL frame as soon as possible (e.g., latency sensitive (or urgent) traffic), the STA may disable the TXS PS Mode 1
Allocation Time
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
QoS Null
ACK
Doze state
DL frame
BA
Enabling TXS PS 1
ACK

## Slide 8: TXS Power Save (PS) Operation – TPS Mode 2
If the TXS assigned STA returns the remaining duration, the STA enters the doze state
AP does not transmit a frame to the STA that enters the doze state during the remaining duration
The detailed procedures are TBD (e.g., signalling, remaining duration)
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
BA
Non-TB PPDU
QoS Null
ACK
Awake state
DL frame
BA
DL frame
BA
Doze state

## Slide 9: TXS Power Save (PS) Operation – TPS Mode 2
The STA can enter the listen state instead of the doze state
AP will transmit an initial control frame firstly before transmitting DL frame to the STA
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
QoS Null
ACK
ICF
BA
ICR
DL frame
DL frame
BA
BA
Non-TB PPDU
Awake state
Listen state
Awake state

## Slide 10: TXS Power Save (PS) Operation – TPS Mode 3
AP can transition to the listen state while the assigned STA transmits frame to a peer STA in TXS mode 2 – First P2P transmission case
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
ICF
BA
ICR
BA
Non-TB PPDU
Listen state
Awake state
Non-TB PPDU
Non-TB PPDU
BA

## Slide 11: TXS Power Save (PS) Operation – TPS Mode 3
AP can transition to the listen state while the assigned STA transmits frame to a peer STA in TXS mode 2– First UL transmission case
CTS
MU-RTS TXS TF
BA
AP
STA1
STA2
Non-TB PPDU
STA3
ICF
BA
ICR
BA
Non-TB PPDU
Listen state
Awake state
Non-TB PPDU
Non-TB PPDU
BA
Awake state

## Slide 12: Conclusion
We proposed the methods to reduce the power consumptions of non-AP STAs and AP in TXS procedure
  Unassigned STAs may enter the doze state during the TXS allocation duration
  Assigned STAs may enter the doze state/listen state after the STAs return the remaining duration to the AP
  In that case, AP should not transmit a frame to those STAs in doze state and transmit, to STA in listen state, ICF before sending other frames to the STA
  AP may also enter the listen state during P2P transmission by the assigned STA
The details (e.g., signaling, conditions) are TBD

## Slide 13: References
[1] 11bn PAR 23/0078
[2] 23/1965r2, Dynamic PS