## Slide 1: Distribution bandwidth of DRU
Date: 2023-12-18
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 
David Xun Yang |  |  |  | 

## Slide 2: Recap on Distributed RU
[1] [2] [3] give a detailed discussion on distributed RU (DRU). Several aspects are discussed including but not limited to:
  Distribution bandwidth
  dRU Size
  dRU operation mode
In this contribution, we will share our views regarding these aspects.

## Slide 3: Distribution bandwidth
Several aspects will affect the distribution bandwidth:
  Preamble puncturing
  BW capability: 20 MHz/40 MHz/80 MHz/160 MHz/320 MHz capability or operating bandwidth.
  Power boost gain of RU
  DRU capability (of other OFDMA users)
20 MHz only non-AP STAs
80 MHz only non-AP STAs
Dist BW = 20 MHz
Dist BW = 40 MHz

## Slide 4: Distribution bandwidth
In [1], distribution BW of 20, 40 and 80 MHz has been proposed.
  20 MHz and 80 MHz are essential when preamble puncturing and 20 MHz only or 80MHz only non-AP STA exist.
  40 MHz is good for a 40 MHz PPDU. For 80 MHz PPDU or above, 40 MHz can be replaced by two 20 MHz distribution bandwidth too. Whether to have 40 MHz distributed bandwidth can be further discussed for PPDU with bandwidth of 80 MHz or above.
20 MHz only non-AP STAs
80 MHz only non-AP STAs
Dist BW = 20 MHz
Dist BW = 20 MHz
Dist BW = 20 MHz
Dist BW = 40 MHz
Opt 1
Opt 2

## Slide 5: Distribution bandwidth
Distribution BW of 160 MHz is also a valid option since:
  It is mandatory for AP to support 160 MHz in 6 GHz.
  160 MHz capable non-AP STA is also well sold in high-end market. Supporting a two user UL DRU OFDMA is a reasonable scenario.
    Support up to 996-tone RU and try to avoid new segment parser design
  Achieve higher power boost gain for RU 106 or above (>= 80 tones).
BW = 160 MHz
DRU 996-1
DRU 996-2
…

## Slide 6: DRU operation mode
In [1], a hybrid of dRU and rRU is proposed. This is valid when:
  dRU size which is equal to the distribution bandwidth is rRU.
  dRU capability (support or not)
In [1], dRU only within BW 20/40/80 MHz, and a hybrid mode is supported within 160 MHz or 320 MHz, where each mode is per 80 MHz indicated. Whilst DRU over 160 MHz may also be possible.
For simplicity, an alternative solution would be: no hybrid is allowed.
  May use A-PPDU instead to support a hybrid of rRU and dRU.
DBW = 160 MHz
DRU 996-3
DRU 996-4
DBW = 80 MHz
rRU
…

## Slide 7: Summary
Based on [1-3], we show our views regarding distribution bandwidth, DRU operation mode and signaling.

## Slide 8: Straw Poll #1
Do you agree to include the following into the 11bn SFD?
  11bn defines distributed bandwidth of 20 MHz, 40 MHz, 80 MHz and 160 MHz.
    Y
    N
    A

## Slide 9: Straw Poll #2
Do you agree to include the following into the 11bn SFD?
  11bn defines distributed bandwidth that is smaller than 80 MHz for an 80 MHz PPDU.
    The exact bandwidth of distributed bandwidth is TBD, and could be 20 MHz, 40 MHz or both.
    Y
    N
    A

## Slide 10: Straw Poll #3
Do you agree to include the following into the 11bn SFD?
  11bn defines distributed tone plan when there is puncturing.
    Y
    N
    A

## Slide 11
https://mentor.ieee.org/802.11/dcn/23/11-23-2020-00-00bn-high-level-perspective-on-distributed-tone-ru-for-11bn.pptx
https://mentor.ieee.org/802.11/dcn/23/11-23-2021-00-00bn-principle-and-methodology-for-dru-tone-plan-design.pptx
https://mentor.ieee.org/802.11/dcn/23/11-23-1919-00-00bn-dru-proposal.pptx
References