## Slide 1: Flexible Control frames
Date: 2024-01-11
Authors:
Mar 2024
Notes: September 2012

## Slide 2: Introduction
QoS/HT Control carry control info. in MAC header of MPDUs
  QoS Control: Limited changes over the years; limited in size/functionality
  HT-Control: Several variants defined, last being A-Control in 11ax
    A-Control design enabled forward compatibility and has been used since then
      To deliver a variety of control information between two STAs and,
      To deliver certain cross link information between two EHT MLDs
Limitations of HT/QoS Control fields
  HT Control field is subject to several restrictions
    Size is 4 octets. can only be present in QoS Data/Null/MGMT,
    Cannot be carried in Control frames
  QoS Control is subject to similar restrictions
    Size is 2 octets, can only be present in QoS Data/Null,
    Cannot be carried in Control frames
Mar 2024

## Slide 3: Problem Statement And Proposal
Absence of control frames that act as a feedback container will be particularly problematic for UHR since
  Target KPIs (low latency, high reliability, etc.) need fast and reliable mechanisms to deliver control feedback information
Proposal: Deliver feedback information in (certain) control frames
  Efficient delivery of information for a variety of mechanisms such as
    power mgmt., coexistence, etc.
    E.g., by including a Control Feedback field in these Control frames
Target: Covering main control frames for MU/SU sequences
  Initial Control Frame (ICF)–Initiate TXOP/sequence (e.g., RTS-like)
  Initial Control Resp. (ICR)–Confirm TXOP/sequence (e.g., CTS-like)
  Control Resp. Frame (CRF)–Immediate response frame (e.g., BA-like)
      Subcase: Unsolicited CRF (e.g., delayed BA-like)

## Slide 4: Control Sequences: Baseline
The following control frames are widely used
  (MU) RTS/CTS frame used to initiate, protect and maintain TXOPs
    Almost always sent in non-HT (dup) PPDU format
    Other Trigger variants can be sent by an AP as an ICF as well
  BAR frames used in a variety of locations within the TXOP
    Mostly sent in non-HT (dup) PPDU format; but also sent as part of an A-MPDU
  (M-)BA/Ack frames used to acknowledge RXed (A-)MPDUs & (MU-)BAR frames
    Mostly sent in non-HT (dup) PPDU format; but also sent as part of an A-MPDU
But do not contain control feedback* other than the following
  Bandwidth information in the Service field (RTS/CTS/BAR/BA/Ack) and
  Receive status of soliciting MPDUs (Ack, BA, etc.)
*Control Wrapper frames may carry HT Control, but have limited flexibility, increased parsing complexity, and are disallowed since 11ax; QoS Null/Data aggregation allows HT/QoS Control but also has limitations, e.g., can’t be sent in non-HT format, added overhead, limited flexibility, etc.
RTS
backoff
AP
STA 1
MU sequence
STA 2
RTS
CTS
CTS
Data
BA
BA
MU RTS
MU RTS
CTS
CTS
Data + Trigger
BA+BSR
BA+BSR
Data
Data
Basic
Basic
M-BA
M-BA
SU sequence

## Slide 5: Control Feedback Candidates
Possible candidates for ICF/ICR (rely on legacy control frames):
  RTS/CTS: Used by both AP & non-AP STAs to protect SU/MU exchanges
    Issue: RTS/CTS frames sent in non-HT (dup) PPDU; format change likely to impact legacy behavior
  MU RTS/CTS: Used by AP to protect MU/SU exchanges, and initiate eMLSR sequences
    Note: Other Trigger variants solicit TB PPDUs, which carry QoS Null/Data;
    Possible Issue: Trigger frames can only be generated by AP; not allowed for non-AP STAs
  BAR/BA frames: Used by AP & STA to reset BA scoreboards and advance BA windows
    Possible Issue: No NAV reset properties when used as ICF/ICR;
Possible candidates for CRF (rely on legacy control frames):
  Ack/BA/M-BA: Used by both AP and non-AP STAs to acknowledge reception of (A-)MPDUs
    Possible issue: format change for certain formats likely to impact legacy behavior
Alternative: Define a new Control frame that contains Control Feedback
  Possible but less preferred due to added complexity design; and
  Possible loss of existing functionalities
ICF
backoff
AP
STA 1
MU sequence
STA 2
ICF
ICR
ICR
Data
CRF
CRF
ICF
ICF
ICR
ICR
Data + Trigger
BA+BSR
BA+BSR
Data
Data
ICF
ICF
CRF
CRF
SU sequence

## Slide 6: Frame Candidates: Down Selection
ICF: Trigger frames and BAR frames
  Trigger frames today cover UL TB (MU), DL MU and UL SU operation initiated by AP
  BAR frame covers DL/UL SU TXOP/sequences initiated by AP and STA
ICR: Multi-STA/C-BlockAck frame
  Covers responding to BAR frames and maybe to an MU RTS Trigger
    Unless we want to define a new flexible CTS frame
CRF: Multi-STA/C-BlockAck frame
  Covers responses in multiple acknowledgment & multiple STAs contexts
  Can also be sent as a response that only contains Control Feedback (ICR)
ICF
backoff
AP
STA 1
MU sequence
STA 2
ICF
ICR
ICR
Data
CRF
CRF
ICF
ICF
ICR
ICR
Data + Trigger
BA+BSR
BA+BSR
Data
Data
ICF
ICF
CRF
CRF
SU sequence

## Slide 7: Flexible Control Frames: Criteria
Proposal is to target a design that provides
  Backwards compatibility and legacy interoperation
    Re-use commonly used existing frames that are legacy compliant
  Flexibility in feedback control delivery
    Native support for variable length feedback control
  Support for existing functionalities wherever appropriate
    BSR, BQR, OM Control, UPH, AAR, CAS control, etc.
  Processing time for resource intensive mechanisms
    Inherit MAC padding functionalities from Trigger frame design
  Secure control feedback exchange
    Ensure integrity of the exchanged information

## Slide 8: Flexible Control Frames: Formats
Octets: | 2 | 2 | 6 | 6 | 2 | variable | variable | variable | 4
 | Frame Control | Duration | RA | TA | BA Control | BA Information | Control Feedback | Padding | FCS
 | Frame Control | Duration | RA | TA | Common Info | User Info List | Padding | FCS
Octets: | 2 | 2 | 6 | 6 | 8 or more | variable | variable | 4
Octets: | 2 | 2 | 6 | 6 | 2 | variable | variable | variable | 4
 | Frame Control | Duration | RA | TA | BAR Control | BAR Information | Control Feedback | Padding | FCS
Trigger frame
BAR frame
BA frame
Special User Info field
0 or 5
User Info field 1
5 or more
User Info field 2
5 or more
Control Feedback
variable
…

## Slide 9: Conclusions
The inclusion of the Control Feedback field in
  M-BA frame, Trigger frame, and BAR frames
Takes care of all cases where feedback is needed
  Initiating control frame that solicits an immediate response,
  Control response frame,
  Unsolicited control frame
Flexible control design can also
  Rely on new control frame formats, however this requires more work and probably not much benefits w.r.t. using above- mentioned control frames
    Especially considering that we will be losing legacy frame functionalities
  Rely on other control frames as well, however the benefits of using other control frames are negligible when considering the added complexity

## Slide 10: appendix

## Slide 11: Control Feedback field
Follow similar design as A-Control or IEs
  For example (one or more of the following)
    Length indicates the length of the Control Feedback field
      Or if multiple CFUs are allowed then the length of each of these
    A Control Feedback ID which identifies the Control Feedback Unit
Control Feedback Unit 1 | CFU 2 | CFU 3 | … | Padding
Control ID | Length | Control Information