## Slide 1: TXOP Level Pre-emption for Low Latency Application
Date: 2024-01-10
Authors:

## Slide 2: Introduction
Pre-emption was discussed in [1] as a general solution to support low latency application in different scenarios [2].
In this document, we will further discuss how this technique can be used in the UL SU TXOP scenario and how to send LL PPDU after pre-emption

## Slide 3: Recap - General solution for case A and case B [1] (Event-based or periodic LL traffic with jitters) Pre-emption in DL TXOP case
Divide the large PPDU into small PPDUs with maximum length limitation and time gaps to enable pre-emption opportunity for low latency (LL) transmitter
One or more LL transmitters can send common pre-emption request (PR) (similar to CTS) during the time gaps when the preemption is allowed
  The time gap allowed for preemption is indicated in the PPDU preceding the time gap.
  Shorter xIFS () channel access will be used for the LL transmitter () to send common PR. <
  Benefit: This avoids reserving time slot periodically within TXOP for LL traffic
  3. LL packet transmission may be initiated by the AP after the reception of the common PR
  AP can trigger the LL STAs to send LL packet. e.g., Sending NFRP to get the LL buffer status report, then trigger the LL data transmission
January 2024

## Slide 4: Pre-emption in UL SU TXOP case
Divide the large UL SU PPDU into small PPDUs with maximum length limitation and time gaps to enable pre-emption opportunity for the AP
AP can send BA with PR or other ways to indicate the pre-emption request when the pre-emption is allowed
  3. LL packet transmission may be initiated by the AP after the transmission of the PR

## Slide 5: How to enable LL PPDUs after pre-emption (Event-based or periodic LL traffic with jitters)
PR + NFRP + NFR + TF + LL PPDU [3]
PR + TF + UORA for LL PPDUs
PR + EDCA for LL PPDUs [4]
PR + basic TF + BSR + TF + LL PPDUs

## Slide 6: Summary
Pre-emption can provide bounded latency while keeping low performance impact to the high throughput traffic.
Further consideration:
  xIFS time
  Pre-emption Request frame
  How to send LL packet after PR frame
  Further overhead reduction

## Slide 7: References
[1] 11-23-0092r0, “Preemption”
[2] 11-23-0018r1, “Low latency support in UHR”
[3] 11-23-1229r1, “Preemption-for-low-latency-application-follow-up”
[4] 11-23-1886r0, “Preemption-techniques-to-meet-low-latency-ll-targets”

## Slide 8: SP
Do you agree to define a mechanism in 11bn for a TXOP holder to allow a STA associated with the TXOP holder to preempt the TXOP holder's frame exchange sequence for low latency traffic delivery
  NOTE: The TXOP holder can be an AP or a non-AP STA and the policy for TXOP holder allowing pre-emption is TBD