## Slide 1: Unequal Modulation in MIMO TxBF in 11bn
Date: 2024-01-15
Authors:
Name | Affiliations | email
Alice Chen | Qualcomm | alicel@qti.qualcomm.com
Bin Tian |  | 
Sameer Vermani |  | 
Akansh Jain |  | 

## Slide 2: Introduction
In MIMO beamformed channel, channel quality difference among the eigen modes makes equal MCS across multiple spatial streams sub-optimal
Different proposals were brought up to use different modulations or MCSs in MIMO TxBF, with two flavors
  Unequal MCS: With separate encoding of each spatial stream, choose an MCS matched to each spatial stream’s SINR [1-2]
  Unequal modulation: With joint coding across streams, choose a QAM modulation matched to each spatial stream’s SINR [3]
In this presentation, we discuss the high level differences between the unequal MCS and unequal modulation and show the potential RvR gain of unequal modulation

## Slide 3: Per Stream SNR Gap in 2x2 Channel
Two eigen channels have median SNR gaps of 10.4dB in DNLoS and 11.5dB in BLoS
Equal MCS in TxBF is not optimal
Per stream SNR gap for other antenna configurations are shown in appendix

## Slide 4: Unequal Modulation Vs Unequal MCS
Unequal MCS: 2 potential methods of implementation
  Method 1: MAC passes down multiple PSDUs to PHY, one PSDU for each stream. Difficult to make them same length
    Gain may go away with the inefficiency introduced from padding
  Method 2: MAC passes down only 1 PSDU to PHY. Need to use an encoder parser to split PSDU information bit among multiple encoders
    There are many different ratios for MCS combinations!
Unequal modulation needs one PSDU and uses joint encoding
  Potentially better performance since the strong stream can help the weak stream in decoding.
We prefer the unequal modulation approach for multiple stream TxBF transmission

## Slide 5: Simulation Setup
20MHz, 2x2x2ss
DNLoS & BLoS
TxBF (using SVD) with equal power allocation to all spatial streams
Linear receiver
Candidate code rates: 1/2, 2/3, 3/4, 5/6
Candidate QAM: from BPSK to 1kQAM
Genie per channel rate adaptation
Different schemes being compared
  Equal MCS with existing MCS
  Optimum Unequal QAM (any QAM combination for a code rate)
  Unequal QAM with existing MCS (both streams use existing MCS from MCS0-11)

## Slide 6: 2x2x2ss, DNLoS
Unequal modulation brings significant gain (up to 2.2dB) over wide range of SNR
With existing MCS only, unequal QAM doesn’t harvest all the potential gain
  At high SNR, unequal QAM uses rates 3/4 and 5/6, which already have good support in existing MCS
  At medium SNR, unequal QAM gain may be improved by adding new QAM and code rate combinations

## Slide 7: 2x2x2ss, BLoS
Similar observation in BLoS

## Slide 8: Summary
Proposed unequal modulation with joint encoding for multiple stream TxBF transmission to deal with per spatial stream channel quality imbalance
  Lower complexity and potential better gain compared to unequal MCS
Gain of unequal modulation may come from two sources
  Matching modulation to SINRs of different spatial streams
  Finer resolution of data rates from using unequal modulation in different spatial streams
Unequal modulation with existing MCS doesn’t harvest all the potential gain
  New QAM and code rate combinations may be added to better support unequal modulation

## Slide 9: SP1
Do you support to allow unequal modulation with same code rate and joint encoding across multiple spatial streams in TxBF transmission in 802.11bn?
Y
N
A

## Slide 10: Reference
11-22/1930r0, Layered QoS and multi-layer transmission
11-22/0060r2, Layered QoS and multi-layer transmission follow-up
IEEE 802.11n-2009, IEEE Standard for Information technology-- Local and metropolitan area networks-- Specific requirements-- Part 11: Wireless LAN Medium Access Control (MAC)and Physical Layer (PHY) Specifications Amendment 5: Enhancements for Higher Throughput

## Slide 11: Appendix

## Slide 12: Per Stream SNR Gaps in 3x3
In 3x3, eigen channels also have larger SNR gaps

## Slide 13: Per Stream SNR Gaps in 4x4
In 4x4, eigen channels also have larger SNR gaps