## Slide 1: Thoughts on Power Control for CSR
Date: 2024-01-12
Authors:

## Slide 2: Introduction
Coordinated Spatial Reuse (CSR) is a technology being considered for UHR
In [1-2], authors show gains of CSR
In [3], authors show gains of CSR and CBF
In [4], authors proposed a sharing AP to control the transmit power of shared APs
In [5], authors proposed a non-AP STA to measure neighboring APs’ signal level (e.g. RSSI)
In this contribution, we share our concern on transmit power control for CSR

## Slide 3: Discussions (1/3)
A CSR scheme with power control has several problems
Performance
  It may not perform better than a scheme without power control depending on the power control algorithm
  Also optimizing transmit power control is not simple
  For example,
    If a sharing AP uses fixed power while a shared AP reduces its power to maintain MCS level at the sharing AP (fairness constraint), then the sharing AP’s performance could be bad as interference from sharing AP could be too high
    If a joint power control algorithm is used (power control for both shared AP and sharing AP), then there could be a fairness issue

## Slide 4: Discussions (2/3)
Hidden node problem
  Even if it transmits a control frame to reserve a medium, OBSS STA or devices in power save may miss the control frame
  Results and discussions in [6, 7] show that the probability of successfully decoded preambles of OBSS is low due to multiple sources of transmissions
  If the actual transmission’s transmit power is low, then OBSS STA’s transmission may overlap in time
Limitation of PHY simulation
  In many simulations, authors assume the network is synchronized
  As discussed in [6, 7], due to multiple sources of transmissions, the network often becomes asynchronized, and thus the network already operates on an aggressive CCA level in a dense environment
  Thus, it is better to evaluate CSR using a network simulator

## Slide 5: Discussions (3/3)
Link Adaptation
  It complicates link adaptation due to varying signal and interference level
  It suffers from inaccuracy of RSSI measurements, e.g. ±3dB in class A device
Non-AP STA feedback
  Most power control algorithm requires knowing the interference level between non-AP STA and neighboring AP
  It makes a non-AP STA consume more power by measuring non-serving APs’ RSSI
  It is better to improve efficiency by a scheme not require feedback
  Note that a scheme without power control does not require a (periodic) report of non-AP STA measurement of neighboring BSS

## Slide 6: Conclusion
We have identified several problems in a CSR scheme with transmit power control
  Performance depends on power control algorithm which could be complex for optimization
  Creates hidden nodes
  Difficulty in link adaptation
  Makes non-AP STA to consume more power
Also, we have identified a limitation of PHY level simulation (network synchronization assumption) which has been done in many studies
It is recommended to study CSR more with system-level simulators with more realistic simulation scenarios such as in [8]

## Slide 7: References
[1] 11-23/1023r2, “Coordinated Spatial Reuse in a 4 AP Topology”
[2] 11-23/1037r0, “Performance of Coordinated Spatial Reuse”
[3] 11-23/776r1, “Performance of C-BF and C-SR”
[4] 11-23/1868r2, “Coordinated Spatial Reuse Design”
[5] 11-23/1917r0, “Coordinated Spatial Reuse”
[6] 11-15/367r0, “OBSS Preamble Detection”
[7] 11-14/1420r1, “The Impact of Preamble Error on MAC System Performance”
[8] 11-14/980r16, “TGax Simulation Scenarios”