## Slide 1: TXOP preemption in 11bn
Date: 2024-01-17
Authors:

## Slide 2: Introduction
In [1] - [4], we discussed TXOP preemption as a candidate feature of UHR to support low latency traffic.
In this document, we discuss further details of TXOP preemption in 11bn.

## Slide 3: Recap) TXOP Preemption – Possible Cases [1]
Case 1: UL TXOP preemption for DL LL traffic
Case 2: DL TXOP preemption for UL LL traffic
Case 3: UL TXOP preemption for UL LL traffic

## Slide 4: UL TXOP preemption for DL LL traffic
Assumption
  A non-AP STA is a TXOP holder.
  An AP is a TXOP responder, and the AP has buffered low latency traffic.
Issue
  When the non-AP STA does not allocate a time period using RDG to the AP, the AP cannot transmit its buffered low latency traffic before the end of the TXOP.
Potential solution
  The non-AP STA that is the TXOP holder may transmit a limited size of UL PPDU to the AP.
  The AP may request TXOP preemption in an immediate response frame (e.g., BA) to the TXOP holder and it can transmit DL low latency traffic.
    The recipient of the DL LL traffic can be either the TXOP holder or other non-AP STA(s)
  After transmitting the low latency frame, the AP transmits a frame indicating TXOP Preemption Release (e.g., a QoS Null frame with an A-Control field) to the TXOP holder.
  The TXOP holder can resume its transmission during the remaining TXOP.

## Slide 5: DL TXOP preemption for UL LL traffic
Assumption
  An AP is a TXOP holder.
  One or more non-AP STAs (TXOP responder or non-TXOP responder) has a buffered low latency frame.
Issue
  The AP is not aware of which non-AP STA has a buffered low latency frame.
  When and how the AP provides a preemption opportunity to a non-AP STA with low latency traffic is the issue to be addressed.
Potential solution
  A non-AP STA can preempt the TXOP using a shorter IFS (e.g., SIFS) to transmit the low latency frame while an AP transmits multiple PPDUs using a longer IFS (e.g., PIFS).
    A DL PPDU can include an indication of whether preemption is allowed after the DL PPDU.
    To avoid collision from multiple non-AP STAs, a Preemption Request frame (w/ unified frame format such as e.g., a simultaneous CTS frame in response to an MU-RTS Trigger frame, etc.) can be transmitted to request preemption for UL LL traffic
    The AP that receives a Preemption Request frame may transmit for UL LL traffic
      NFRP Trigger
      BSRP Trigger (w/, or w.o/ RA RUs)
      Basic Trigger
    Or the non-AP STA that transmitted the Preemption Request frame may do additional EDCA based channel access to transmit the UL LL traffic [5]

## Slide 6: Summary
For low latency frame transmission, TXOP preemption in UHR can be define with the followings.
  For a UL TXOP, an AP that is a TXOP responder may request TXOP preemption in an immediate acknowledgement frame (e.g., BA) to a non-AP STA that is a TXOP holder to transmit DL LL traffic.
  For a DL TXOP, a non-AP STA that is not a TXOP holder may transmit a Preemption Request frame to an AP that is a TXOP holder to transmit UL LL traffic.
    The Preemption Request frame can be defined as a unified frame format such as a CTS frame in response to an MU-RTS Trigger frame. The detailed frame format is TBD.
    The Preemption Request frame can be transmitted only if a received PPDU indicates preemption allowance.

## Slide 7: References
[1] IEEE 802.11-23/0018 Low latency support in UHR
[2] IEEE 802.11-23/0092 Preemption
[3] IEEE 802.11-23/1174 TXOP Preemption Follow-Up
[4] IEEE 802.11-23/1229r1 Preemption-for-low-latency-application-follow-up
[5] IEEE 802.11-23/1886r0 Preemption-techniques-to-meet-low-latency-ll-targets

## Slide 8: Straw Poll
Do you agree to define a mechanism in 11bn for a TXOP holder to allow a STA associated with the TXOP holder to preempt the TXOP holder's frame exchange sequence for low latency traffic delivery
  Note 1: The TXOP holder can be an AP or a non-AP STA
  Note 2: The policy for TXOP holder allowing preemption is TBD