## Slide 1: Some thoughts on the beamforming feedback
Name | Affilations | Address | Email
Xiaogang Chen | Spreadtrum Communications, USA | 2680 N 1st St. San Jose, CA. 95134 | Xiaogang.chen1@unisoc.com
Chunyu Hu |  |  | 
William Li |  |  | 
Date: 03/01/24

## Slide 2: Outline
Average SNR in the CBF (compressed beamforming feedback);
  Discussions on the order of average SNR in the CBF.
The potentials of CBF overhead reduction.
  Time domain correlation of CBFs.

## Slide 3: Average SNR in the CBF (1/2)
The average SNR in the CBF
is the 1st bit after MIMO control field in the CBF frame;
is a time demanding processing if it is generated strictly following the spec;
  SVD + Compression across all tones are challenging to achieve especially for wider BW (wider BW has the same timing constraint as narrower BW);
  Timing budget is roughly: SIFS + PHY Preamble – delay_from_multiple_sources – MAC_timing_advance;
The average SNR in the CBF may not be reliable:
Bfee cut the corner to save area given the timing constraint;
Bfer cannot rely on this information for rate adaptation;
No certification on the accuracy has been conducted.
11bn has adopted the unequal modulation which may leverage the average SNR for better rate adaptation.
Protocol should provide the flexibility for the Bfee to generate accurate average SNR.
Finish processing all the tones

## Slide 4: Average SNR in the CBF (2/2)
Swapping the order of average SNR and Bfing matrix will mostly solve the issue.
Most of the overhead in the CBF is the compressed Bfing matrix;
A low rate feedback will gain more time for the CBF generation: SIFS + Pre-EHT + Data symbol (a few) – delay_from_multiple_sources – MAC_timing_advance.
  1572Bytes (4x2,80MHz,Ng=4,codebook(6,4)) can fill in several data symbols before Average SNR is generated.
  PHY doesn’t need to process all tones before sending data to MAC.
Finish processing all the tones

## Slide 5: The potentials of sounding overhead reduction
The current sounding procedure is controlled by Bfer;
  Bfer cannot predict the channel variation on Bfee side, so Bfer usually poll the Bfee periodically to avoid the Bfing matrix is outdated.
  Bfee must send back the CBF as long as the Bfee is polled.
  In reality, the channel maybe stable for a much longer period than the periodicity of the Bfee is polled.
    In this case the CBF from Bfee is mostly redundant.
The next few slides shows the time domain correlation of the CBF by OTA capture.
Measurement setup:
  80MHz AP as BFer -> 80MHz STA as Bfee;
  Antenna profile: 4Tx -> 2Rx;
  CBF is SU feedback with 2 columns.
  Bfer poll Bfee every 100ms for CBF.
    Note that not every CBF can be captured.
  CBF is recovered by post process and time domain correlation for tone k is calculated as: Corr(k) = abs(V1t1 (k)’ * V1t2 (k));
    250 tone in each CBF frame for 80MHz.
    Ng =4, codebook {6,4} for SU.
    Mean(Corr(k)) over k=1,2,…250 is plotted.

## Slide 6: The time domain correlation of CBF
Watching movie (left):
  The correlation is almost 1 all the time until body moving (~3 fts to BFee).
Walk around (middle):
  The correlation fluctuates and reflect channel variation due to walking, and goes back to ~1 when stop (~8 fts to BFee).
Holding /playing smart phone(right. Very challenging case to maintain stable channel)
  The correlation change significantly because the hands are immediate proximit to Bfee, but still goes back to ~1 for half of the whole duration.
The CBFs that can be saved are the instances that time domain correlation approximately equal to 1.
  Challenge is to reliably detect CBF variation by Bfee with reasonable buffer and computation.

## Slide 7: CBF variation detection by Bfee (1/2)
Bfee doesn’t need to save all the tones of the previous CBF to detect the variation.
Instead, only a few tones need to be used for reliable variation detection.
  The variance of “the time domain correlation from different tones” is very low. i.e. the samples of correlation from a few tones can well represent the channel variation across the whole band.
    E.g if the time domain correlation is determined as 0.99 by observing 5 tones, then all the 250 tones will have a time domain correlation equal to 0.99 (with a very high chance).
  Variance = Var (Corr_set ), where
    Corr_set = {correlation(cbf_current_tone_0, cbf_previous_tone_0),
          correlation(cbf_current_tone_1, cbf_previous_tone_1),
          correlation(cbf_current_tone_2, cbf_previous_tone_2),
          …….
          correlation(cbf_current_tone_N, cbf_previous_tone_N}.

## Slide 8: CBF variation detection by Bfee (2/2)
FFT (Corr_set), which visualize the variance, is shown in right figure.
The large low frequency component near DC means the values in Corr_set are almost constant across the whole band.
Channel variation detection based on a few tone significantly reduce the memory and computational complexity in the Bfee.

## Slide 9: How much can be saved by eliminating CBF in stable channel condition?
1572 Bytes need to be carried in CBF for the CBF profiled measured (4x2, 80MHz, ng=4, cb{6,4});
Relatively low rate is used to carry CBF as shown in the figure;
  12 Bfees are tracked including 11ac/11ax/11be STAs.
  >90% Bfee use rate < 50Mbps.
  Minimum rate is 6Mbps. Mean is 33Mbps.
1572 Bytes takes
  ~252 us if 50Mbps is used;
  ~524 us if 24Mbps is used;
  ~2 ms if 6Mbps is used.
Given the feedback frequency and number of users associated, the saving on the medium time is quite considerable.
Statistics of the rate used for CBF
Data rate (Mbps)

## Slide 10: Gap in the protocol for overhead reduction
Need a mechanism to enable the Bfee informing the Bfer no CBF report is needed if no channel variation is detected.
Bfer should be able to force the Bfee sending back CBF in case Bfer failed to receive a feedback.

## Slide 11: Summary
Consider swapping the Average SNR and the beamforming matrix in the CBF.
Beside SU,MU and CQI, consider adding a new feedback type as “no feedback is required”, to enable the Bfee informing the Bfer to use the previous Bfing matrix instead of sending a new CBF.

## Slide 12: SP1
Do you agree that the compressed beamforming matrix is the first subfield immediately following the MIMO control field in the compressed beamforming frame?

## Slide 13: SP2
Do you agree to add a new feedback type in the MIMO control field to indicate no beamforming information is reported in the current compressed beamforming frame?