## Slide 1: Discussion on A-PPDU follow-up
Date: 2024-02-29
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 
David Xun Yang |  |  |  | 
Yan Xin |  |  |  | 
Stephen McCann |  |  |  | 

## Slide 2: Recap
In [1], three preferred modes are proposed:
  Other modes, for example, EHT+UHR, need further study, depending on the benefits of UHR features, when compared with a standalone EHT PPDU.
  Opt (1) and (d) are proposed because large bandwidth OFDMA is optional for a non-EHT HE non-AP STA, and seldom applied.
HE PPDU
HE PPDU (by UHR STA)
80 MHz
80 MHz
(1)
HE PPDU
UHR PPDU
160 MHz
160 MHz
(a)
HE PPDU
HE PPDU (by UHR STA)
UHR PPDU
80 MHz
80 MHz
160 MHz
(d)

## Slide 3: A-PPDU Q&A clarifications
Q1: HE MU PPDU has to be used for PPDU alignment in DL. The use case is limited.
Below are the replies:
  For HE 80 + HE 80, an HE SU PPDU can be used. If Only two users are scheduled, this can be frequently used.
  For HE + UHR, HE MU PPDU is needed.
    Case 1: HE MU PPDU is transmitted to two or more users.
    Case 2: HE MU PPDU is transmitted to one user (optional feature).
    Case 3: HE MU PPDU is transmitted to one user and one dummy user.
      Some spectrum is wasted, but can earn more spectrum back.
  This can also be frequently used.
Q2: HE STAs are two generations away.
Below are the replies:
  Legacy devices are used quite often, especially in home scenario.
  There is report forecasting $7.96 billion of Wi-Fi 6E devices market size by 2030 [2].
  Wi-Fi 6 and Wi-Fi 6E devices keep increasing until 2025 (no data beyond that) [3].

## Slide 4: Summary
In this contribution, some questions from previous presentations are further clarified.
Regarding the benefits, the cases of HE 80 + HE 80 and HE 160 + UHR 160 can double the Tput. The case of HE 80 + HE 80 + UHR 160 can result in a four times Tput gain. They can also reduce the latency.
A-PPDU can be used together with dynamic subband operation (DSO) or subband selective transmission (SST).

## Slide 5: Straw Poll #1
Do you agree to include the following into the 11bn SFD?
  11bn defines frequency domain aggregation of aggregated PPDUs. An aggregated PPDU consists of multiple PPDUs.
    The PPDU format combinations include HE PPDU, other PPDUs are TBD.
    The number of PPDUs is TBD.
    Y
    N
    A

## Slide 6: Straw Poll #2
Do you agree to include the following into the 11bn SFD?
  11bn defines frequency domain aggregation of an 80 MHz HE PPDU and 80 MHz HE PPDU.
    Y
    N
    A

## Slide 7: Straw Poll #3
Do you agree to include the following into the 11bn SFD?
  11bn defines frequency domain aggregation of a 160 MHz HE PPDU and 160 MHz UHR PPDU.
    Y
    N
    A

## Slide 8: Straw Poll #4
Do you agree to include the following into the 11bn SFD?
  11bn defines frequency domain aggregation of an 80 MHz HE PPDU, 80 MHz HE PPDU and 160 MHz UHR PPDU.
    Y
    N
    A

## Slide 9
https://mentor.ieee.org/802.11/dcn/23/11-23-1865-01-00bn-discussion-on-sst-and-a-ppdu.pptx
https://www.industryarc.com/Research/wifi-6E-devices-market-research-800237#:~:text=Wi%2DFi%206E%20Devices%20Market%20size%20is%20estimated%20to%20reach,devices%20that%20require%20wireless%20connectivity
https://www.wi-fi.org/beacon/the-beacon/wi-fi-by-the-numbers-technology-momentum-in-2023
References