## Slide 1: Further Considerations on Coordinated TDMA
Date: 2024-02-28
Authors:

## Slide 2: Introduction
Coordinated TDMA (C-TDMA), due to its simplicity and similarity to Triggered TXOP Sharing (TXS) procedure, has been a favorable approach for multi-AP coordination in 11bn [1] – [9].
One of the main design challenges of C-TDMA over the TXS procedure is to regulate multiple BSSs. When the sharing AP and the shared APs are communicating based on the C-TDMA procedure, associated STAs should also be aware of the signaling between APs.
In cases where STAs are hidden to sharing/shared APs, the STAs may not hear parts of the signaling between APs and may cause the C-TDMA procedure work inefficiently.
In this contribution, we consider some of the problems caused by STAs that are hidden to shared APs and propose solutions to overcome inefficiency in the C-TDMA procedure.

## Slide 3: Recap: TXOP Return by Shared AP
As presented in [2], a shared AP (e.g., AP2) may want to return the TXOP to the sharing AP (e.g., AP1) before the end of a shared TXOP.
On hearing the CF-End frame, a non-associated STA (e.g., STA1) may reset its basic NAV. As such, the STA can respond to frames transmitted by the sharing AP.
(Sharing AP)
(Shared AP)
(Can hear AP2)
NAV is reset
NAV is set by hearing AP2

## Slide 4: TXOP Return by Shared AP
When AP2 and its associated STAs are communicating in the TXOP allocated to AP2, a non-assoc. STA (e.g., STA1) may not be able to hear AP2 if they are far from each other.
When AP2 returns the TXOP to AP1 before the end of the shared TXOP, STA1 may not hear the CF-End frame and may not reset its basic NAV. Thus, STA1 may not respond to frames from AP1.
(Sharing AP)
(Shared AP)
(Cannot hear AP2)
NAV is not reset
NAV is set by hearing STA2

## Slide 5: Informing STAs hidden from Shared AP (1)
If AP2 returns the TXOP before the end of a shared TXOP, AP1 may transmit a CF-End frame before transmitting a frame to STA1.
  For example, the sharing AP hears a trigger frame from a shared AP during the shared TXOP and transmits a CF-End frame if AP2 returns the TXOP before the end of the shared TXOP  Suitable for 11bn and legacy STAs
(Sharing AP)
(Shared AP)
NAV is reset
(Cannot hear AP2)
NAV is set by hearing STA2

## Slide 6: Informing STAs hidden from Shared AP (2)
Before returning TXOP to AP1 before the end of a shared TXOP, AP2 may transmit a frame to trigger its associated STAs to transmit CF-End frames.
  For example, if the associated STA of the shared AP informs the shared AP that it has no buffered data for transmission, the shared AP transmits a trigger frame to the associated STA to trigger CF-End frame transmission  Suitable for 11bn and legacy STAs
(Sharing AP)
(Shared AP)
NAV is reset
(Cannot hear AP2)
NAV is set by hearing STA2

## Slide 7: Ignoring basic NAV during TXOP sharing
Sharing AP (e.g., AP1) may transmit an MU-RTS TXS TF that includes an indication of whether a STA is permitted to ignore its basic NAV if set during the shared TXOP.
  In such a case, AP1’s associated STA (e.g., STA1) ignores its basic NAV, and responds to frames sent by AP1 during the shared TXOP  Suitable only for 11bn STAs
(Sharing AP)
(Shared AP)
NAV is ignored
Indic. to ignore NAV
(Cannot hear AP2)
NAV is set by hearing STA2

## Slide 8: Conclusion
In this contribution, we considered a problem caused by STAs that are hidden to shared APs during a C-TDMA procedure.
We proposed three solutions to overcome inefficiency in the C-TDMA procedure:
    Informing STAs hidden from shared AP via either the sharing AP or the associated STAs
    (can be adopted for both 11bn and legacy STAs)
    Ignoring basic NAV during TXOP sharing
    (can be adopted for only 11bn STAs)
For an efficient implementation of the C-TDMA procedure, further investigation is needed to determine signaling between sharing/shared APs and STAs.

## Slide 9: References
[1] 23/0041r0, Considerations on Coordinated TDMA
[2] 23/0739r1, Follow-up on Coordinated TDMA (C-TDMA)
[3] 23/0249r1, Extended TXOP Sharing
[4] 23/0261r0, TDMA for WiFi-8
[5] 23/1085r0, Thoughts on Coordinated TDMA
[6] 23/1910r1, Coordinated TDMA (Follow up)
[7] 23/1912r0, Coordinated TDMA Procedure
[8] 23/1895r2, C-TDMA Frame Sequence
[9] 24/0093r1, NAV Setting for Coordinated TDMA