## Slide 1: TXOP Sharing for C-BF transmission
Date: 2024-03-xx
Authors:

## Slide 2: Introduction
In the contribution [1]-[2], Coordinated Beamforming (C-BF) shows significant gain as a candidate technology in 11bn to improve the BSS throughput.
TXOP sharing among multiple APs (i.e., a sharing AP and a shared AP) has been heavily discussed and likely agreed for multi-AP coordination, especially for C-TDMA.
  A modified MU-RTS TXS Trigger frame can be re-used for an initial control frame triggering C-TDMA operation.
In this document, we discuss TXOP sharing mechanism for C-BF as a unified solution for multi-AP coordination features in 11bn.
  A sharing AP (C-BF initiator) can share its TXOP with a shared AP (C-BF responder) by transmitting a MAC control frame (e.g., MU-RTS TXS Trigger frame) for C-BF transmission.

## Slide 3: Recap) Multi-AP C-TDMA MAC procedure
Discussion on extending the 11be Triggered TXOP Sharing (TXS) framework to Coordinated Time Division Multiple Access (C-TDMA) in 11bn
  An MU-RTS TXS Trigger frame can be used for a sharing AP to allocate a time duration to a single shared AP.
Potential signaling sequence
  A sharing AP transmits an MU-RTS TXS Trigger frame to a shared AP for C-TDMA time allocation.
  The shared AP responds with a CTS frame in response to the MU-RTS TXS Trigger frame.
  The shared AP can do frame exchange with its associated non-AP STAs during the allocation time indicated in the MU-RTS TXS Trigger frame.

## Slide 4: Recap) Multi-AP Coordinated Beamforming (C-BF)
M-AP C-BF is to form spatial nulls using the channel state information (CSI) to allow concurrent transmissions from neighboring APs.
  In the figure, AP1 and AP2 transmit frames to each associated STA (e.g., AP1 to STA1-1 and STA1-2, and AP2 to STA2-1 and STA2-2) concurrently by forming spatial nulls (e.g., AP1 to STA2-1 and STA2-2, and AP2 to STA1-1 and STA1-2).
A sharing AP and a shared AP can obtain the CSI/nulling matrix for C-BF by multi-AP sounding procedure in advance.
  CSI from the sharing AP to its associated non-AP STAs
  CSI from the sharing AP to OBSS non-AP STAs that are associated with the shared AP
  CSI from the shared AP to non-AP STAs associated with the sharing AP
A sharing AP can initiate C-BF transmission by sharing its TXOP with a shared AP if the CSI for C-BF is available.

## Slide 5: M-AP TXOP sharing for C-BF transmission
Triggered TXOP sharing among multiple APs can be extended to support multiple APs’ C-BF operation.
If the CSI for C-BF is available, a sharing AP can determine candidate shared AP(s) and OBSS non-AP STA(s) associated with the shared AP(s) for C-BF transmission.
A sharing AP as a TXOP holder can share its TXOP with a shared AP by transmitting a MAC control frame (e.g., modified MU-RTS TXS Trigger frame or a new MAC control frame) that triggers C-BF transmission.
  The MAC control frame can indicate an identifier of OBSS STA to be nulled by the sharing AP for C-BF transmission, and an identifier of In-BSS STA that is a recipient of the C-BF transmission from the sharing AP.
After the MAC control frame, the sharing AP and the shared AP(s) can transmit a DL PPDU concurrently to its associated non-AP STA(s) that is indicated in the MAC control frame by using C-BF transmission.
For this, we can have two options.
  See the next two slides

## Slide 6: M-AP TXOP sharing for C-BF transmission (continued)
Option 1: Shared AP confirming C-BF Tx by the CTS frame
  MAC control frame (sharing AP)  CTS frame (shared AP)  C-BF Tx (sharing AP & shared AP)
  A shared AP’s identifier (e.g., BSS color, BSSID, etc.) is indicated in the MAC control frame (e.g., MU-RTS TXS Trigger frame) triggering C-BF transmission.
  The MAC control frame indicates OBSS non-AP STA’s identifier(s) (e.g., MAC address) to be nulled by the sharing AP for C-BF transmission.
  The shared AP responds with a CTS frame in response to the MAC control frame when the following conditions are met.
    The shared AP has the CSI/nulling matrix to the In-BSS STA(s),
    The medium is idle, and
    The shared AP has pending traffic to its associated STA(s) that is indicated in the MAC control frame.
  The shared AP may transmit a DL PPDU by using C-BF to its associated STA(s) indicated in the MAC control frame (e.g., OBSS non-AP STA) SIFS after the CTS frame.
  If the CTS frame is received from the shared AP, the sharing AP may transmit a DL PPDU to its associated non-AP STA(s) (e.g., In-BSS STA(s)) by using C-BF transmission SIFS after the CTS frame.
    Otherwise, the sharing AP may transmit a DL PPDU to the In-BSS STA(s) (or any other associated non-AP STA) PIFS after the MAC control frame.
  To solicit an acknowledgement frame (e.g., Ack, BA, etc.) after the C-BF PPDU, a BAR frame can be transmitted in a separate TXOP or during an allocation time allocated by the sharing AP in the same TXOP.

## Slide 7: M-AP TXOP sharing for C-BF transmission (continued)
Option 2: Shared AP’s C-BF Tx with no confirmation
  A shared AP’s identifier is not indicated a MAC control frame (e.g., MU-RTS TXS Trigger frame) triggering C-BF transmission.
  The MAC control frame indicates In-BSS non-AP STA’s identifier(s), and OBSS non-AP STA’s identifier(s) (e.g., MAC address) to be nulled by the sharing AP for C-BF transmission.
  An AP operating on the same channel listens to the MAC control frame and figure out whether it can take advantage for C-BF transmission to its associated STAs.
  A shared AP may transmit a PPDU by using C-BF to the indicated non-AP STA(s) SIFS after the MAC control frame when the following conditions are met.
    The MAC control frame indicates its associated non-AP STA’s identifier(s),
    The shared AP has the CSI/nulling matrix to the In-BSS STA(s),
    The medium is idle, and
    The shared AP has pending traffic to its associated STA(s) that is indicated in the MAC control frame.
  After transmitting a C-BF PPDU, the shared AP may transmit a frame (e.g., BAR, MU-BAR, etc.) soliciting the corresponding acknowledgement frame in a separate TXOP.

## Slide 8: MAC Control frame triggering C-BF transmission
A MAC control frame triggering C-BF transmission (e.g., a modified MU-RTS TXS Trigger frame, etc.) can include the following parameters.
  M-AP TXS type
    E.g., 0: C-BF, 1: C-TDMA, and 2: C-SR, etc. Set to 0 for C-BF Tx indication.
  OBSS STA ID
    e.g., AID or (partial) MAC address of the non-AP STA that is associated with the shared AP, etc.
    The OBSS STA to be nulled by the sharing AP for C-BF Tx and that is a target recipient of the C-BF transmission from the shared AP
  In-BSS STA ID
    e.g., an AID or a partial MAC address of the non-AP STA that is associated with the sharing AP, etc.
    In-BSS STA is a target recipient of the C-BF transmission from the sharing AP.
    Note. The shared AP can form the spatial null to the In-BSS STA when transmitting a PPDU using C-BF to its associated STA if the CSI/nulling matrix from the shared AP to the In-BSS STA is available.
  Shared AP ID (if the option 1 is applied in the previous slide)
    e.g., BSS color of the shared AP, or LSB of the shared AP’s BSSID, etc.
    It can be included in the RA field or the frame body of the MAC control frame.
  PPDU length for C-BF transmission
    Specifies the PPDU length that is used for C-BF transmission SIFS after the MAC control frame (or SIFS after the CTS frame).

## Slide 9: Multiple C-BF PPDU transmission
A MAC control frame triggering C-BF transmission triggers a single C-BF PPDU transmission concurrently from a sharing AP and one or more shared APs.
More than one MAC control frame can be transmitted in a TXOP to trigger multiple C-BF PPDU transmission.
After transmitting the C-BF PPDU to its associated STA(s), the shared AP(s) may transmit a BAR frame (or MU-BAR frame) to solicit an acknowledgement frame from the associated STA(s) in a separate TXOP.

## Slide 10: Summary
TXOP sharing can be used for C-BF transmission as a unified solution to support multi-AP coordination feature in 11bn.
A MAC control frame triggering C-BF transmission (e.g, a modified MU-RTS TXS Trigger frame) can indicate OBSS STA’s ID, C-BF PPDU length, In-BSS STA’s ID, and optional shared AP’s ID.
C-BF transmission can be done opportunistically if the shared AP senses the medium idle and if the shared AP has pending traffic for its associated non-AP STA indicated in the MAC control frame.
A MAC control frame can trigger a single C-BF PPDU transmission, and more than one C-BF PPDU transmission can be triggered by multiple MAC control frames sent by a sharing AP within a TXOP.

## Slide 11: References
[1] 11-23/776, Performance of C-BF and C-SR
[2] 11-23/1193, Nulling Performance of Coordinated Beamforming