## Slide 1: Seamless Roaming within a Mobility Domain – Follow Up
Date: 2024-02-20
Authors:

## Slide 2: Introduction
UHR is aiming to provide improved support for roaming. Several UHR presentations have covered seamless and improved roaming [1-7]. In [1] we presented a proposal for seamless roaming within a mobility domain.
In this presentation, we expand on [1] and share further details on:
  Association to an SMD (Seamless Mobility Domain)
  FT and Seamless Mobility Domains
  Single secure association with an SMD
  SMD entity and its functions
  Discovery of an SMD
  Two phase roaming approach
    Roaming reparation phase and roaming execution phase
  Seamless roaming e2e call flows

## Slide 3: Association to an SMD (1)
In [1] we proposed an architecture where a non-AP MLD establishes an association with an SMD (Seamless Mobility Domain) through an AP MLD.
SMD conceptually is like the FT mobility domain – SMD defines a set of AP MLDs within the same ESS that coordinate with each other to support seamless roaming between themselves, and that are identified by an SMD MAC Address.
An ESS can have one or more SMDs configured covering its AP MLDs.

## Slide 4: Association to an SMD (2)
Initial association to an SMD establishes security context (PMKSA, PTKSA) which apply across all AP MLDs of the SMD
  Similar to FT initial mobility domain association (REVmeD5.0 clause 13.4) where the security context (PMK R0, PMK R1) is established across all APs/AP MLDs of an FT Mobility domain.
To associate with an SMD, the non-AP MLD includes an SMD element in the Association Request. This signals that the non-AP MLD is associating with an SMD.
When roaming to another AP MLD within same SMD, the non-AP MLD includes SMD element in the roaming add link request. This signals non-AP MLD is moving links within its current SMD.
The act of association to an SMD through an AP MLD 1 provides (non-AP MLD to AP MLD 1) mapping to the DS. When the non-AP MLD roams to another AP MLD 2 (using roaming add link) within the same SMD, that provides (non-AP MLD to AP MLD 2) mapping to the DS.
Successful completion of roaming add link operation with a target AP MLD opens the 802.1X port (on the target AP MLD) for that non-AP MLD to access the DS.

## Slide 5: FT and Seamless Mobility Domains
An ESS can be configured with multiple SMDs. All AP MLDs of an ESS in large deployments may not provide seamless roaming (e.g. ESS covering multiple buildings, each building is an SMD)
FT should be used for roaming across SMDs of an ESS.
An ESS can be configured to have one or more FT Mobility Domains (FT MD). Each FT MD can be configured to have one or more SMDs.
  Note: FT MD and SMD can have 1:1 mapping, and in that case FT roaming is not used by UHR STAs.
  Note: All AP MLDs of an SMD are in the same FT MD. If AP MLDs can support seamless roaming, then these AP MLDs can also support FT.

## Slide 6: Single Secure Association with an SMD (1)
For seamless roaming, it is important that the non-AP MLD maintains its association and security context as it roams – to avoid reauth, reassociation and rekeying delays.
  Note: in 802.11REVme, roaming term is used in the context of ‘roaming consortium’. To avoid overloading roaming term, we could use ‘Seamless BSS Transition’ (SBT), along the same line as 11r Fast BSS Transition.
SMD defines a single security domain where all AP MLDs are trusted (and in same ESS). A non-AP MLD establishes a single secure association with this trusted security domain. All AP MLDs of an SMD can be configured to have the same set of cipher suites.
Since all AP MLDs in an SMD are trusted, we propose that same set of pairwise keys (PMK and PTK) can be shared across these AP MLDs over secure channels.
  Note: enterprise deployments today support OKC (Opportunistic Key Caching) and standard defined PMKSA caching which enables same PMK to be used across multiple APs.
  Sharing same PTK avoids delay associated with PTK regeneration and MPDUs decryption/encryption (in case of data transfer across AP MLDs) during roaming
PMK and PTK pairwise keys are established between an (SMD, non-AP MLD) pair at the time of initial association with the SMD
  PTK generation gets tied to the SMD, by setting Authenticator Address (AA) to SMD MAC Address.

## Slide 7: Single Secure Association with an SMD (2)
Sharing of pairwise keys (PMT, PTK) between AP MLDs must be done over a secure channel. Exchange of keys between trusted entities is already supported for FT. The exact protocol for keys transfer is outside the scope (similar approach as used for FT).
RSNA defines rekeying mechanism by which PTK gets renewed. PTK will get renewed independent of whether it is used at one AP MLD or across multiple AP MLDs of an SMD.
  A typical setting of PTK rekeying interval could be 3600 sec. In the proposal, the PTK will be used for the same X time (say 60 mins) whether on one AP MLD or across more than one AP MLD when client roams.
  Roaming could also be used as a trigger for PTK rekeying, after any buffered DL PPDUs have been delivered/fetched. This reduces the time duration for which same PTK key is used on another AP MLD.

## Slide 8: SMD Entity and its Functions (1)
SMD Entity is a logical entity which provides functions of initial association to SMD, add/delete links with the SMD, management of SMD security context (PMKSA, PTKSA), SMD roaming related context transfer and any other SMD related functions.
These SMD functions reside in the MLD Upper MAC.
SMD related context for a non-AP MLD moves from the serving AP MLD to the target AP MLD when that non-AP MLD roams.

## Slide 9: SMD Entity and its Functions (2)
  SMD defines a seamless mobility domain, and not an MLD as per 11be MLD definition.
  SMD does not define another level of MLD which could have 100’s of affiliated AP MLDs (e.g. for enterprise deployment) and operate using one or more of those AP MLDs.
    In a non-roaming state, a non-AP MLD has setup links with only a single AP MLD within the SMD.
  SMD does not present a single MAC SAP (across all AP MLDs) to the LLC. SMD MAC Address is not on the DS data path. Providing same SMD MAC Address for different physical AP MLDs to the DS does now align with current backhaul architecture. In mapping to the DS, AP MLD MAC address is provided (not SMD MAC Address).
  SMD entity can be involved in transferring of buffered DL data (if supported) to the target AP MLD during roaming.
1
2
3

## Slide 10: Discovery of an SMD (1)
An SMD element (SMDE) is included in Beacon and Probe Response frames - similar to FT Mobility Domain IE (MDE).
SMD IE includes SMD MAC Address, possibly a shorter SMD identifier (SMD ID) and SMD capabilities and policy (e.g. support for resource reservation, roaming preparation, roaming data transfer, etc).
SMD IE does not include list of all AP MLDs of the SMD. Clients only need to know neighboring AP MLDs in the SMD, and not all 100’s/1000’s of AP MLDs of an SMD.
Clients learn about SMD of neighboring AP MLDs through discovery process (e.g. from Beacon, Probe Responses, RNR, Neighbor Report, BTM).

## Slide 11: Discovery of an SMD (2)
RNR can be enhanced to indicate if a reported AP is part of the same SMD as the reporting AP. One of the reserved bits in MLD Parameters or BSS Parameters can indicate ‘Same SMD’ field.
When a reported AP in RNR is part of a different SMD, a new TBTT Information field can signal SMD Parameters providing SMD identifier. A short SMD identifier can be used.
A non-AP MLD can determine the SMD of reported APs from RNR based on the ‘Same SMD’ bit and SMD Parameters.
Neighbor Report element (in the Neighbor Report Response and the BTM Request) can include the SMD IE as a subelement, indicating the SMD of the reported AP.

## Slide 12: Two Phase Roaming Approach (1)
Roaming Preparation Phase
  When context is transferred from serving to target AP MLD, the UL Tx would need to be paused, else DS path will switch back to serving AP MLD. Hence, it is desirable to shorten the context transfer time.
  Roaming preparation phase is proposed to achieve that
    Prepares one or more neighboring candidate AP MLDs for roaming, by transferring near static context in advance (SCS, TWT, BA agreements, STA capabilities etc). Installs keys (PMK, PTK) if not already installed
    Enables candidate target AP MLDs to better plan resources for receiving the non-AP MLD in future.
  It is preferred for a non-AP MLD to do roaming preparation as it will lead to more reliable and deterministic roaming performance
    However, it may not be possible to do roaming prep in all cases for a non-AP MLD (e.g. sudden RSSI change), and when not performed the roaming experience may be degraded
  Roaming prep can also be initiated by serving AP MLD (e.g. based on load, roaming predictions etc.)
    Once completed, the serving AP MLD notifies the client about the list of candidate target AP MLDs.
    Serving AP MLD may perform prep with all/subset of neighboring AP MLDs without explicitly notifying the client. This will be effective only if done with all neighboring AP MLDs. Option a is preferred.

## Slide 13: Two Phase Roaming Approach (2)
Roaming Execution Phase
  Here the dynamic context is transferred including data exchange context (SN, PN, BA scoreboarding).
  If no roaming preparation done before, then near static context (e.g. agreements, capabilities etc) is also transferred, and keys (PMK, PTK) fetched if not installed before  adds to roaming delay.
  Resource reservation:
    Non-AP MLD may indicate all or some of the resources (SCS+QC, TWT) which are desired to be reserved on the target AP MLD in roaming request. Client RSSI with Target APs should be reported for the Target AP MLD to determine how much resources to reserve.
    Serving AP MLD asks for resource reservation from the target AP MLD. Set of resources which are successfully reserved indicated to the non-AP MLD.
    Client may indicate roaming is acceptable even if some or all resources can’t be reserved
  DL data delivery time:
    Source AP MLD indicates the time for which buffered DL data will be attempted for delivery or will be available for fetching. This can be set conservatively.
    Only buffered DL MPDUs delivery/fetching allowed with serving AP MLD during this time. No UL Tx.
    Links with the serving AP MLD are auto deleted after this time, or client can send delete link earlier.

## Slide 14: Seamless Roaming E2E Call Flow (with prep phase)
Roaming prep time: indicates time during which non-AP MLD must initiate roaming execution.
Dual DL – for a period after response is received confirming context transfer, STA has DL active with both serving and target AP MLDs. DL buffered MPDUs can be delivered/fetched from the source AP MLD.
Optionally some (selective) data transfer can happen if supported by AP MLDs
Link Reconfiguration Notify frame and Link Reconfiguration Request/Response frames can be leveraged/extended for seamless roaming procedure

## Slide 15: Seamless Roaming E2E Call Flow (w/o prep phase)
In this case the roaming execution time is much longer, which in turn means UL transmission is paused for longer. This may lead to degraded roaming experience, compared to when roaming preparation was done.

## Slide 16: Conclusion
In this presentation we covered further details on seamless roaming within a seamless mobility domain (SMD), in following areas:
  Association to an SMD
  FT and Seamless Mobility Domains
  Single secure association with an SMD
  SMD entity and its functions
  Discovery of an SMD
  Two phase roaming approach
    Roaming reparation phase and roaming execution phase
  Seamless roaming e2e call flows
Existing ML Reconfiguration management signaling can be leveraged/extended for the seamless roaming procedure

## Slide 17: SP1
Do you agree to define a mechanism in 11bn that enables a non-AP MLD to establish a single association with a logical entity covering a set of multiple AP MLDs and the non-AP MLD remains associated with the logical entity as it roams from one AP MLD to another AP MLD within the set of multiple AP MLDs?

## Slide 18: References
[1] 11-23-2157 “Seamless roaming within a mobility domain”
[2] 11-22/1910 “Seamless Roaming for UHR”
[3] 11-23/0170 “Smooth Roaming”
[4] 11-23/1131 “Thoughts on seamless roaming”
[5] 11-23-1416 “Seamless roaming follow up”
[6] 11-23-1996 “Improve roaming between MLDs”
[7] 11-23-0632 “smooth-roaming-follow-up”